## Slide 1: EDCA Enhancement with AP support -- follow up
Date: 2025-6-7
Authors:

## Slide 2: Introduction
In [1], we proposed a solution to consider AP’s intervention for P-EDCA recovery.

## Slide 3: Recap: AP-assisted recovery solution
CTS
  AP provides support among non-AP STAs.
  LL non-AP STAs send DS and start contending the channel, after a longer channel acquisition time, e.g., “channel acquisition time limit”, AP may provide control and support.
  The AP does not necessarily have to explicitly detect or count individual failed RTS/CTS transmissions. Its primary role is to ensure that channel acquisition time remains within acceptable limits.
  AP can send some trigger frames such as BSRP or LLT schedule can restore order and fairness.
Hip EDCA contention period
Previous TXOP
(could be a TXOP won by one of the LL STA via Hip EDCA)
AP may manage the LLT and assign time/frequency resources to LL STAs
STA4
STA2
STA1
Frame exchanges in the TXOP
SIFS
DIFS
PIFS
AP
Delay bound for STA1
Delay bound for STA2
DS
STA3
DS
DS
RTS
RTS
RTS
DS
BO
BO
BO
SIFS
DS
RTS
BO
RTS
RTS
P-EDCA contention duration limit
DS
DS
DS
RTS

## Slide 4: AP intervention in PEDCA
  AP’s intervention use cases:
  STA may repeatedly fail P-EDCA contention, e.g., RTS collisions, and repeated DS-CTS + RTS transmissions, and thus a long channel acquisition time, i.e., airtime from unproductive DS/RTS cycles is detected.
  A congested network with multiple prioritized access non-AP STAs (LL STAs) need to be transmitted using PEDCA. Due to the NAV setting by DS-CTS attempts, other STAs may be blocked.
  AP can better utilize and manage the network during PEDCA operation, and balance the fairness and impact among LL STAs and other STAs.

## Slide 5: What metrics may trigger AP’s intervention?
  When PSRC[AC_VO] is allowed to be set greater than default value (i.e., PEDCAPSRCThreshold equals to 1 [2]), for example, AP advertises the threshold of PSRC is 4. In such case, when PSRC[AC_VO] is greater than 3 or 4, AP is allowed to intervene/step in since STA may failing too often.
  AP may intervene by using PEDCA with AIFSN equals to a TBD value, which may be shorter than DSAIFS.
DS
P-EDCA
TXOP1
RTS
DS
DS
DS
DS
RTS
RTS
P-EDCA
TXOP2
RTS
DS
RTS
DS
DS
DS
RTS
RTS
RTS
RTS
DS
BO
BO
DS
RTS
DS
RTS
DS
RTS
DS
RTS
P-EDCA
TXOPN
…
…
AP may step in

## Slide 6: Stroll Poll 1
  Do you support allowing an AP to end the P-EDCA contention attempts from non-AP STAs if the number of consecutive failed P-EDCA contention attempts is greater than TBD value?

## Slide 7: References
[1] 11-25-0380-00-00bn-edca-enhancement-with-ap-support
[2]11-23-1065-00-0uhr-low-latency-channel-access
[3] 11-25-0627-14-00bn-cc50-cr-for-p-edca