## Slide 1: HP EDCA Follow Up – Condition to Use DS
Date: 2025-06-11
Authors:
Name | Affiliation | Address | Phone | Email
Yonggang Fang | MediaTek |  |  | yonggang.fang@mediatek.com
James Yee | MediaTek |  |  | 
Kaiying Lu | MediaTek |  |  | 
Li-Hsiang Sun | MediaTek |  |  | 
Frank Hsu | MediaTek |  |  | 
Gabor Bajko | MediaTek |  |  | 

## Slide 2: Introduction
This contribution discusses the condition of starting a Defer Signal for P-EDCA contention

## Slide 3: Recap of EDCA Enhancement
In SFD [1]
  TGbn improves EDCA to reduce tail access delay of Low Latency (LL) traffic in multi-BSS dense scenarios in presence of best effort traffic
    The solution to improve EDCA is distributed
    The impact on legacy device has to be balanced
    Low Latency traffic is treated as AC_VO traffic. Other cases are TBD
In 802.11bn D0.3 [2]
  A P-EDCA STA may start a P-EDCA contention if all of the following conditions are satisfied:
    ….
    QSRC[AC_VO] is equal or greater than dot11PEDCARetryThreshold
  Issues
  This retry counter based condition of starting P-EDCA would not resolve latency tail efficiently.
  Not handle the case that multiple STAs have needs of P-EDCA for LL transmissions
  It is necessary to revisit the condition for starting P-EDCA contention.
3

## Slide 4: Issues of Condition For Starting DS
Latency Tails
  “retry counter” based condition relies on legacy channel access result:
    It only considers the condition that the STA failed channel access but does not consider whether the traffic has the LL delay bound requirement or not.
    For the case of a few LL STAs among large number of legacy STAs, the chance for the LL STA to acquire TXOP with legacy EDCA is very low. Therefore, it is possible that the LL STA would not have a chance to get TXOP before the delay bound expired.
    It would not be helpful to resolve the latency tail for the case that the STA already suffered long access latency tail of LL traffic before it can use P-EDCA.
  Access for multiple P-EDCA STAs
  In the dense deployment, multiple STAs would reply on P-EDCA to reduce LL tail. Without prioritizing the needs from multiple LL STAs in the resource limited environment, it is possible that a LL STA may acquire TXOP using P-EDCA after its delay bound requirements.

## Slide 5: Proposal
Defer Access Time Based Condition For Starting DS
  Proposal
    Use the defer access time due as an alternative condition to enable STA to transmit Defer Signal to start the protected P-EDCA contention.
      The defer access time due can be estimated based on the delay bound and the packet arrival time, e.g., the packet arrival time + delay bound – 2 * TXOP[AC_VO] limit
  Benefits
    Link to the QoS Characteristic parameters, including Delay Bound directly via SCSID, see [3][4]
    Reduce the latency tail via P-EDCA only when it is necessary, i.e., reaching to the defer access time due.
    Prioritize the needs for the LL transmissions among LL STAs. A LL STA starting DS only at the time approaching to the defer access time due.
    Fair to non-P-EDCA STAs. During the period between the time of LL data arrival and its the defer access time due, the STA still uses legacy EDCA for channel access.

## Slide 6: References
11-24-0209-14-00bn-specification-framework-for-tgbn
Draft 802.11bn D0.3
802.11me D7.0
802.11be D7.0
6