## Slide 1: Incompatibility issue between NPCA and MAPC
Date: 2025-03-12
Authors:
Name | Affiliation | Address | Phone | Email
Junbin Chen | TP-Link Systems Inc. |  |  | chenjunbin@tp-link.com.hk
Yunpeng Yang |  |  |  | yangyunpeng@tp-link.com.hk
Renfang Zhou |  |  |  | zhourenfang@tp-link.com.hk
Yaoshen Cui |  |  |  | cuiyaoshen@tp-link.com.hk
Haozheng Li |  |  |  | lihaozheng@tp-link.com.hk
Qingwei Fu |  |  |  | fuqingwei@tp-link.com.hk
Shuyu Shi |  |  |  | shishuyu@tp-link.com.hk
Yu Zhu |  |  |  | zhuyu@tp-link.com.hk

## Slide 2: Recap: MAP framework
In 11bn D0.1 [1-2] we have agreed that the MAP shall be defined in a unified framework:
[M50] 11bn defines a common framework of a Multi-AP Coordination for various coordination schemes.
  Note - Coordination schemes such as (but not limited to): Co-SR (TXOP-based with power control), Co-BF, Co-TDMA, Co-RTWT, etc.
[M51] 11bn defines a common framework of a Multi-AP Coordination that can enable the following procedures:
  Multi-AP Coordination Discovery procedure
  Multi-AP Coordination agreement negotiation procedure
  Note: Details of the procedures and whether the above procedures are mandatory/optional - TBD

## Slide 3: Recap: MAP framework
AP1
AP2
Negotiation phase
e.g., C-SR & C-BF
Transmission phase
e.g., C-SR
Transmission phase
e.g., C-BF
TXOP1
TXOP2 of AP1
TXOP4 of AP2
ICF
ICR
Beacon
Beacon
ICF
ICR
Negotiation phase
e.g., C-SR & C-BF
& C-TDMA
Transmission phase
e.g., C-TDMA
TXOP6 of AP1
ICF
ICR
MAP Discovery
TXOP5
During the negotiation phase, the APs may set up more than one MAPC agreements [3-4]. The agreements can exist until they are updated or deleted in another negotiation phase.
  e.g., both C-BF and C-SR are negotiated for period 1, and C-TDMA is further negotiated for period 2 as shown below.
Once the agreement has been set up, the AP who wins TXOP shall use an ICF to poll the coordinated AP, and notify the exact MAP coordination feature to be used in this TXOP [3].
If the polled AP response with an ICR, then the APs can perform the procedures defined for the specific MAP coordination feature [3-5].
MAP negotiation for period 1
MAP negotiation for period 2
TXOP of OBSS AP3
TXOP3 of AP3

## Slide 4: Motivation
As stated before, the MAP coordination is initiated by an ICF/ICR for each TXOP.
The shared AP responding ICR may choose to stay on PCH for a potential MAPC transmission later.
The non-AP NPCA STAs associated with shared AP will classify the ICF and the PPDUs from sharing BSS as an inter-BSS PPDU, and switch to the NPCA primary channel.
Thus, the MAPC operation would lead to the different view between NPCA APs and non-AP NPCA STAs.
AP1
AP2
TXOP of AP1
ICF to AP2
ICR to AP1
STA1
ICF to AP2
STA2
ICF to AP2
ICF to AP2
Data transmission
MAPC transmission
C-SR/C-BF/C-TDMA
failed
MAPC transmission with AP2
MAPC transmission
C-SR/C-BF/C-TDMA
Receiving an inter-BSS PPDU, STA 2 switches to NPCH
Responding an ICR, AP2 stay on the PCH
ICR to AP1
ICR to AP1
The data transmission failed due to different view of primary channel
Sharing BSS
Shared BSS

## Slide 5: The shortcoming for beacon-based NPCA disablement
Generally a beacon interval is around 100ms, which contains multiple TXOPs.
There might be some TXOPs obtained by AP1 and/or AP2, which is available for MAPC operation, and some other TXOPs obtained by other OBSS STAs, which is unavailable for MAPC but suitable for NPCA operation.
An AP transmitting a Beacon frame can not determine whether it would be always available for NPCA in the next beacon interval.
AP1
AP2
Negotiation phase
e.g., C-SR & C-BF
Transmission phase
e.g., C-SR
Transmission phase
e.g., C-BF
TXOP1
TXOP2 of AP1
TXOP4 of AP2
ICF
ICR
Beacon
Beacon
ICF
ICR
TXOP of OBSS AP3;
NPCA available for both AP1 and AP2
TXOP3 of AP3
Beacon
Beacon
TXOP5 of ???
NPCA should be available or not?

## Slide 6: Proposal: implicit NPCA disable announcement
The NPCA AP shall announce an NPCA-delayed BSS list to its associated NPCA STAs in advance.
  The list indicates the BSSs, APs in which has an established MAPC agreement with the NPCA AP.
  The announcement includes at least the BSS color and/or BSSID of the coordinated APs.
The non-AP NPCA STA, receiving an inter-BSS PPDU that belongs to a BSS which is announced in the list, wait for a TBD-timeout before NPCA switch.
  The PPDU classification can be based on the BSS color and/or the BSSID of the received PPDU.
If receiving an ICR sent from the associated AP indicating the intention to participate in the MAP coordination in this TXOP, the non-AP NPCA STA shall not switch to the NPCA primary channel.
  Otherwise, the non-AP NPCA STA may switch to NPCA primary channel.
  If no ICR is received for the TBD-timeout, the non-AP NPCA STA may switch to NPCA primary channel.

## Slide 7: Proposal: implicit NPCA disable announcement
AP3
STA3
Beacon
Beacon
Beacon
AP1
AP2
TXOP of AP1
ICF to AP2
ICR to AP1
STA1
ICF to AP2
STA2
ICF to AP2
ICF to AP2
Data transmission
MAPC transmission succeed
MAPC transmission
MAPC trigger
CTS
Hearing ICF from AP1 and ICR from AP2, NPCA is disabled implicitly
ICR to AP1
ICR to AP1
MAPC trigger
CTS
Negotiation phase
Negotiation phase
Beacon
ICR to AP1
Announce the coordinated AP lists to associated non-AP STAs
Respond with ICR indicating the MAP participation intention
The MAPC transmission succeed since the AP2 and STA2 parks on the same primary channel
TXOP of AP3
TXOP of OBSS AP3
NPCA transmission
NPCA transmission
MAPC
AP3 is not a coordinated AP with AP2, NPCA operation is enabled for STA2 again
MAPC transmission

## Slide 8: The coordinated AP list announcement - option 1
Include a new MAP coordination list element in Beacon/probe resp/association resp frames, announcing the MAP coordination info (both BSS info and negotiated MAP features).
 | Element ID | Length | Extension element ID | Num of coordinated APs | Coordinated AP entry 1 | Coordinated AP entry 2 | … | Coordinated AP entry x
Octets : | 1 | 1 | 1 | TBD | 8 | 8 | … | 8
 | BSS info | MAP feature bitmap
Octets : | 7 | 1
 | C-TDMA | C-SR | C-BF | C-RTWT | reserved
Bits : | 1 | 1 | 1 | 1 | 4
 | BSSID | BSS color | reserved
Bits : | 48 | 6 | 2

## Slide 9: The coordinated AP list announcement - option 2
Include a new MAP coordination list element in Beacon/probe resp/association resp frames, announcing the MAP info without explicit negotiated MAP features.
 | Element ID | Length | Extension element ID | Num of coordinated APs | Coordinated AP entry 1 | Coordinated AP entry 2 | … | Coordinated AP entry x
Octets : | 1 | 1 | 1 | TBD | 7 | 7 | … | 7
 | BSSID | BSS color | reserved
Bits : | 48 | 6 | 2
 | NPCA Primary Channel | NPCA Minimum Duration Threshold | NPCA Switching Delay | NPCA Switch Back Delay | NPCA-delayed BSS list bitmap
Bits: | 8 | TBD | 6 | 6 | x
Include a new NPCA-delayed BSS list bitmap subfield in NPCA OP IE, indicating the BSS that shall be treated as NPCA delayed BSS.

## Slide 10: Summary
The MAP coordination is incompatible with NPCA to some degree.
  The ICF for MAP coordination may lead to unexpected NPCA switch of non-AP STAs.
To address such incompatibility, we propose the concept of NPCA-delayed BSS.
  After MAP negotiation, the AP shall announce the peer BSS as NPCA-delayed BSS.
  Receiving a inter-BSS PPDU which belongs to NPCA-delayed BSS (e.g., an ICF for MAPC query phase), the non-AP STA waits until a TBD-timeout, and then decide whether to perform the NPCA switch or not.

## Slide 11: References
[1] 802.11bn-D0.1
[2] 24/0171 TGbn Motions List - Part 1
[3] 24/1514 Multi-AP framework for C-SR, Geonhwan Kim (LG Electronics)
[4] 23/1871 M-AP Coordinated Transmission framework, Arik Klein (Huawei)
[5] 24/1220 A Framework for Coordinated Access Points, Giovanni Chisci (Qualcomm)