## Slide 1: Spatial Reuse triggered NPCA
Date: 2025-03-25
Authors:

## Slide 2: Abstract
This presentation proposes a new mechanism to mitigate the OBSS hidden node problem for NPCA

## Slide 3: Introduction
Non-Primary Channel Access (NPCA) feature in UHR enables an AP and a non-AP STA to communicate on a nonprimary channel when the primary channel is busy due to OBSS traffic [1] – [5]
OBSS hidden node is a critical problem for NPCA, which may degrade the overall performance
  [2] proposed that each AP/STA build a list of OBSS APs and AP announces to its associated STAs
  [4], [5] proposed to define a mode of operation in NPCA where the NPCA non-AP does not use untriggered UL transmissions on the NPCA primary channel
[3] discusses the coexistence issue of Spatial Reuse (SR) and NPCA and proposes to enable SR or NPCA at one time period
In this contribution, we propose to use SR to mitigate the OBSS hidden node problem for NPCA

## Slide 4: Recap: NPCA Goal [1]
If the primary channel is busy and the secondary channel(s) are available, an AP/STA transmits on the available secondary channel(s)
Busy
Primary 20MHz
Secondary 20MHz
Secondary 40MHz
time
20MHz PPDU
(interference, OBSS)
80MHz PPDU
Busy
Busy
frequency
40MHz PPDU
(interference, OBSS)
(STA to AP or AP to STA)
STA can transmit a packet on the secondary channels while the primary channel is busy
60MHz PPDU
40MHz PPDU

## Slide 5: Recap: OBSS hidden node problem for NPCA
When one peer observes OBSS but other does not
  Case 1: AP observes OBSS but non-AP STA doesn’t
  Case 2: non-AP STA observes OBSS but AP doesn’t
AP1
non-AP STA2
AP2
BSS2=OBSS
BSS1
Case 1
Case 2
AP1
AP2
BSS2=OBSS
BSS1
non-AP STA1
non-AP STA3
non-AP STA2
non-AP STA1
non-AP STA3

## Slide 6: Recap: Spatial Reuse
Spatial reuse allows STAs to transmit frames under the OBSS traffic in the same channel with some conditions and transmission power constraints
  OBSS Packet Detection (PD)-based spatial reuse
    If the RSSI of the detected OBSS frame is lower than the specific threshold (OBSS_PDlevel), STA can continue the backoff procedure
  Parameterized Spatial Reuse (PSR)-based spatial reuse
    STA can continue the backoff procedure during the OBSS TXOP if it satisfies the condition indicated by the PSRR PPDU (i.e. OBSS Trigger frame) or the TB PPDU that follows the PSRR PPDU

## Slide 7: Proposal: Spatial Reuse triggered NPCA
STA (including both non-AP STA and AP) of a BSS detects an OBSS TXOP on its primary channel.
  The OBSS transmission meets the criteria for Spatial Reuse operations.
The STA transmits a NPCA switching frame (i.e. Channel Switch-ICF; CS-ICF) to other STAs of the BSS, on its primary channel (PCH) using the spatial reuse operation
  The frame indicates OBSS interference to those other STAs that are too far to detect it
The CS-ICF triggers a switching of channel access to NPCA at these other STAs.
Next, the STAs perform NPCA operations on an NPCA Primary Channel (NPCA PCH), even if some of them have not directly detected the OBSS interference.

## Slide 8: Spatial Reuse triggered NPCA (Case 1)
When AP1 detects an OBSS TXOP which allows SR operation, AP1 sends an CS-ICF to trigger NPCA
OBSS
AP1
non-AP STA1/
non-AP STA2
OBSS TXOP
NPCA
NPCA
PCH
PCH
PCH
NPCA PCH
CS- ICF
NPCA PCH
AP1
non-AP STA1
AP2
BSS2=OBSS
BSS1
non-AP STA2
non-AP STA3

## Slide 9: Spatial Reuse triggered NPCA (Case 2)
When STA1 detects an OBSS TXOP which allows SR operation, STA1 sends an CS-ICF to trigger NPCA
OBSS
non-AP STA1
AP1/
non-AP STA2
OBSS TXOP
NPCA
NPCA
PCH
PCH
PCH
NPCA PCH
CS-ICF
NPCA PCH
AP1
non- AP STA1
AP2
BSS2=OBSS
BSS1
non- AP STA2
non- AP STA3

## Slide 10: Consideration on CS-ICF
CS-ICF shall contain information that indicates the duration remained for the NPCA operation
CS-ICF may contain intermediate FCS
CS-ICF should be sent in a low data rate to be decodable by the receiver STAs
CS-ICF may be sent in a non-HT duplicate PPDU which covers the NPCA Primary Channel to initiate TXOP of the NPCA Primary Channel
Further details are TBD

## Slide 11: Summary
This contribution proposes a new mechanism to mitigate the OBSS hidden node problem for NPCA by sending CS-ICF under the spatial reuse operation

## Slide 12: Straw Poll
Do you support the following in the NPCA operation?
  If an NPCA STA detects OBSS traffic which meets one of the condition of Spatial Reuse operation (OBSS PD-based SR and/or PSR-based SR), the NPCA STA transmits an CS-ICF which triggers NPCA on the receiver NPCA STA
  Details on CS-ICF are TBD

## Slide 13: References
[1] 11-23/961 UHR Secondary Channel Access
[2] 11-23/2005r1 Non-Primary Channel Access (NPCA)
[3] 11-24/0802r0 Discussion on NPCA and SR
[4] 11-24/1093r3 Special scenarios in Non-Primary Channel Access
[5] 11-24/1218r1 NPCA - next level discussions