## Slide 1: Co-SR Power Control
Date: 2025-03-26
Authors:

## Slide 2: Introduction
TGbn defines multi-AP Coordinated Spatial Reuse (Co-SR) at TXOP-level with power control [1].
There have been discussions on power control methods, but no consensus have been reached yet on this topic.
  In [2], The Trigger frame that initiates the Co-SR transmission indicates the TX power limit of the shared AP.
  In [3] and [4], ICF and ICR are porposed for exchanging control information between APs to support power control.
In this contribution, we introduce a power control solution for Co-SR with some shared information, and using ICF/ICR exchange to facilitate power control.

## Slide 3: Recap: Power Limitation in PSR
802.11ax introduces the Parametrized Spatial Reuse (PSR) mechanism, which allows an HE STA to identify a PSR opportunity for the duration of an ongoing TB PPDU.
  An AP that aims to use PSR determines an Acceptable Receive Interference Level (ARIL) in dBm
    : expected receive signal power of the ensuing HE TB PPDUs
    : minimum SNR value that yields ≤ 10% PER
    : safety margin value
  The AP determines the parameter, and finds as the highest value less than or equal to in Table 27-24.
  If an HE STA receives a inter-BSS TF that allows PSR and its expected TX power does not exceed the power limit specified in the TF, it will identify a PSR opportunity.
    : number of non-punctured 20 MHz subchannels of the PSRT PPDU
    : normalized received signal power in units of dBm/20MH

## Slide 4: Power Limitation in Co-SR
Unlike PSR, Co-SR involves simultaneous DL transmissions. When AP1 utilizes Co-SR for delivering DL PPDU to STA1, it shall determine the maximum TX power limit of AP2:
  It can be derived from a), b) and c) that :
The same way is used for AP2 to determine the maximum TX power limit of AP1.
Based on the above equation, we can draw the following conclusion:
  Except for the AP TX power, the other items on the right side of the equation are semi-static parameters related to the STA, and the AP can obtain these parameters through the measurement procedure.
  The maximum TX power limit of OBSS AP solely depends on the AP’s TX power.

## Slide 5: Power Control for Co-SR (1/4)
In this contribution, we assume that the APs have completed both the MAP negotiation and the Co-SR measurement procedure, and have already obtained measurement results related to their STAs (i.e., Pathloss, minimum SNR and other TBD parameters).
Information required for power control at an AP:
  Expected TX power: The expected TX power to send DL PPDU during Co-SR transmission.
  Maximum TX power limit of OBSS AP: Determined by the expected TX power of the AP and the measurement results.
  Power headroom (or Maximum TX power): The gap between the expected and the maximum TX power of the AP in units of dB.
  Minimum TX power: The minimum TX power by the AP, ensuring that its STA is available to decode the PPDU without interference from OBSS AP.

## Slide 6: Power Control for Co-SR (2/4)
Power negotiation procedure between sharing AP and shared AP are as follows:
  Step1: Sharing AP and shared AP calculate their own power control information based on measurement.
  Step2: Shared AP shares its power control information to sharing AP.
  Step3: With knowledge of global power control information, sharing AP can decide whether to do Co-SR or not and perform STA selection.
  Step4: The sharing AP informs the shared AP if there is a change in the TX power parameters.

## Slide 7: Power Control for Co-SR (3/4)
AP2’s power cannot be reduced to 4dBm (5dBm), So AP1 increase its power by 6dB instead
Example: An AP with knowledge of global power control information can adjust parameter values to meet the power requirements of both sharing AP and shared AP.
 | AP1-> STA1
Expected TX power | 5dBm
Maximum TX power limit of AP2 | 4dBm (10dBm,10dBm)
Power headroom | 10dB
Minimum TX Power | 3dBm
 | AP1-> STA1
Expected TX power | 5dBm
Maximum TX power limit of AP2 | 
Power headroom | 10dB
Minimum TX Power | 3dBm
AP1-> STA1
11dBm
10dBm (10dBm, 10dBm)
4dB
3dBm
AP1-> STA1
11dBm
4dB
3dBm
Expected TX power of AP1
Adjusted TX power of AP1
 | AP2-> STA2
Expected TX power | 10dBm
Maximum TX power limit of AP1 | 12dBm (5dBm)
Power headroom | 5dB
Minimum TX Power | 5dBm
 | AP2-> STA2
Expected TX power | 10dBm
Maximum TX power limit of AP1 | 
Power headroom | 5dB
Minimum TX Power | 5dBm
 | AP2-> STA3
Expected TX power | 10dBm
Maximum TX power limit of AP1 | 10dBm (5dBm)
Power headroom | 5dB
Minimum TX Power | 5dBm
 | AP2-> STA3
Expected TX power | 10dBm
Maximum TX power limit of AP1 | 
Power headroom | 5dB
Minimum TX Power | 5dBm
AP2-> STA2
10dBm
12dBm (11dBm)
5dB
5dBm
AP2-> STA2
10dBm
5dB
5dBm
AP2-> STA3
10dBm
10dBm (11dBm)
5dB
5dBm
AP2-> STA3
10dBm
5dB
5dBm
AP2 discards STA3 because it cannot meet the requirements no matter how the power is adjusted.
Slide 7

## Slide 8: Power Control for Co-SR (4/4)
The benefits of AP gathering global power control information before performing Co-SR:
  Using global information for power control overcomes the limitation of an AP recommending power for an OBSS AP based solely on its own information. For example:
    While recommending the maximum TX power limit for the OBSS AP, the AP is unaware of its impact on the OBSS STA, which can potentially lead to transmission failure.
    In some cases, the APs cannot do Co-SR transmission due to one AP’s power cannot be reduced below its minimum TX power. Since no shared information like power headroom is provided, Co-SR cannot be achieved in an alternative way: increasing the other AP’s TX power.
  Therefore, it is important to negotiate the power in advance to avoid sudden transmission failures before performing Co-SR transmission.
  AP can also perform STA selection from more than one candidate STAs based on this information.

## Slide 9: Co-SR Power Control Negotiation
The power control negotiation is done by performing ICF/ICR exchange during the polling phase Before Co-SR transmission.
  Whether to allow more than one candidate shared AP is TBD.
Shared power control information
power limit of AP2
Sharing AP gather global power control information
  Pre-transmission: AP1 selects one or more candidate STAs.
  ICR: If AP2 is willing to participate, the ICR includes the shared power control information of its candidate STAs.
  Co-SR trigger: Based on known information, If AP1 decide they cannot do Co-SR, it will not send the Co-SR trigger. If AP1 decides to initiate Co-SR, it first perform STA selection, and:
    If AP1 the power of either AP needs to be changed, the Co-SR trigger includes the adjusted TX power limit of AP2 .
    Or it includes the original TX power limit of AP2.

## Slide 10: Summary
This contribution introduces a power control solution based on shared power control information for Co-SR.
  Power control signaling based on ICF/ICR exchange is proposed.

## Slide 11: Straw Poll
SP: Do you support to include the following text to 11bn SFD?
  In UHR Co-SR, Sharing AP needs to obtain global power control information before Co-SR transmissions. The following shared power control information shall be carried in the ICR during the polling phase before Co-SR transmission:
    Expected TX power
    Maximum TX power limit of sharing AP
    Power headroom (or Maximum TX power)
    Minimum TX power
  The adjusted TX power limit for shared AP shall be carried in the trigger frame that initiates Co-SR.
Huixuan Zhou, OPPO

## Slide 12: References
[1] 11-24-0209-12-00bn-specification-framework-for-tgbn
[2] 11-25-0254-00-00bn-co-sr-power-control-considerations
[3] 11-24-1514-01-00bn-multi-ap-framework-for-c-sr
[4] 11-25-0343-00-00bn-consideration-on-multi-ap-framework-for-co-sr