## Slide 1: Discussion on NPCA and DPS
Date: 2025-03-31
Authors:
Name | Affiliations | Address | Phone | email
Chaoming Luo | OPPO |  |  | luochaoming@oppo.com
Liuming Lu | OPPO |  |  | 
Ning Gao | OPPO |  |  | 
Yapu Li | OPPO |  |  | 
Liangxiao Xin | OPPO |  |  | 

## Slide 2: Abstract
Proposes a mechanism to resolve CID 1774.
CID | Clause | Comment | Proposed Change
1774 | 37.10 | Could a DPS STA enable NPCA? Should a DPS STA switch to HC mode by default when switch to NPCA P-channel? | Define the behavior of a DPS STA switching to HC mode in NPCA procedure.

## Slide 3: Discussion
Could a DPS STA enable NPCA?
  Does not find a reason to disallow this.
Should a DPS STA switch to higher capability mode when switch to NPCA P-channel?
  [2] proposes when a DPS STA is in low capability mode and transitions from the BSS primary channel to the NPCA primary channel, it still is in low capability mode.
  However, why a NPCA STA switches to NPCA P-channel? A typical reason is it has much data to transmit or receive. And, a DPS STA switches from LC mode to HC mode due to the same reason.
  Both NPCA switch and DPS switch consume time. If the DPS STA switches to HC mode the same time when it switches to NPCA P-channel, the DPS assisting AP saves time in the NPCA TXOP.
  We should allow a DPS STA to make the decision based on its own traffic status and power status.
    E.g., with low latency traffic, switch to HC mode may be better
    E.g., with low power level, keep in LC mode may be better

## Slide 4: Proposal
A DPS STA is in low capability mode and transitions from the BSS primary channel to the NPCA primary channel, by default it still is in low capability mode.
The DPS STA may change the default behavior and switch to HC mode when it switches to the NPCA P-channel.
The DPS STA may announce in advance that it switches to HC mode when it switches to the NPCA P-channel.
  E.g., announcement in OMN or OMI, signaling TBD.

## Slide 5: Straw Poll
Do you support to add the following into the latest TGbn draft ?
  A DPS STA may announce in advance through TBD frame that it switches to HC mode when it switches to the NPCA primary channel.

## Slide 6: References
[1] Draft P802.11bn_D0.1
[2] 11-24-1886-00-00bn-npca-with-emlsr-dps-coex-mode