## Slide 1: Addressing Challenges for Coordinated TDMA (Co-TDMA) in Wi-Fi Networks
Name | Affiliations | Address | Phone | email
Hui Che | Ruijie Networks Co., Ltd |  |  | chehui@ruijie.com.cn
Fachang Guo | Ruijie Networks Co., Ltd |  |  | 
Shu Yang | Ruijie Networks Co., Ltd |  |  | 
Ke Zhong | Ruijie Networks Co., Ltd |  |  | 
Hang Yang | Ruijie Networks Co., Ltd |  |  | 
Date: 2025-03-31
Authors:

## Slide 2: Abstract
Background of Co-TDMA
Dynamic Time Allocation
  Sharing AP splits TXOP into time slots for other APs or P2P STAs (Motion 184).
  Supports on-demand allocation and return (Motion 160/277).
Coordination Signaling Framework
  Polling via BSRP Trigger (Motion 269) and response via M-BA (Motion 270).
  MU-RTS TXS Trigger for time allocation (Motion 159).
Challenges
Resource Allocation Fairness
  Sharing AP retains minimum TXOP for its traffic (Motion 329).
  Preventing excessive channel occupation by cooperative APs (Motion 274).
Increased Signaling Overhead
  Polling, allocation, and return phases consume resources.
  Short TXOP scenarios (e.g., AC_VO) may have lower gains than signaling costs.

## Slide 3: Problem Statement：Challenges in Dynamic Resource Allocation of Co-TDMA
Causal Path of Dynamic Resource Allocation
  TXOP Segmentation → Dynamic Time Allocation → Reduced Idle Time → Increased Utilization
TXOP Allocation Conflicts
  Sharing AP's own BSS traffic (e.g., video streaming, large file transfers) dominates TXOP.
  Insufficient remaining TXOP for polling (ICF/M-BA) and allocation (MU-RTS/CTS).
  Example overhead in 802.11ax:
  ICF (BSRP Frame): ~20μs
  SIFS: 16μs
  M-BA Response: ~30μs
  Total Overhead ≥ 66μs → If TXOP < 100μs, cooperation gain is negative.

## Slide 4: TXOP Allocation Issues Impact of Large TXOP Allocation for Sharing AP
Fairness Conflict
  Large TXOP (e.g., 10ms) may block other APs/STAs for extended periods, violating EDCA fairness.
Dynamic Environment Adaptation
  Fixed large TXOP wastes resources in low-load scenarios, reducing network efficiency.
Hidden Node Problem
  Longer TXOP increases the chance of hidden nodes initiating transmissions, causing collisions.
Inefficient Utilization
  If the cooperative AP has no traffic demand, the channel remains idle.

## Slide 5: Proposed Solution
Optimized TXOP Allocation Strategy
Adaptive TXOP Partitioning
  Introduce a flexible TXOP partitioning algorithm based on traffic demand.
Efficient Signaling Mechanism
  Optimize control frame structures to reduce overhead.
Dynamic Fairness Adjustment
  Adjust TXOP allocation dynamically to balance fairness and efficiency.
Collision Mitigation
  Implement NAV-based coordination to prevent hidden node issues.