## Slide 1: Discussion on Protection after Roaming Preparation
Name | Affiliations | Address | Phone | email
Hang Yang | Ruijie Networks Co., Ltd. |  |  | yanghang1@ruijie.com.cn
Ke Zhong | Ruijie Networks Co., Ltd. |  |  | zhongke@ruijie.com.cn
Hui Che | Ruijie Networks Co., Ltd. |  |  | chehui@ruijie.com.cn
Fachang Guo |  |  |  | 
Date: 2025-3-31
Authors:

## Slide 2: Introduction
TGbn has agreed on specify several parts of the Seamless Roaming procedure:
  [Motion #283]As part of seamless roaming procedure, a non-AP MLD can initiate a roaming preparation procedure with a target AP MLD by sending a TBD request frame to its current AP MLD.
  [Motion #335]After the roaming preparation request/response exchange, there is an indicated timeout
    If there is no successful transmission of the roaming execution request frame from the non-AP MLD within the indicated timeout, then the target AP MLD may delete all preparation information related to the non-AP MLD
    If the roaming preparation request for a target AP MLD is accepted in the roaming preparation response, and the non-AP MLD sends a following roaming execution request for the target AP MLD received within the indicated timeout, then the roaming execution request shall be accepted in the roaming execution response
In this contribution, we discuss some details about protection issue when target AP is waiting for roaming execution request after roaming preparation Request/Response exchange.

## Slide 3: Case 1 - Execution via Target AP
链路设置完成
Roam
STA
Current AP
Target AP
1.Prep. Request
4.Link Setup
Response
5.DL data from AP1
Timeout
2.Link Setup & context transfer
STA 2
6.Execution Request
8.Execution Response
UL DATA or OBSS interference
End of transmission with Other STA
DL data from AP2
3.Prep. Response
Issue: During the timeout period between the Preparation Request/Response exchange and Execution Request, STA 2 may initiate transmission with Target AP, or Target AP may be interfered by the OBSS.
Case 1: When Roaming STA send Execution Request to Target AP, Target AP could not receive the Execution Request due to being occupied or OBSS interference. It may result in preparation information being deleted and roaming failure.
Target AP is occupied

## Slide 4: Case 2 - Execution via Current AP
链路设置完成
Roam
STA
Current AP
Target AP
1.Prep. Request
4.Link Setup
Response
5.DL data from AP1
Timeout
2.Link Setup & context transfer
7. Context transfer & DS map switch
STA 2
6.Execution Request
8.Execution Response
UL DATA or OBSS interference
End of transmission with Other STA
DL data from AP2
3.Prep. Response
Delay
TBD frame to start AP2 transmission
Case 2 : When Roaming STA send Execution Request to Current AP, current AP could inform Target AP. However Target AP could not transfer DL data to Roaming STA until the transmission with STA2 is completed (or the OBSS interference ends). It may cause extra roaming latency.

## Slide 5: Protection of Timeout period
Roam
STA
Current AP
Target AP
1.Prep. Request
4.Link Setup
Response
5.DL data from AP1
Timeout
2.Link Setup & context transfer
7. Context transfer & DS map switch
STA 2
6.Execution Request
8.Execution Response
DL data from AP2
3.Prep. Response
NAV
After Preparation Request/Response frame exchange, Target AP could send a TBD frame to keep other nodes staying in NAV state until the timeout.
  Whether to allow data transmission during the timeout period could be negotiated according to QoS requirements, Timeout setup and other TBD parameters.
TBD frame

## Slide 6: Summary
After Preparation Request/Response exchange, Target AP may be occupied by transmission or OBSS interference during the timeout period. This issue might results in extra roaming latency or even roaming failure.
This contribution proposed a solution that Target AP sends a TBD frame to provide protection during the timeout period.
  The details of Target AP’s behavior after the Preparation Request/Response exchange needs further discussion.

## Slide 7: Straw Poll 1
Do you agree that during the timeout period after the Preparation Request/Response exchange, Target AP could provide protection to prevent roaming affected by other transmission and OBSS interference?
  Details of Protection method is TBD