## Slide 1: CoBF MAC Sequence Analysis
Date: May 5th, 2025
Authors:
Name | Affiliation | Address | Phone | Email
Avner Epstein | MaxLinear |  |  | aepstein@maxlinear.com
Oren Kedem |  |  |  | okedem@maxlinear.com
Elad Ben Yosef |  |  |  | ebenyosef@maxlinear.com
Amir Rosenblum |  |  |  | arosenblum@maxlinear.com
Sigurd Schelstraete |  |  |  | sschelstraete@maxlinear.com
Rainer Strobel |  |  |  | rstrobel@maxlinear.com
Iñaki Val Beitia |  |  |  | ival@maxlinear.com

## Slide 2: Introduction
  CoBF is one of the proposed AP Coordination Schemes for UHR
  Ref [1] and [2] outline the applicable MAC sequences that are considered for CoBF as part of 11bn draft.
  The sequences described in Ref [1] and [2] also include sounding.
  CoBF provides theoretic gain in applicable use-cases, as will be shown in the next slides.
  However, the MAC sequences that are described in Ref [2] add considerable overhead which may eliminate all the potential gain of CoBF, as will be shown next.

## Slide 3: CoBF Use-Cases USE CASE A – 4 STAs with single Antenna
  The basic use case for CoBF includes two STAs per each BSS that are located in the overlap zone between the two BSSs.
  AP1 and AP2 have four antennas each, while each STA has a single antenna.
  During CoBF transmission, both AP1 & AP2 transmit a PPDU simultaneously.
  Each AP uses its four antennas to transmit a total of 4STS:
    1STS per each of its associated STAs (e.g. AP1 provides 1STS to STA11 and 1STS to STA12)
    2*1STS for Full Rank Nulling to each of AP2 STAs (STA21, STA22)
  CoBF requires frequent sounding (every ~20msec)
  Since this scheme allows Full-Rank-Nulling it may be supported by either Joint or Sequential Sounding)

## Slide 4: CoBF Use-Cases USE CASE A – 4 STAs with Single Antenna
  When CoBF is disabled:
    Each AP may form an MU-MIMO group of its associated STAs
    Each AP transmits at its own time to its associated STAs; it is assumed that each AP obtains the wireless medium 50% of the time
    For the sake of the example, it is assumed that each STA is able to receive with good SNR at MCS9/1SS, while the AP uses 4 antennas for transmitting a total of 2STS

## Slide 5: CoBF Use-Cases USE CASE A – 4 STAs with Single Antenna
  When CoBF is activated:
    Both AP1 & AP2 transmit simultaneously to their associated STAs while creating null to the other AP’s STAs, hence both APs obtain the wireless medium 100% of the time
    Since each AP “wastes” 2STS for creating the nulls towards the other AP’s STAs, the SNR at the STA’s receivers is degraded (compared with the), hence it is assumed roughly (under worst case conditions) that 2MCSs are reduced compared to the non-CoBF operation; hence, for the sake of the example each STA receives with MCS7/1SS
    For simplifying the example, the illustration does not show any MAC overheads (such as Backoffs, SIFS, Blockack, etc.); these overheads will be analyzed in next slides
    The theoretic CoBF Gain in this example (excluding MAC overhead) is:
      x2 (since both APs transmit simultaneously)
      x0.75 (MCS9MCS7 reduction)
      Total gain is 2*0.75 = ~1.5  roughly between 40-50%

## Slide 6: CoBF Use-Cases USE CASE A1 – 4 STAs with Two Antenna
  In this use case each STA has two RX antennas.
  Each AP uses its four antennas to transmit a total of 4 STS, the same way as in Use Case A
  However, performing the nulling in this use case requires one of the following options to be supported:
    Option 1: via Joint Sounding to allow Partial-Rank-Nulling (the STAs need to support a CSI Report of 8x2)
    Option 2: STAs may disable their secondary RX path when performing CoBF (requires additional signaling to be defined as part of 11bn)

## Slide 7: CoBF Use-Cases USE CASE A1 – 4 STAs with Two Antenna
  When CoBF is disabled:
    As opposed to Use-Case A, each STA is allocated 2STS within the MU-MIMO group
    However, since each AP now uses its four antennas for transmitting a total of 4STS (as opposed to 2STS in Use-Case A), the MCS is degraded compared with the Non-CoBF option in Use-Case A, hence it is assumed that each STA is able to receive with good SNR at MCS7/2SS
  When CoBF is activated:
    Same scheme used for CoBF as in Use-Case A (MCS7/1SS per STA)
    No theoretic CoBF Gain:
      x2 over time is evened out by 1SS (CoBF) instead of 2SS (no CoBF)
      MCS7 used in both modes (CoBF disabled/activated)

## Slide 8: CoBF Use-Cases USE CASE B – 2 STAs with Two Antenna
  This use case includes only one STA per each BSS (total of two) that is located in the overlap zone between the two BSSs.
  AP1 and AP2 have four antennas each, while each STA has two antennas.
  Since this scheme allows Full-Rank-Nulling it may be supported by either Joint or Sequential Sounding)
  When CoBF is disabled, each AP serves its associated STA as a SU

## Slide 9: CoBF Use-Cases USE CASE B – 2 STAs with Two Antenna
  When CoBF is disabled, each AP transmit 2STS to its associated STA using its four antennas 50% of the time; assuming MCS9 for the example
  When CoBF is activated, both APs transmit 2STS simultaneously (100% of the time) to their associated STA while creating null to the other APs STA (using four antennas); assuming 2MCSs drop due to reduced SNR (i.e. MCS7 for the example).
  Same theoretic CoBF Gain as in Use Case A: x2 x0.75 = ~1.5  roughly between 40-50%

## Slide 10: CoBF Sequences
  According to Ref [2] the CoBF Sequences include 3 sections:
    PREPARE: Sharing & Shared AP perform initial handshake (Shared AP may refuse the coordination) and also each AP may send ICF to its STAs (e.g. in case of EMLSR/DPS/etc.).
    SOUNDING: fresh sounding is required every ~20msec prior to CoBF Data transmission
      Sequential Sounding – STAs only need to support Nr=4; Partial-Rank-Nulling is not possible
      Joint Sounding – STAs need to support Nr=8; Partial-Rank-Nulling is possible
    DATA: Sharing AP triggers the Shared AP and both transmit DL Data PPDU, following which the BA from the applicable STAs are solicited by each AP via MU-BAR TF
  NOTES:
    The diagrams are not up to scale
    All PPDUs are SIFS apart
    Since fresh sounding is required every ~20msec, it is assumed from a practical pov, that each CoBF sequence will include a Sounding section
    AP1-STAs and AP2-STAs may include more than one STA, in which case, the PPDU shown is a TB PPDU
    PPDUs designated with C (e.g. ICRC) indicate communication between STA and unassociated AP (“cross”). It is assumed that in such case a very low MCS needs to be used.

## Slide 11: CoBF Sequences with reduced MAC Overhead
    Note: The APs are symmetric (both play alternately either the role of Sharing/Shared AP)

## Slide 12: CoBF Sequences with reduced MAC Overhead
    The Sharing AP shall transmit Control Frames to all STAs (its associated STAs and the Shared AP’s STAs)

## Slide 13: CoBF Sequences with reduced MAC Overhead
    A STA participating in CoBF DL Data TXOP will be able to receive and respond to a broadcast control frame from an unassociated AP (pre-configured to it by its associated AP following CoBF agreement with other APs)

## Slide 14: CoBF Sequences with reduced MAC Overhead
    The BACKs from the STAs to their associated APs shall be provided simultaneously as a TB PPDU (each AP shall aggregate a Basic TF in the A-MPDU that it transmits in the DL Data PPDU)

## Slide 15: CoBF Sequences with reduced MAC Overhead
    The TB feedback from the STAs may either be UL OFDMA or UL MU-MIMO

## Slide 16: MAC Overhead Comparison
  The simulation results for the above table is provided in [3]
  Working Assumptions:
    No-CoBF DL Data PPDU are using 320MHz, MCS9, 1SS/2SS per STA (in Use-Case A/B, respectively)
    CoBF DL Data PPDU are using 320MHz, MCS7, 1SS/2SS per STA (in Use-Case A/B, respectively)
    The analysis assumes full utilization of the DL Data PPDU by both APs (i.e. ~5.4msec PPDU with no EOF padding)
    The analysis uses MCS0 for Cross BSS PPDUs (i.e. between AP1’s STAs and AP2 and vice versa).
    The analysis uses 256usec transition delay in ICF (assuming WC conditions)
    In MxL proposed sequences, the Sharing AP is aware of the Shared APs status and may abort the sequence if deemed unworthy (e.g. Shared AP STAs did not respond to ICF, etc.).
Use Case | Num STA per AP | Ant Per STA | Feedback | TP No CoBF1 [Mbps] | TP 11bn Draft2 [Mbps] |  | TP MxL Proposal2 [Mbps] | 
 |  |  |  |  | Sequential | Joint | Sequential | Joint
A | 2 | 1 | UL OFDMA | 674.66 | 630.95 -6% | 561.35 -17% | 603.60 -11% | 607.32 -10%
 |  |  | UL MU-MIMO | 674.81 | 685.06 2% | 663.79 -2% | 774.88 15% | 814.06 21%
B | 1 | 2 | UL OFDMA | 1,439.43 | 1,391.85 -3% | 1,345.94 -6% | 1,470.34 2% | 1,494.72 4%
 |  |  | UL MU-MIMO | 1,439.43 | 1,391.85 -3% | 1,345.94 -6% | 1,575.59 9% | 1,494.72 4%

## Slide 17: MAC Overhead Comparison
  The simulation results for the above table is provided in [3]
  Conclusions:
    The CoBF sequences as specified in 11bn_D0.2 eliminate all the theoretic gain due to the excessive overhead and in most cases is even worse than not activating CoBF at all.
    The proposed CoBF sequences by MxL always provide higher TP than The CoBF sequences as specified in 11bn_D0.2.
    Soliciting TB feedback from the applicable STAs as UL MU-MIMO always provides lower overhead and higher TP than UL OFDMA.
    In most cases, the proposed CoBF sequences by MxL provide TP gain vs. not activating CoBF at all
    Use Case A with UL MU-MIMO provides the highest TP gain when employing the MxL proposed sequences with UL MU-MIMO TB feedback – 15%-21% out of the theoretic 40-50%
    Sequential vs. Joint Sounding TP gain is use case dependent
Use Case | Num STA per AP | Ant Per STA | Feedback | TP No CoBF1 [Mbps] | TP 11bn Draft2 [Mbps] |  | TP MxL Proposal2 [Mbps] | 
 |  |  |  |  | Sequential | Joint | Sequential | Joint
A | 2 | 1 | UL OFDMA | 674.66 | 630.95 -6% | 561.35 -17% | 603.60 -11% | 607.32 -10%
 |  |  | UL MU-MIMO | 674.81 | 685.06 2% | 663.79 -2% | 774.88 15% | 814.06 21%
B | 1 | 2 | UL OFDMA | 1,439.43 | 1,391.85 -3% | 1,345.94 -6% | 1,470.34 2% | 1,494.72 4%
 |  |  | UL MU-MIMO | 1,439.43 | 1,391.85 -3% | 1,345.94 -6% | 1,575.59 9% | 1,494.72 4%

## Slide 18: SP
  Do you agree to add the option to CoBF sequences in 11bn, so that the Sharing AP can transmit broadcast control frames (e.g. ICF, NDPA, BFRP) to all the STAs that are the recipients of the CoBF DL Data PPDU (including the Shared AP STAs)?
  Do you agree to add the option to CoBF sequences in 11bn, so that the BlockAck from all the STAs that are the recipients of the CoBF DL Data PPDU shall be solicited in a single TB PPDU (by aggregating Basic TF to the DL Data by each of the APs)?

## Slide 19: References
  [1] 24/2142: Multi-AP Sounding Analysis
  [2] 25/0412: CoBF Frame Sequences and Signaling Details
  [3] 25/0765: CoBF Sequences Analysis (CoBF.xlsx)