## Slide 1: Impact of hidden nodes on NPCA performance – Follow up
Date: 7-24-2025

## Slide 2: NPCA: Recap
The BSS of interest detects the OBSS activity, identifies the OBSS transmission length, and determines if they can trigger NPCA
Proper BSS operation of NCPA requires
  R1: Joint operation of AP and non-AP STAs for changing to the non-primary channel
  R2: Joint operation of AP and non-AP STAs for returning to the primary channel, before the OBSS ends, and guarantee fairness re-accessing to the primary channel
ICF
Time
OBSS
ICR
DL/UL Exchanges in the Primary Channel
DL/UL Exchanges in the NPCA Primary Channel
OBSS activity detected
Move to NPCA primary channel
BSS returns to the primary channel before OBSS finishes

## Slide 3: General Simulation Assumptions
Simulation only considers DL traffic
AP initiates a TXOP using RTS/CTS frames, to protect the channel
  NPCA is activated by listening to the RTS/CTS sequence
The OBSS TXOP is limited to one PPDU
  Avoid the problem identified in [1] with the premature termination of the TXOP
All the involved OBSSs are NPCA capable
  The APs have the same bandwidth BW
  The STAs have different bandwidths (BW and BW/2), to allow the activation of NPCA in the OBSS
Assume there is no switching delay for changing the channel
EDCA parameters based on 802.11REVme (Table 9-194)
  For primary and non-primary channel access

## Slide 4: Simulation Setup – 2 BSS
Simulations cover OBSS scenarios under different deployment circumstances, mainly focused on hidden node situations
Two independent 160 MHz NPCA BSSs (BW = 160 MHz), in the same primary channel, each one is composed of one AP and 4 non-AP STAs
Data traffic per non-AP STA for both BSSs
  UDP DL: 150Mps (MCS 9, 1 SS)
Half of the STAs are 80 MHz (BW/2) capable (the advantage to activate NPCA)
AP1
160MHz
AP2
160MHz
STA11
160MHz
STA14
80MHz
STA13
160MHz
STA21
160MHz
STA22
160MHz
STA23
80MHz
BSS1
BSS2
STA24
80MHz
STA12
80MHz

## Slide 5: Simulation Setup – 2 BSS
Gradually, the BSS2 STAs start becoming “Hidden nodes”
The BSS2 AP may also become a Hidden node.
AP1
160 MHz
AP2
160 MHz
STA11
STA14
STA13
STA21
STA22
STA23
BSS1
BSS2
STA24
STA12

## Slide 6: NPCA Simulation Results (2 BSSs)
The NPCA feature enables a 45% of improvement in the aggregated throughput, under ideal circumstances (no hidden nodes)
At each step adding a hidden node in BSS2, the overall performance decreases
  The performance loss is larger when the affected STA is 80 MHz BW.
Once all the BSS2 STAs or the AP are hidden, the performance drops to the lower limit (No NPCA)
  There is a waste of energy for those STAs that change the channel when the AP does not change

## Slide 7: Simulation Setup – 3 BSS
The same setup is proposed, but having 3 BSSs in the same primary channel
In the baseline setup, all the STAs are in the ED/PD range (no hidden nodes)
Like in the previous scenario, the BSS3 STAs and AP are gradually replaced by hidden nodes

## Slide 8: NPCA Simulation Results (3 BSSs)
The NPCA feature enables a 39% of improvement in the aggregated throughput, under ideal circumstances (no hidden nodes)
At each step adding a hidden node in BSS3, the overall performance decreases
  The performance loss is larger when the affected STA is 80 MHz BW.
Once all the BSS3 STAs are hidden, there is still a performance gain, as BSS1 and BSS2 may perform NPCA with each other, but it is less effective as BSS3 AP still tries to get the NPCA Primary channel

## Slide 9: Realistic Simulation Setup
Previous setups assume the OBSS is NPCA capable, but considering more “realistic” deployments:
  OBSS is not NPCA capable and 50% of the STAs are hidden nodes
The performance gain is decreased
  Compared to the baseline, the performance gain is reduced to 13%

## Slide 10: Coordinated NPCA Operation (1/2)
Partial performance decrease is due to the fact that the AP does not know which associated (NPCA capable) STAs have changed to their NPCA Primary Channel
  Channel coordination within the BSS is lost
After the AP changes to NPCA Primary Channel and the AP wins the contention, the AP may transmit a MU BSRP frame to inquire about its STAs, receiving responses from those STAs that changed the channel
  The channel coordination is recovered

## Slide 11: Coordinated NPCA Operation (2/2)
The use of BSRP as ICF (after NPCA activation) attenuates the performance reduction in hidden node scenarios
  All the NPCA TXOPs are used, thanks to the knowledge gained after asking the STAs
Compared to the baseline, the performance gain is increased to 24%

## Slide 12: NPCA Simulation Results - Summary
NPCA should consider deployment limitations such as hidden nodes, remembering that the performance gain will depend on the number of NPCA STAs deployed
The introduction of hidden nodes under different scenarios, as expected, shows a reduction in the NPCA performance gain
The use of a mechanism (e.g., BSRP as ICF) that allows the AP to know in advance which STAs may have changed the primary channel, increases the efficiency, and therefore the overall performance

## Slide 13: References
[1] Inaki Val et al., “Impact of hidden nodes on NPCA performance”, 24/2110r0