## Slide 1: Protection method of OBSS R-TWT for Coordinated AP
Date: 2025-05-08
Authors:

## Slide 2: Introduction
In CC50, there are many comments suggesting that a definition of “Extended Protection” for Co-RTWT is needed in 11bn Draft 0.1 [1]
The motion related to signaling the parameter of Co-RTWT has been agreed on March F2F meeting [2]
  (Motion #362) A Co-RTWT Requesting AP shall include one or more Co-RTWT Parameter Set fields corresponding to each requested R-TWT schedule in the TBD individually addressed Management frame used for the request to the Co-RTWT Responding AP. The Co-RTWT Parameter Set field includes the following:
    Target Wake Time field/Broadcast TWT ID field/Broadcast TWT Persistence/TWT Wake Interval Mantissa/TWT Wake Interval Exponent/Nominal Minimum TWT Wake Duration/TBD other fields
In this contribution, we discuss extended protection for Co-RTWT and propose the related parameter in Co-RTWT negotiation

## Slide 3: Recap: Quiet STAs during R-TWT SPs in 11be
In 11be, R-TWT scheduling AP may schedule at most one quiet interval that overlaps with an R-TWT SP
  A quiet interval, if scheduled, shall have a duration of 1 TU and shall start at the same time as the corresponding R-TWT SP
  Before transmitting an MPDU, the legacy non-AP STA shall check whether sufficient time remains to complete the exchange before the start time of the quiet interval. If there is insufficient time, the STA shall defer transmission by selecting a random backoff count based on the current CW
Quiet Interval
R-TWT SP
1 TU
EHT AP
Non-AP STA 1
Non-AP STA 2
(HE )
Beacon
…
…
…
Defer the transmission
Defer the transmission

## Slide 4: Considerations on protection of Co-RTWT
Same protection rule for the R-TWT SP in 11be is proposed to the Co-RTWT SP in 11bn [3]
  37.8.2.4.3 Co-RTWT announcement rules
    The Co-RTWT coordinated AP's associated STA(s) that support R-TWT follow the rules defined in 35.8.4.1 (TXOP and backoff procedure rules for R-TWT SPs) for the R-TWT schedule(s).
However, the overlapping quiet interval, which is set to protect the R-TWT SP from legacy non-AP STAs, has not yet been considered for Co-RTWT
A Co-RTWT requesting AP may schedule overlapping quiet intervals for one or more R-TWT SPs and may request a Co-RTWT responding AP to protect these R-TWT SPs using Co-RTWT negotiation
To provide the Co-RTWT protection at the same level as R-TWT in 11be, the Co-RTWT requesting AP should be able to request the Co-RTWT responding AP to protect the requested R-TWT schedule using overlapping quiet intervals

## Slide 5: Proposal
We propose a mechanism to ensure that R-TWT SPs protected by overlapping quiet intervals can be protected as the same level in Co-RTWT
  A Co-RTWT requesting AP shall be able to request the Co-RTWT responding AP to schedule overlapping quiet intervals for the requested R-TWT schedule
Co-RTWT Requesting AP
Co-RTWT Responding AP
Co-RTWT
Negotiation
Request frame
Co-RTWT
Negotiation
Response frame
Beacon
1 TU
Quiet Interval
R-TWT SP
Frame exchange
Request to set the overlapping quiet interval
(UHR/EHT STA)

## Slide 6: Proposed Signaling Detail at the Co-RTWT Requesting AP
We propose a 1-bit indication within the Co-RTWT Parameter Set field to request the configuration of an overlapping quiet interval for the requested R-TWT schedule
  When the Quiet Interval Request subfield is set to 1, it indicates that the Co-RTWT requesting AP is requesting Co-RTWT responding AP to configure the overlapping quiet interval to a duration of 1 TU
Fig. A part of Co-RTWT Parameter Set field [3]
Target Wake
Time
Bit:
1
Nominal Minimum TWT Wake Duration
TWT Wake
Interval Mantissa
Service Period Info
B0
B4
B5
B12
B13
B14
B15
Quiet Interval Request
TWT Wake Interval Exponent
Broadcast TWT Persistence
Restricted TWT Schedule Info
2
8
5

## Slide 7: Further Considerations
Conditions for Requesting Overlapping Quiet Intervals by the Requesting AP
  The Co-RTWT requesting AP shall not request the Co-RTWT responding AP to schedule overlapping quiet intervals for the requested R-TWT schedule unless it has also scheduled overlapping quiet interval for the R-TWT schedule
  This condition is necessary to maintain fairness – if the requesting AP does not protect its R-TWT SP from its own legacy non-AP STAs but requests the responding AP to block channel access for its legacy STAs, it creates an imbalance in protection and channel usage
No impact on the result of Co-RTWT negotiation
  The request for overlapping quiet interval scheduling by the requesting AP shall not affect the outcome of the Co-RTWT negotiation. The Co-RTWT responding AP may reject the request by setting the Quiet Interval Request subfield to 0 in Co-RTWT negotiation response frame
  E.g., If the Co-RTWT responding AP has a larger number of legacy STAs compared to EHT/UHR non-AP STAs, scheduling overlapping quiet intervals may lead to throughput degradation within its own BSS.

## Slide 8: Summary
We discussed the issue of requesting overlapping quiet interval scheduling as part of Co-RTWT negotiation
We proposed a signaling mechanism to indicate whether the Co-RTWT requesting AP is requesting the Co-RTWT responding AP to schedule overlapping quiet intervals for the requested R-TWT schedule
  This indication can be included using a one-bit field in the Co-RTWT Parameter Set field
Additionally, we presented further considerations related to the configuration of overlapping quiet intervals
  Restriction on the requesting AP regarding when such a request can be made
  The decision to configure overlapping quiet interval lies with the the Co-RTWT responding AP

## Slide 9: Straw Poll 1
Do you agree to add the following into the 11bn SFD ?
  A Co-RTWT Requesting AP shall include a field that indicates a request for configuring an overlapping quiet interval in the TBD individually addressed Management frame
    1-bit subfield within the Co-RTWT Parameter Set field

## Slide 10: Straw Poll 2
Do you agree to add the following into the 11bn SFD ?
  A Co-RTWT Requesting AP shall not request a Co-RTWT Responding AP to schedule overlapping quiet interval for the requested R-TWT schedule unless it has scheduled overlapping quiet interval for the R-TWT schedule

## Slide 11: References
[1] 11-25/0296 IEEE 802.11bn CC50 comments on D0.1 Ross Jian Yu
[2] 11-25/0014 tgbn-motions-list-part2 Alfred Asterjadhi
[3] 11-25/0600 PDT-MAC-Co-RTWT Signaling and Protocol Aspects Giovanni Chisci