## Slide 1: NSTR Status During NPCA
Date: 2025-05-09
Authors:

## Slide 2: Background
In current baseline operation, a non-AP MLD can signal its STR/NSTR capability for each pair of links during multi-link setup [1]
  Through NSTR Indication Bitmap field
Some transmission behavior/limitation needs to be followed if a link pair is signaled as NSTR to achieve so-called “simultaneously transmit”
In this proposal, we discuss NSTR status update procedure during NPCA operation

## Slide 3: Motivation
According to passed motions [2], while the primary channel is known to be busy due to OBSS traffic, AP and STAs associated with the AP may switch to the NPCA primary channel and initiate transmission on the NPCA primary channel
However, the NSTR status may change during NPCA operation duration due to channel switching, and this issue has not been addressed yet
  If link1 operates on 5 GHz, link 2 operates on 2.4 GHz, they are STR link pair regardless of NPCA channel switching
  If neither of the two links works on 2.4 GHz, their NSTR status may very likely change (see Table below)
NSTR status before switching | Effect caused by switching | NSTR status after switching
STR | Frequency separation decreased; link status changed | NSTR
 | Frequency separation decreased/increased; link status unchanged | STR
NSTR | Frequency separation increased; link status changed | STR
 | Frequency separation decreased/increased; link status unchanged | NSTR

## Slide 4: Motivation
If non-AP MLD does not report its NSTR status during NPCA to the AP MLD, following issue may occur
NSTR status before switching | NSTR status after switching | Effect if not updated
STR | NSTR | AP MLD is unaware of such change, does not follow NSTR transmission limitations, transmission may fail or interfere with the other link
NSTR | STR | AP MLD is unaware of such change, still applies NSTR transmission limitations such as PPDU end time alignment on an NSTR link pair, which is not so efficient

## Slide 5: Proposed Solution
Option 1: Indicate NSTR status (update) in NPCA ICR/ICF
  If non-AP STA can transmit ICR/ICF, it can include such NSTR status in ICR/ICF, then AP MLD apply the new STR/NSTR status during current NPCA operation
  Dynamic
Option 2: Indicate NSTR status (update) in NPCA Capabilities
  Assume the location of NPCA primary channel is known by non-AP, it can signal such NSTR status as a type of capability
  Semi-static
Option 3: Follow some access rules, for example,
  Non-AP do not perform NPCA switching or do not reply ICR if current NPCA txrx may interfere with the txrx of other links
  AP follows NSTR transmission behavior when transmitting NPCA ICF if it expects current txrx may interfere with the txrx of other links of the non-AP MLD

## Slide 6: Further Discussions
Q: Other scenarios?
A: Such issue also exists in DSO operation and NPCA+DSO operation, especially when two links are performing NPCA/DSO, which may very likely happen considering we are developing these two important features
Q: Why not use Multi-Link Operation Update Request frame?
A: Multi-Link Operation Update Request frame is used for long-term update, not suitable for temporary NSTR status update only during NPCA duration
Q: Why not rely on the Frequency Separation for STR parameter?
A: This parameter is only used as a reference value, and it may have no value
“A non-AP MLD may set the Frequency Separation For STR subfield in the Common Info field of the Basic Multi-Link element to a nonzero value if it intends to indicate the minimum frequency separation that is recommended between two links for the non-AP MLD for STR operation; otherwise, the non-AP MLD shall set the Frequency Separation For STR subfield to 0.”[1]

## Slide 7: Conclusion
In this contribution, we discussed the NSTR status change issue caused by channel switching from primary channel to NPCA primary channel and proposed corresponding solutions
  Option 1: Indicate NSTR status (update) in NPCA ICR/ICF
  Option 2: Indicate NSTR status (update) in NPCA Capabilities
  Option 3: Follow some access rule

## Slide 8: Straw Poll 1
Do you agree that the NSTR status change issue caused by channel switching during NPCA duration need to be addressed ?

## Slide 9: References
IEEE P802.11be/D7.0, August 2024
11-24/209r13, Specification Framework for TGbn