## Slide 1: Dynamic MPDU Adjustment for A-MPDU Transmission
Date: 2025-09-04
Authors:
Name | Affiliation | Address | Phone | Email
Shailender Karmuchi | Samsung |  |  | karmuchi.s@samsung.com
Ravi Gidvani | Samsung |  |  | ravi.gidvani@samsung.com
Arif Hussain | Samsung |  |  | 
Yongsen Ma | Samsung |  |  | 
Srinivas Kandala | Samsung |  |  | 

## Slide 2: Problem Statement
Under certain conditions (for eg:- congestion or concurrency) a STA may want to restrict reception of PPDU size due to memory constrain or channel conditions on STA side. [1]
Once a BA session is established then there is no way to indicate to peer STA to temporarily adjust the size of PPDU or reduce the number of MPDUs sent in a PPDU.
Only mechanism exists is for STA to tear down BA session and expect peer STA to renegotiate BA. This mechanism is not only time consuming but also implementation dependent as peer is not obligated to renegotiate the BA session that is used to transmit data stream to current STA.
*In case of seamless roaming STA may have negotiated higher (for eg:- 1K) BA window size with current AP however target AP may be able to accommodate only lower (for eg:- 256 buffers) and would need to renegotiate lower (256) BA window size.
*Open topic of discussion in seamless roaming

## Slide 3: Proposal For MAX number of MPDUs in AMPDU
If an AP or a non-AP STA negotiates the BA session with peer STA after the connection and detects the condition requiring the peer STA to reduce or increase the number of MPDUs in an A-MPDU, it can indicate this using new Control id in A-control field / frame sent.
New Buffer size indication can be 3 bits and have values as follows :
0 ->32 buffers; 1->64 buffers; 2->128 buffers; 3->256 buffers; 4->512 buffers; 5->1024 buffers.
This new A-Control shall also indicate specific TID(s) or ALL TID of the BA session whose number of MPDUs in AMPDU have to be adjusted.
The indications (to reduce or increase the number of MPDUs in an A-MPDU, congestion bit if congestion is detected)

## Slide 4: Proposal For indicating Congestion Detected
To improve the reliability, this new A-Control can also indication for congestion bit which if set indicates congestion is detected. A congestion is described as medium busy with traffic that is not mean for STA’s under consideration.
Upon receiving this A-Control field, the STA shall initiate an RTS/CTS frame exchange before transmitting the data frame.
There exists TXOP Duration RTS Threshold in the HE Operation element, which provides similar functionality to AP side, i.e. AP can enforce all STA use RTS/CTS protection in certain situations. However, in existing standard non-AP STA cannot use RTS Threshold mechanism to enforce such mechanism with its peer.
Above proposal provides a means for any STA to inform it’s peer to use RTS-CTS protection before sending data.

## Slide 5: Proposal For Delete and Renegotiate BA
  Recipient BA peer needs have an ability to delete existing BA session and renegotiate a new BA session. This can be done by adding a new bit (renegotiate BA) in DELBA parameter field. On receiving DELBA control frame with renegotiate BA bit set, initiator BA peer shall initiate a new BA session right after deleting current BA session on same TID. This way Recipient has opportunity to accept or suggest new buffer size.

## Slide 6: Summary
This submission presents a mechanism for a BA originator/recipient STA to indicate to its peer STA to reduce or increase the number of MPDUs in an A-MPDU.
It enables dynamic MPDU adjustment for A-MPDU transmissions under certain channel and traffic conditions, such as congestion and coexistence cases.
It enables a mechanism to inform peer about existence of congestion at destination STA’s environment.
This submission also proposes a mechanism to mandate a peer to initiate a new BA session right after deletion.

## Slide 7: Reference
[1] 20/0362r4, Proposals on AMPDU-BA mechanisms, Sindhu Verma (Broadcom)

## Slide 8: Straw Polls
SP1: Do you agree to include the following into the TGbn SFD?
For two STAs with a BA agreement, the originator/recipient STA may indicate to the recipient/originator STA to request to reduce or increase the number of MPDUs for A-MPDU transmissions for a particular BA Session.
Note 1: the indication can be sent in TBD conditions.
Note 2: the indication can be sent in A-Control Control field/frame.
Result: Y, N, A

## Slide 9: Straw Polls
SP1: Do you agree to include the following into the TGbn SFD?
A STA with a BA agreement to indicate congestion and enforce its peer to request RTS-CTS exchange before PPDU transfer.
Result: Y, N, A

## Slide 10: Straw Polls
SP2: Do you agree to introduce a mechanism to force originator delete and immediately initiate BA session.
Result: Y, N, A