## Slide 1: Adaptable Traffic Indication
Date: 2025-05-09
Authors:

## Slide 2: Introduction
In this proposal, we discuss the current traffic indication methods and their limitations, then propose a new flexible method

## Slide 3: Current Methods
Current baseline [1] :
  BSRP polling + BSR feedback is used for solicited buffer indication
  QoS Control and BSR Control can be used for unsolicited buffer indication
Enhanced BSR in 11bn [2] :
  EBSR has been introduced to report a larger per TID queue size
Proposal [3]:
  For MAPC, indicate requested medium time, TID/AC, expiration time of the traffic in a new control field in a QoS Null frame or Multi-STA BA (MBA) frame
Proposal [4]:
  Use MBA container to carry QoS Control, BSR Control, EBSR Control in original Block Ack Bitmap field

## Slide 4: Limitations
For solicited buffer indication, TXOP holder cannot indicate the traffic constraint or requirement for its solicited feedback
  such as allowed traffic type, traffic direction, whether reported in terms of queue size or TXOP duration
For traffic reporter, QoS Control, BSR Control, EBSR Control have limited traffic information, which may not fit the growing need for low latency indication, MAPC traffic indication, multi-directional traffic indication, AP’s scheduling decision, TXS decision
  QoS Control lies in MAC header, modifying this field may cause legacy incompatibility issue
  BSR Control and EBSR Control can only report TID and Queue Size information
  EBSR has 2 reserved bits, there is no extra room to carry extended traffic information

## Slide 5: Adaptable Traffic Indication
TXOP holder indicates the traffic constraint or requirement for the solicited feedback in BSRP/BSRP GI3
  Traffic Type Constraint: provide AC constraint or TID constraint
    Report traffic only from the same AC as the last Data frame received from the TXOP holder;
    Report traffic from any TID
  Traffic Direction Constraint
    Between AP and non-AP: Reverse Direction, Other Direction; DL, UL, P2P
    Between AP and AP: report AP’s traffic for associated STAs or for other APs
  Queue Size/TXOP Duration Requested
    Choose either one of these two, provide flexibility
Traffic reporter indicates traffic information in MBA or a new control field
  AC/TID Type; Traffic Direction; Traffic Expiration Time, TSF Info
  Queue Size/TXOP Duration; Resource Sharing Requested
If TXOP holder indicates the traffic constraint, traffic reporter shall follow such constraint

## Slide 6: Conclusion
In this contribution, we discussed the limitations of current traffic indication methods and proposed an adaptable traffic indication method
  TXOP holder can indicate the traffic constraint or requirement for its solicited feedback
  Traffic reporter can indicate extended traffic information that can fit the growing need for low latency indication, MAPC traffic indication, multi-directional traffic indication, AP’s scheduling decision, TXS decision
Notes: In this proposal, we focus on the TXOP level preemption, introducing a credibility criterion to assist the fair classification among streams and honest behavior between STAs to further promote the preemption feature

## Slide 7: Straw Poll 1
Do you agree that the current traffic indication methods need to be improved to allow more adaptable traffic report/indication?

## Slide 8: References
IEEE P802.11-REVme/D7.0, August 2024
11-24/209r13, Specification Framework for TGbn
11-24/2126, Intention Announcement and Feedback in Multi-AP Coordination, Jason Yuchen Guo et al.
11-25/0312, BSR in M-STA BA, Seongho Byeon et al.