## Slide 1: Further Considerations on Multi-AP Coordination
Date: April 16, 2025
Authors:
Name | Affiliations | Address | Phone | Email
Pei Zhou | TCL | Building G1, TCL International-E City, Shenzhen, Guangdong, China. |  | zhoupei36@gmail.com
 | TCL |  |  | 

## Slide 2: Background
Currently, TGbn is defining multiple multi-AP coordination mechanisms [1] [2]
  for example, Co-TDMA, Co-BF, Co-SR, Co-RTWT.
Some of them may be used together to achieve efficient coordination and medium usage,
  for example, instead of executing backoff to obtain a TXOP to perform Co-BF/Co-SR, AP 2 and AP 3 (or, AP 2 and AP 1) can use the TXOP time duration shared by AP 1 to perform Co-BF/Co-SR
  In this proposal, we discuss some updates to the Co-TDMA procedure to achieve jointly use of two or more multi-AP coordination mechanisms

## Slide 3: Recap of Co-TDMA Procedure
The coordinated time division multiple access (co-TDMA) procedure enables an AP to share a time portion of an obtained TXOP with another AP that belongs to a set of APs (the set is TBD and can consist of one AP) to transmit one or more PPDUs.
  The set can be a Co-BF/Co-SR set

## Slide 4: Proposed updates to Co-TDMA Procedure
Intention to perform Co-BF/Co-SR and its peer AP
Shared TXOP usage mode (Co-BF/Co-SR) and intended APs
AP 1 & AP 3
AP 2 & AP 3
Perform
Co-BF/Co-SR
ICR indicates polled AP’s intention to perform Co-BF/Co-SR (and its peer AP’s ID, if it is not sharing AP)
MU-RTS TXS TF additionally indicates the allowed mode (e.g., Co-BF/Co-SR/others) and intended APs (e.g., AP 1 and AP 3, or AP 2 and AP 3) during the shared TXOP
  It is TBD MU-RTS TXS TF indicates only one or two Co-TDMA coordinated AP(s)
Frame exchange during shared TXOP: perform indicated mode (e.g., Co-BF/Co-SR/others)

## Slide 5: Discussions on TXOP Sharing Updates
If the shared TXOP is used by AP 1 (i.e., Co-TDMA sharing AP) and AP 3 (i.e., Co-TDMA coordinated AP) for Co-BF/Co-SR, the following may apply
  A new TXS Mode* may be added to support AP 1 (and AP 3 concurrent) DL transmission
  Note*: In EHT [3], we have mode 1 for STA’s UL, and mode 2 for STA’s UL and P2P
  If the shared TXOP is used by AP 2 and AP 3 (both are Co-TDMA coordinated APs) for Co-BF/Co-SR, the following may apply
  Define new rule to allow two intended APs to be allocated to the same shared TXOP time period
    MU-RTS TXS TF includes two separate User Info fields, each corresponds to an AP
  A new TXS Mode* may be added to support AP 2 and AP 3 concurrent DL transmission

## Slide 6: Summary
Co-TDMA can be used as a basis for obtaining TXOP to perform Co-BF/Co-SR
The following updates may be needed
  ICR indicates polled AP’s intention to perform Co-BF/Co-SR
  MU-RTS TXS TF indicates the shared TXOP is used for Co-BF/Co-SR
  MU-RTS TXS TF indicates one or two intended APs
  TXS Mode updates to support Co-BF/Co-SR in the shared TXOP

## Slide 7: Straw Poll 1
Do you agree to add the following text to the TGbn SFD:
Co-BF/Co-SR is allowed to be performed during the TXOP shared by Co-TDMA sharing AP.
Y/N/A

## Slide 8: Straw Poll 2
Do you agree to add the following text to the TGbn SFD:
In order to perform Co-BF/Co-SR within the shared TXOP in Co-TDMA, the following updates may apply:
  Polled AP indicates its intention to perform Co-BF/Co-SR in the ICR of Polling phase
  MU-RTS TXS TF may include two User Info fields, each corresponds to a Co-TDMA coordinated AP
  MU-RTS TXS TF may indicate the shared TXOP is used for Co-BF/Co-SR
  A new TXS Mode is added to support Co-BF/Co-SR in the shared TXOP
Note: detailed signaling and frame formats are TBD.
Y/N/A

## Slide 9: References
[1] 11-24-0209-11-00bn-specification-framework-for-tgbn
[2] Draft P802.11bn_D0.2
[3] Draft P802.11be_D7.0