## Slide 1: Multi-level Protection in Co-RTWT Operation
Date: 2025-03-24
Authors:

## Slide 2: Abstract
IEEE P802.11bn D0.2 has defined coordinated restricted target wake time (Co-RTWT) operations in the Multi-AP coordination framework[1]
In this contribution, we discuss the multi-level protection mechanisms in Co-RTWT operation

## Slide 3: Recap
TGbn has made progress on Co-RTWT with following motions passed.
[Motion #48, [2]]
Define mechanisms that enable APs to coordinate their rTWT schedule(s) and/or to ensure that one AP provides the protection of the rTWT schedule(s) of the other AP.
NOTE – TBD mechanisms including negotiation between 2 APs and advertisement.
[Motion #149, [2]]
If an AP extends the protection of the rTWT schedule of another AP, following negotiation or through other means, then:
  The AP shall ensure its TXOP ends before the start time of the corresponding OBSS rTWT SP(s)
  The AP, if it has at least one associated STA that is capable of rTWT, shall advertise in the beacon frames it transmits the OBSS rTWT schedule so that its associated STAs supporting rTWT follow the baseline rTWT rules for the OBSS rTWT schedule.
[Motion #362, [2] ]
A Co-RTWT Requesting AP shall include one or more Co-RTWT Parameter Set fields corresponding to each requested R-TWT schedule in the TBD individually addressed Management frame used for the request to the Co-RTWT Responding AP. The Co-RTWT Parameter Set field includes the following:
  Target Broadcast TWT ID field
  Broadcast TWT Persistence
  TWT Wake Interval Mantissa
  TWT Wake Interval Exponent
  Nominal Minimum TWT Wake Duration
  TBD other fields
  Wake Time field

## Slide 4: Medium Access during Co-RTWT SP in 11bn
Some Channel access policies in previous contributions:
    Ending TXOP before the Co-RTWT SP start time[3-4]
      Responding AP shall ensure that its TXOP ends before the start time of the SP
    Access to channel by negotiating Co-TDMA or Co-SR or Co-BF [5]
      Responding AP may piggyback Co-TDMA/Co-SR/Co-BF information in the Co-RTWT negotiation and access to channel by Co-TDMA or Co-SR or Co-BF mechanism
    Access to channel by R-TWT sharing [6]
      Responding AP access to channel by requesting AP to share the TXOP obtained during the R-TWT SP

## Slide 5: Considerations in Co-RTWT SP
Overprotection/ Network efficiency Issues
  The requesting AP may not leverage the SP, which reduces the whole network efficiency, while the responding AP (OBSS) provides the protection for the whole SP duration
Overlapped SP issues
  The Co-RTWT coordination negotiation may be failed due to the overlapped RTWT SP in OBSS
Requesting AP
TX/RX
Access forbidden
Co-RTWT SP
Responding AP
Idle (Overprotected)
BSS-1
RTWT SP in BSS-1
RTWT SP in BSS-2
BSS-2
Co-RTWT SP protection Negotiation Failing

## Slide 6: Proposal: Multi-level Protection in Co-RTWT
OBSS APs negotiate Multi-level protection for the Co-RTWT SP
  Level 1: Robust protection (eg, non-overlapped RTWT SP)
    Responding AP and its associated STAs shall not access to the channel during the Co-RTWT SP
    Responding AP may switch into Power Saving state for higher power efficiency
  Level 2: MAP coordinated transmission (MAPCT) protection (eg, overlapped RTWT SP)
    The channel access in controlled by the requesting AP
    Responding AP may access to the channel by Co-TDMA, Co-BF and Co-SR
  Level 3: Other protection
    Eg., Responding AP may access to channel by negotiating a non-overlapped NPCA primary channel
Requesting AP
Responding AP
Protection level request
Protection level response
Co-RTWT coordination negotiation procedure

## Slide 7: Examples
When Robust protection negotiated, the power efficiency can be improved in responding AP
When MAPCT protection negotiated, the OBSS network efficiency can be improved
Requesting AP
Robust protection Request
Robust protection Response
Co-RTWT SP
TX/RX
AP Power Save
Responding AP
Requesting AP
MAPCT protection Request
MAPCT protection Response
Co-RTWT SP
TX/RX
TX/RX
Responding AP

## Slide 8: Summary
In this contribution, we propose a multi-level protection mechanism in Co-RTWT operation that throw a potential method to leverage the channel resource and improve the efficiency in the MAP OBSS system.
  Multi-level protection may include
    Robust protection
    MAP coordinated transmission protection (details are TBD)
    Others protection (eg, Co-RTWT based NPCA primary channel negotiation )

## Slide 9: Straw Poll 1
Do you agree to add the following text to the TGbn SFD?
  Define a multi-level protection mechanism for Co-RTWT coordination negotiation
    Multi-level protection may indicates either;
      Robust protection
      MAP coordinated transmission protection (details are TBD)
      Others protection is TBD (eg, Co-RTWT based NPCA primary channel negotiation )

## Slide 10: References
[1] IEEE P802.11bn D0.2
[2] 11-24/0209r13, Specification Framework for TGbn
[2] 11-23/0226r3, Coordination of R-TWT for Multi-AP Deployment
[3] 11-24/0678r2, Coordinated R-TWT Follow Up
[4] 11-25/0011r0, Co-RTWT Follow Up
[5] 11-25/0289r2, R-TWT Sharing Follow-Up