## Slide 1: UHR OFDMA Sounding Limitations
Date: February 11th, 2025
Authors:
Name | Affiliation | Address | Phone | Email
Avner Epstein | MaxLinear |  |  | aepstein@maxlinear.com
Oren Kedem |  |  |  | okedem@maxlinear.com
Elad Ben Yosef |  |  |  | ebenyosef@maxlinear.com
Sigurd Schelstraete |  |  |  | sschelstraete@maxlinear.com

## Slide 2: Introduction
  EHT Sounding provides inherent support for (static) preamble puncturing; however, it includes some inherent inefficiencies as described in [1].
  UHR introduces renewed interest in MU-MIMO in an OFDMA PPDU
    Note: referred to as ‘Partial Bandwidth MU-MIMO’ in 802.11be spec
  In this contribution we describe how the sounding inefficiencies, that stem from the original definition of 11be, impact MU-MIMO + OFDMA in UHR.
  Further enhancements will need to be introduced into UHR Sounding Procedure in order to efficiently support MU-MIMO + OFDMA.

## Slide 3: EHT Sounding Reminder
  The sounding procedure, defined in the 802.11be spec, consists of multiple frames, as depicted in the following diagram:
  Note: a STA may be requested by the AP to provide a partial BW report, in granularity of either 20MHz/40MHz for 160MHz/320MHz NDP BW, respectively.

## Slide 4: EHT Puncturing Reminder
  The 802.11be spec defines the following puncturing schemes:
    EHT MU (non-OFDMA) has 45 supported patterns that correspond to non-OFDMA Large MRUs, defined by the 5-bit punctured channel indication in the U-SIG field
      See Table 36-30
    EHT MU (OFDMA) – any one of 7 puncturing patterns is supported for each 80MHz subblock (‘0111’,’1011’,’1101’,’1110’,’0011’,’1001’,’1100’) by using 4 of 5 bits of the punctured channel indication in the U-SIG field
    Note: every non-OFDMA puncturing pattern is also regarded as an OFDMA puncturing pattern, but not vice versa.
  An AP uses the Disabled Subchannel Bitmap in the EHT Operation Element to indicate to all STAs which subchannels should not be used for any PPDU exchanges on this operating channel in this EHT BSS
    The Disabled Subchannel Bitmap shall correspond to one of the non-OFDMA puncturing patterns
      See 35.15.2
    An AP may puncture other subchannels in addition to those indicated in the Disabled Subchannel Bitmap in a DL PPDU, provided that the AP’s transmission carries a triggering frame that solicits a TB PPDU from any responding STAs
      No additional puncturing allowed in frames that expect immediate response

## Slide 5: Static vs. Dynamic Puncturing
  For clearer explanation of the problem, we would like to introduce the following concepts:
    Static Puncturing: only subchannels indicated as being punctured in the Disabled Subchannel Bitmap in the EHT Operation Element (i.e. having a value of ‘1’); as such, this puncturing pattern must conform with Non-OFDMA puncturing.
    Dynamic Puncturing: subchannels indicated as not being punctured in the Disabled Subchannel Bitmap in the EHT Operation Element (i.e. having a value of ‘0’), may be punctured by the AP (in addition to the Static Puncturing) due to dynamic interference based on CCA within the current TXOP.
  The combined Static+Dynamic Puncturing must conform to either OFDMA or non-OFDMA puncturing, depending on the DL PPDU. OFDMA puncturing which does not also conform to non-OFDMA puncturing pattern is only allowed in an OFDMA PPDU.
  Hereby an example of dynamic OFDMA puncturing:

## Slide 6: MU-MIMO in OFDMA and Sounding
  Supporting MU-MIMO on one or more RUs in an OFDMA PPDU exist since 11ax but is not utilized
  In [2], a set of combinations of OFDMA+MU-MIMO are proposed for 11bn for getting better vendor adoption
  As opposed to OFDMA, DL MU-MIMO highly benefits from a fresh sounding prior to any Data sequence.
  The inherent limitations of EHT Sounding may make MU-MIMO in OFDMA unusable under certain conditions, as will be explained in the next slides.

## Slide 7: Problem Statement
  The following example shows a 160MHz PPDU with the following RUs:
    RU#1: 996 tone RU designated for DL MU-MIMO
    RU#2: 484+242 tone RU designated for DL MU-MIMO (20 MHz removed due to static puncturing)
  Due to Busy Medium, also RU#1 needs to be punctured (and reduced to 484+242)
  This is permitted according to EHT OFDMA puncturing; however, this configuration cannot be sounded, since NDP must conform to Non-OFDMA puncturing.
  Hence, the AP must fall back to one of the following options:
    Utilize the entire 160MHz (punctured) for OFDMA only without fresh sounding
    Reduce the BW to 80MHz (punctured) to allow Full BW MU-MIMO with fresh sounding

## Slide 8: Problem Statement (2)
  The following example shows a 320MHz PPDU with the following RUs:
    RU#1: 2x996 tone RU designated for DL MU-MIMO
    RU#2: 996+484 tone RU designated for DL MU-MIMO (40 MHz removed due to static puncturing)
  Assume that the upper 20MHz subchannel of RU#1 has interference, hence RU#1 also needs to be punctured; however, since the partial BW info field in NDPA is limited to 40MHz granularity, RU#1 must be reduced to 996+484
  This is permitted according to EHT OFDMA puncturing; however, similar to the 160MHz example, this configuration cannot be sounded, since NDP must conform to Non-OFDMA puncturing.
  Hence, the AP must fall back to one of the following options:
    Utilize the entire 320MHz (punctured) for OFDMA only without fresh sounding
    Reduce the BW to 160MHz (punctured) to allow Full BW MU-MIMO with fresh sounding

## Slide 9: Proposed solution
    Introduce a new NDP PPDU variant for 802.11bn – UHR NDP, that will be designated as an OFDMA PPDU, thus enabling the puncturing available in OFDMA PPDUs.
    802.11bn shall support the following sounding flavors:
No. | Purpose | Procedure | NDP Flavor | Comment
1 | OFDMA/Full BW MU-MIMO with Non-OFDMA Puncturing | 35.7 – EHT sounding operation | EHT | No change from 11be
2 | CoBF (Joint & Seq) | 37.12 – UHR Co-BF sounding operation | EHT | An entirely new sequence for 11bn
3 | OFDMA/Partial BW MU-MIMO with OFDMA Puncturing | 37.XX – New procedure for UHR | UHR (new!!) | Optional new sounding procedure for 11bn (based on 35.7, but using UHR NDP)

## Slide 10: Conclusions
  We described how the fact that EHT NDP must conform to Non-OFDMA puncturing severely restricts the employment of MU-MIMO in OFDMA.
  This limitation may also reduce the attractiveness of DSO, which is also planned for UHR.
  It is our view that 802.11bn should address this issue by introducing a new NDP flavor UHR NDP as an OFDMA PPDU, thus enabling the puncturing available in OFDMA PPDUs.
  The sounding procedure for OFDMA/Partial BW MU-MIMO with OFDMA Puncturing shall be based on the existing EHT Sounding procedure but using UHR NDP instead of EHT NDP.
  The new sounding procedure shall be based on EHT Sounding but using UHR NDP instead of EHT NDP.
    The effort to support this seems relatively small

## Slide 11: SP
  Do you agree to define a new NDP flavor (UHR NDP), that will be designated as OFDMA PPDU, thus be able to support OFDMA puncturing schemes?
  Do you agree to define a UHR Sounding Operation procedure, that will be based on EHT Sounding Operation but using UHR NDP instead of EHT NDP, in order to be able to perform fresh sounding for Partial BW DL MU-MIMO?
  Yes / No / Abstain

## Slide 12: References
  [1] 21/1778: EHT Sounding Enhancements
  [2] 24/1827: On OFDMA and MU-MIMO