## Slide 1: ML-KEM in 802.11

## Slide 2: Introduction
In this presentation, we offer some high level thoughts on ML-KEM in 802.11 .

## Slide 3: Recap: PTK/PMK generation based on public key cryptography in 802.11 today
DH cryptography is widely used in different protocol to generate PTK or PMK
  In SAE/OWE, 4-way handshake between AP and non-AP STA to generate PMK or PTK via DH algorithm.
  In PASN, 3-way handshake between AP and non-AP STA to generate PMK or PTK via DH algorithm.
STA
AP
Beacon(RSNE,RSNXE)
authentication(commit)
authentication(commit)
authentication(confirm)
authentication(confirm)
SAE protocol

## Slide 4: Single directional vs. bi-directional ML-KEM
[1] proposes bi-directional ML-KEM message exchange while [2] proposes single direction ML-KEM in OWE protocol.
Single directional ML-KEM requires at least 3-way handshake.
  Compatible with SAE、OWE、PASN protocol
Bidirectional ML-KEM requires at least 4-way handshake.
  Compatible with SAE and OWE, but conflict with current PASN protocol.
The task group should make the early decision on the direction
  A uniformed solution(single directional or bi-directional) for all security protocols
  Some protocols support single ML-KEM, while others support bi-directional ML-KEM

## Slide 5: The following figure depicts 3-way handshake and 4-way handshake for single directional ML-KEM and bi-directional ML-KEM respectively
STA
AP
Encapsulation key, E1
Ciphertext, C1、MIC1
K
K’
MIC2
STA
AP
Encapsulation key, E1
Ciphertext, C1、Encapsulation key E2
K1
K1’、K2
Ciphertext, C2、 MIC1
MIC2
Single direction ML-KEM
Bidirectional ML-KEM
Note: the MIC is used to verify the K=K’, can be replaced with confirm message.
K2

## Slide 6: The compatible issue of public key in Beacon
[1] propose the public key included in Beacon frame.
  Assuming the AP support ML-KEM-512,ML-KEM-768 and ML-KEM-1024 algorithm, totally 800+1184+1568=3552 octets will be added into Beacon frame, which will cause a serious Beacon bloating issue.
[3] and [4] complained the Beacon bloating issue caused by new features signaling in Beacon frame in other group.
  A larger beacon may cause the compatible issue with the legacy devices.
Parameter set | Encapsulation key (octets) | Decapsulation key (octets) | Ciphertext (octets) | Shared secret key (octets)
ML-KEM-512 | 800 | 1632 | 768 | 32
ML-KEM-768 | 1184 | 2400 | 1088 | 32
ML-KEM-1024 | 1568 | 3168 | 1568 | 32

## Slide 7: The proposal to avoid the Beacon bloating issue
If this is the requirement that one encryption key should be exchanged before the authentication procedure.
  Following the similar procedure proposed in [3] and [4], only add the support indication of ML-KEM-512,ML-KEM-768 and ML-KEM-1024 in the RSNXE.
  The PQC STA may query the encryption key of one ML-KEM algorithm via a probe request frame, and then AP provides the corresponding encryption key via the probe response frame.

## Slide 8: The following figure depicts an example for the STA to obtain the encryption key of ML-KEM
STA
AP
Beacon frame(RSNXE[ML-KEM-512/768/1024])
probe request(RSNXE[ML-KEM-512])
probe response(encryption key E1,ML-KEM-512)

## Slide 9: Summary
High level discussion on how to incorporate ML-KEM into current protocols.
  Propose to define a uniformed solution(single direction or bidirection ML-KEM) for all security protocols(SAE, OWE, PASN, etc.) to simplify the implemation.
Analyse the possible compatible issue if encyption key including in Beacon frame.
  Propose the encyption key shall be obtained by the STA via probe request/response frame exchange to void the Beacon bloating issue if encryption key need to be exchanged out of the authenciation frame.

## Slide 10: Reference
[1]. 24/1103r1 Post-Quantum 802.11
[2]. 25/218r1 Post-Quantum Opportunistic Wireless Encryption (OWE)
[3]. 24/1880 Solutions for Beacon Bloating
[4]. 24/1888 Light beacon consideration
[5]. 11-25/0462r2 Post Quantum Crypto Project submission, Mike Montemurro
[6]. https://media.defense.gov/2022/Sep/07/2003071836/-1/-1/0/CSI_CNSA_2.0_FAQ_.PDF

## Slide 11
THANK YOU 

## Slide 12: SP1
Do you agree to add the following text into PQC PAR?
This amendment shall be backward compatible with legacy IEEE 802.11 devices(E.g. the encryption key of ML-KEM shall not be added into Beacon frame).

## Slide 13: Reference
1. 11-24/1103r1 “Post-Quantum 802.11”, Dan Harkins
2. 11-25/0218r2 Post-Quantum Opportunistic Wireless Encryption (OWE)”, Alex Lungu
3. 11-25/0462r2 Post Quantum Crypto Project submission, Mike Montemurro
4. https://media.defense.gov/2022/Sep/07/2003071836/-1/-1/0/CSI_CNSA_2.0_FAQ_.PDF