## Slide 1: Details on Ove-the-DS Probe Mechanism
Date: 2025-04-22
Authors:
July 2024
Notes: September 2012

## Slide 2: Introduction
Considering the following motion had been approved in 11bn, this contribution discusses some details on the over-the-DS probe mechanism.
(Motion 333) Move to add to the TGbn SFD the following:[1]
Define a mechanism to retrieve probe response content for neighboring AP MLD(s) of the current AP MLD, through the current AP MLD
Note. The neighboring AP MLD and the current AP MLD are in the same ESS
Generally, there are two options to design the over-the-DS probe mechanism.
  Option 1. One is to reuse the existing ML Probe Request/Response frames with some modifications;
  Option 2. the other one is to define new protected Action frames by leveraging the existing ML probe design.
In this contribution, we will also compare these two options.

## Slide 3: Existing ML Probe
The existing ML probe allows a non-AP STA affiliated with a non-AP MLD to request an AP affiliated with an AP MLD to include the complete or partial profile of the AP(s) affiliated with the AP MLD in the ML Probe Response frame.[2]
  Note that the complete profile on the transmitting link shall be included within ML Probe Response frame body (excluding the Basic ML element). For the over-the-DS probe scenario, this info is useless.

## Slide 4: Option 1. Reuse Existing ML Probe
Option 1a. Don’t include the info on the transmitting link of the current AP MLD with the ML Probe Response frame body (excluding Basic ML element)
  The info on target AP MLD is indicated through Basic ML element.
  Issue: There is no way to indicate the following info on the AP corresponding to the link indicated through the Probe Response frame body (excluding Basic ML element),
    E.g. BSSID, Operating Class, Channel Number, which are missing in the current Probe Response frame
  Solution. Include the info on all APs affiliated with the target AP MLD in RNR
Option 1b. Still include the info on the transmitting link of the current AP MLD within the ML Probe Response frame body
  The info on target AP MLD is indicated through per-STA profile subelements of a second Basic ML element. The first Basic ML element without any per-STA Profile subelement is used to indicate the current AP MLD.
    First Basic ML element: Link ID Present = 1; Second Basic ML element: Link ID Present = 0
  Issue: how to carry the MLD-level info on the target AP MLD, e.g. T2L Mapping element, Multiple BSSID element and so on?
  Solution. Modify the current inheritance rules to allow the MLD-level info to be include within the Per-STA Profile?  more complex！
Note that ML Probe Request/Response frames are unprotected.

## Slide 5: Over-the-DS Probe Mechanism
Essentially, the over-the-DS probe mechanism is the interaction between the non-AP MLD and the target AP MLD through the current AP MLD. In other words, the current AP MLD shall tunnel the received probe request (or response) to the target AP MLD (or the non-AP MLD).
  It’s not feasible and efficient way to let the current AP MLD always store the complete profiles of the APs affiliated with the neighboring AP MLD and generate the probe response, especially considering there exists some dynamic parameters.
  Before initiating the link setup with the target AP MLD through the current AP MLD, the non-AP MLD normally needs to get the complete profiles of the APs affiliated with the target AP MLD by leveraging the over-the-DS probe.
We should clearly describe the behaviors of the current AP MLD and target AP MLD when receiving the over-the-DS probe request/response, rather than completely leave it to the implementation.
  Otherwise, there is a risk on the interoperation between different AP vendors and may cause the failure of the 11bn roaming feature. Note that it’s a very general scenario to deploy APs from different AP vendors in an ESS. Even for the SMD, the spec. also doesn’t prohibit this scenario.

## Slide 6: Option 2. Tunneled Probe Request/Response frames
Define a new protected action frame exchange, e.g. Tunneled Probe Request/Response frames.
  Similar issue: There is no way to indicate the following info on the AP corresponding to the link indicated through the Probe Response frame body (excluding Basic ML element),
    E.g. BSSID, Operating Class, Channel Number, which are missing in the current Probe Response frame
  Solution. Include the info on all APs affiliated with the target AP MLD in RNR of the Probe Response frame body field of the Tunneled Probe Response frame
This design can minimize the changes on the existing ML probe mechanism.
  Which also facilitates the current AP MLD’s parsing.
Order | Info
1 | Category
2 | Action
3 | Non-AP MLD Address
4 | Target AP MLD Address
5 | Probe Request frame body
Table. Tunneled Probe Request frame Action field
Table. Tunneled Probe Response frame Action field
Order | Info
1 | Category
2 | Action
3 | Non-AP MLD Address
4 | Target AP MLD Address
5 | Probe Response frame body

## Slide 7: Message flow

## Slide 8: Other Details
The non-AP MLD can obtain the target AP MLD address info by leveraging the BTM operation or directly set the Target AP MLD Address subfield to a broadcast address.
  If the Target AP MLD Address subfield is set to a broadcast address, then the current AP MLD will tunnel the received Tunneled Probe Request frame to all the known neighboring AP MLDs in the same ESS.
    The AP MLD ID of the Common Info field in Probe Request ML element of the Tunneled Probe Request Action frame is set to 255.
The current AP MLD will reply to the non-AP MLD with received Tunneled Probe Response frame(s).
If a wired time synchronization protocol (e.g. 802.1AS Precision Time Protocol) is implemented within the DS and the current AP MLD knows the TSF offset info with respect to the target AP MLD, the current AP MLD may adjust the Timestamp value before replying the Tunneled Probe Response frame to the non-AP MLD.
  Otherwise, the Timestamp subfield of the Probe Response frame body subfield of the Tunneled Probe Response frame is reserved.

## Slide 9: Summary
In this contribution, we propose a very simple solution to enable the over-the-DS probe mechanism by newly defining Protected Tunneled Probe Request/Response frames.
Compared with reusing the existing ML probe (i.e. option 1), the proposed option 2 has the following advantages, e.g.
  Signaling overhead: no need to include the info of the transmitting link, which is useless for roaming
  Security: Tunneled Probe Request/Response frames are protected.
  Complexity: no need to change the current inheritance rules; More simpler to parse for the current AP MLD.
  Interoperation: the behaviors of the current AP MLD and the target AP MLD are clearly described. There is no risk on the interoperation between different AP vendors.
In addition, a broadcast over-the-DS probe manner is proposed, which allows the non-AP MLD to gather the info on all the known neighboring AP MLDs (e.g. on-hop neighbors).

## Slide 10: References
[1] 11-25-0014-14-00bn-tgbn-motions-list-part-2
[2] Draft P802.11be_D7.0.pdf

## Slide 11: SP
Do you support to define new protected Action frames to retrieve probe response content for neighboring AP MLD(s) of the current AP MLD, through the current AP MLD
  Note. The neighboring AP MLD and the current AP MLD are in the same ESS.