## Slide 1: On Interference Mitigation Pilots
Date: May 11, 2025
Authors:

## Slide 2: Interference Sources
To understand the interference Sources [1]:
  Bluetooth [2.4GHz, 1/2 MHz, low power, 1600/ x0-x00hop/s, 600us/x-x0ms per hop]
  UWB [3-10GHz, wideband, very low power, >500MHz]
  Radar [ 2-4GHz(S band) and other bands, wideband]
  WLAN Sig (11b/11a/…, OBSS, fully or partially overlapped)
  Spur (from RF or other sources, like USB)
  Dc leakage [supported from the beginning with null subcarriers around indices as “0”]
  Other signals (NRU, LTEU, or other signals)…
Interference type at frequency domain
  Partial band/wideband
  Narrow band with hopping or not
  Spur like
  Inband, ACI or AACI …
Interference type at Time domain
  It happens within STF (AGC), or any data Part (Detect)

## Slide 3: Potential Scenarios for IM Pilots (1)
Transmission
Benefits may be achieved with following methods:
  For interference with small power, IM pilots would be utilized within equalizer with interference reduction & whiten.
  For narrow band or spur with large power, the soft LLR of the symbols around the interference would be set as 0 or updated directly.
  For too large interference , the receiver may drop the rxProcess for power saving.
  It would provide better noise estimation performance for bands without interference.
  The interference info could be reported to aid the data transmission or retransmission.
LSIG&RLSIG
UHR
Preamble
UHRSTF
/UHRLTF
LSTF/LLTF
ACI
spur
Narrow Band
Partially overlapped
Band
Data

## Slide 4: Potential Scenarios for IM Pilots (2)
OBSS interference
Data Transmission
For Spatial Reuse,
  The intended data transmission would overlap the OBSS interference.
  The transmitter that knows the interference info could utilize the IM pilots to improve detect performance;
  The OBSS interference may be partially or fully band-overlapped.
For Co-SR,
  A sharing AP shall transmit a Trigger frame to initiate concurrent Co-SR transmissions with one other AP within its obtained TXOP BW.
  IM pilots could be configured to improve the link perf if necessary.
Co-SR
SR

## Slide 5: Observations
Equally distributed IM Pilots would provide better performance due to the randomness of interference.
To handle Bluetooth-like narrowband interference, the density of IM Pilots had better be around 1-2 MHz.
It seems there is no restriction for IM pilots utilized with OFDMA system. As the interference could be overlapped with partial or full band, perSTA IM pilots configuration seems more flexible.
It would be much helpful for IM configuration if the transmitter knows the interference information, link SR/Co-SR scenarios.

## Slide 6: IM Pilots
 | normal Pilots | zero-energy Pilots
chanEst/PT impacts | Depends on chanEst perf | Not depends on chanEst perf
Interference power impacts | Worse perf for low power | Not depends on interference power
Noise Est perf | No gain for noiseEst. | NoiseEst gain
Seq design | Need | Not need
From our perspective, zero-energy (null-subcarrier) pilots would be preferred, as it would provide better interference estimation performance, and there is less standardization work for sequence design.

## Slide 7: An Example on IM pilots (20MHz)

## Slide 8: An Example on IM pilots (40MHz)
…

## Slide 9: An Example on IM pilots (80MHz)
…

## Slide 10: Proposal
Almost equally distributed IM Pilots pattern with around 1-2 MHz density, is preferred no matter what the BW is.
zero-energy pilot (null pilot) is supported.
IM pilots could be configured perSTA within OFDMA system.

## Slide 11: References
[1] 11-24-1264r0: Supporting Rx Interference Mitigation in TGbn (Shimi Shilo et al)
Notes: at least one mode of operation capable of improved support, compared to 802.11be, for applications with stringentworst-case latency and jitter requirementscompared to 802.11be // i.e., avoid “worst-case”