## Slide 1: Co-RTWT protection for Multi-AP
Date: 2025-04-01
Authors:

## Slide 2: Abstract
This contribution is a follow-up of 11-24-742, and highlights additional medium access functionalities during a Co-RTWT SP for multi-AP coordination in 802.11bn (AP side).

## Slide 3: Introduction
Multi-AP (MAP) Coordination is one of the key features considered for IEEE 802.11bn.
The Co-RTWT was incorporated in D0.1 (section 37.8.2.4)
  Currently the only existing protection is: “the Co-RTWT coordinated AP as a TXOP holder shall ensure that its TXOP ends before the start time of any active Co-RTWT SP for which protection is extended”.
Recent contributions (e.g. [3]) discuss some degree of protection for the negotiating R-TWT
    Only AP protects
    AP and associated STAs protect (e.g. [2] )
The present contribution falls into the “only AP Protects” category

## Slide 4: Recap of [2]
2 neighbouring APs negotiate with each other a TWT schedule for the coordinated BSS (AP2) that at least partially overlaps with a first TWT schedule set in the coordinating BSS (AP1)
A coordinated AP adjusts the communication policy of its own STAs:
  Option 1: OBSS TWT element forbids the stations of the AP2 BSS to access the medium during the second TWT SPs
  Option 2: OBSS TWT element defines a waiting time for the stations of AP2 BSS to access the medium that is larger than a waiting time for stations of AP1 BSS to access the medium during the first TWT SPs. Typically, STAs perform a CCA (channel sensing) during a larger time. e.g. degraded AIFSN value
  Option 3: OBSS TWT element indicates a temporary operating channel for stations of AP2 BSS to switch to for their communication during the second TWT SP
    E.g. Channel Switch Announcement, DSO, Secondary Channel Access , …

## Slide 5: Recap of [2] (cont.)
An SP was run for [2] on 12/12/2024 :
  Shortly failed: 53 yes / 28 no / 40 abstain
Feedback received:
  Co-RTWT is built on legacy R-TWT
  Co-RTWT was supposed to be an AP feature that has no modification on STA side

## Slide 6: Proposal : protection by APs
Target:
  The coordinating AP keeps priority in accessing the channel during the TWT schedule, thereby protecting it from OBSS interference from the second BSS.
How:
  The coordinating AP waits for less time before decrementing a backoff counter and accessing the channel, compared to the coordinated AP and the coordinated BSS.
AP1
STA11
AP2
STA21
beacon
STA22
First
BSS
Second
BSS
TWT IE
MAP Req
MAP Resp
R-TWT SP
TWT SP
Sensing period for non-AP STAs of coordinated BSS
Beacon
Waiting time for coordinated AP
Waiting time for coordinating AP

## Slide 7: Example recommendations
Minimum time durations are negotiated in between the Requesting and Responding APs, or imposed by the Requesting AP :
  For instance, the parameters in the MAP coordination frame include an AIFSN increment :
    AIFSN for the coordinating AP can be set to 0.
    AIFSN for the coordinated AP can be set to 1.
    AIFSN for coordinated non-AP STA can be set to 2.
  For instance, coordinating AP takes always a strict and shortest waiting time,
    such as the PIFS value
AP adopts different contention behaviours (different sets of parameters) depending on whether it operates during SPs of a TWT schedule or not.
If required, coordinated AP announces a new update of the EDCA Parameter Set for the coordinated BSS.
Notes: PIFS = aSIFSTime + aSlotTime
DIFS = aSIFSTime + 2 * aSlotTime
AIFS[AC] = aSIFSTime + AIFSN[AC] × aSlotTime.
For non-AP STAs : The AIFSN subfield indicates the number of slots after a SIFS a STA defers before either invoking a backoff or starting
a transmission. The minimum value of the AIFSN subfield is 2.

## Slide 8: Advantage
The behaviour of the non-AP stations of the coordinated BSS does not need to be modified, resulting in both:
  legacy stations in the coordinated BSS
  and stations capable of R-TWT operations
  keeping the same behaviour .

## Slide 9: Summary
To reduce OBSS interference among a Multiple AP set, we introduced concepts and solutions for reduced communication activities for stations of neighbouring BSS during the Coordinated R-TWT (Co-RTWT) SPs.
Present document provides protection mechanism by APs.

## Slide 10: Straw Poll
Do you agree to add to the TGbn SFD the following ?
  define additional mechanisms that enable APs of a Multi-AP set to protect the coordinating AP during Co-RTWT SP
  example mechanism is that a coordinating AP keeps priority in accessing the channel during its Co-RTWT SP .

## Slide 11: References
[1] 802.11bn PAR
[2] 11-24/742 OBSS TWT management for MAP, Pascal Viger (Canon)
[3] 11-24/909 R-TWT Announcement in Multi-BSS - Follow up, SunHee Baek (LG)
[4] 11-24/1966 PDT MAC CRTWT