## Slide 1: CSI open issues in CBF
Date: 2025-05-10
Authors:

## Slide 2: Abstract
Coordinated Beamforming (CBF) is already in D0.2 and sounding is an important part to realize CBF. [1]
Two sounding methods (sequential and joint) are defined.
This presentation discusses the CSI open issues in sequential and joint sounding, namely, CSI overhearing and CSI acknowledgement.

## Slide 3: Recap
In sequential sounding,
In joint sounding,
The real transmission
The overhearing transmission
The intended transmission

## Slide 4: Open issues in the current CBF sounding
In Cross-BSS UHR sounding in Seq Sounding and Joint Sounding,
1) CSI overhearing
CSI is technically sent from the STA (e.g. STA1) to its associated AP (e.g. AP1) but needs to be overheard by the unassociated AP (e.g. AP2).
Since the channel between unassociated STA and the AP is “unknown”, CSI overhearing might fail, i.e. AP might not be able to overhear the CSI from unassociated STA.

## Slide 5: Open issues in the current CBF sounding
2) CSI Acknowledgement [2, 3, 4, 5]
One AP runs the sequence but can’t tell if the other AP overheard the CSI.
If other AP misses the CSI, the sounding ends with bad CSI and CBF degrades.
See below for seq sounding (same goes for joint sounding too)
AP1 does not know whether AP2 received the CSI correctly.
AP2 does not know whether AP1 received the CSI correctly.

## Slide 6: Proposal
CSI overhearing requires CSI acknowledgement. Some possible options might be:
Option 1) CSI Status Req(optional)/Resp is exchanged between APs (seq sounding shown, joint sounding similar)
aa
TBD when CSI Status Req (optional)/Resp is sent such as:
after each cross-BSS/joint sounding during sounding (advantage: immediate feedback) or
at the end of sounding (advantage: lower overhead) or
after the sounding (advantage: faster sounding), maybe part of a frame (e.g. CBF invite/response) in CBF transmission phase

## Slide 7: Proposal
CSI overhearing requires CSI acknowledgement. Some possible options might be:
Option 2) Simple ACK is exchanged between APs (seq sounding shown, joint sounding similar)
advantage: immediate feedback & relatively short overhead
Note that AP not receiving ACK does not necessarily force re-sound (i.e. ACK is informative)

## Slide 8: Proposal
CSI overhearing requires CSI acknowledgement. Some possible options might be:
Option 3 (maybe)) Existing frame during sounding such as NPDA is used (seq sounding shown, joint sounding similar)
advantage: no extra frame is needed Note: This requires strict order of sequences as shown as follows (CSI ACK in NDPA in EHT TB sounding after cross BSS sounding): Note: This doesn’t seem to work for joint sounding.
CSI ACK
CSI ACK
CSI ACK

## Slide 9: Summary
CSI open issues (CSI overhearing and CSI Acknowledgement) are discussed for UHR sounding in CBF
Some methods for CSI Acknowledgement for CSI overhearing are discussed.

## Slide 10: Straw Poll
Do you agree that 802.11bn will define a method for a CBF participating AP (AP1) to confirm to another CBF participating AP (AP2), the reception or lack of reception of cross-BSS CSI from a concluded joint sounding or cross-BSS sounding step of sequential sounding corresponding to CBF clients of that AP (AP2)?
  Yes
  No
  Abstain

## Slide 11: References
[1] IEEE P802.11bn/D0.2
[2] https://mentor.ieee.org/802.11/dcn/25/11-25-0553-00-00bn-cross-bss-csi-feedback-for-co-bf.pptx
[3] https://mentor.ieee.org/802.11/dcn/25/11-25-0247-01-00bn-m-ap-cobf-sounding-sequence.pptx
[4] https://mentor.ieee.org/802.11/dcn/25/11-25-0379-01-00bn-considerations-on-uhr-sounding-operation.pptx
[5] https://mentor.ieee.org/802.11/dcn/25/11-25-0362-00-00bn-improvement-on-co-bf-sounding.pptx