## Slide 1: TXOP Transfer in Co-RTWT
Date: 2025-09-10
Authors:
Name | Affiliations | Address | Phone | Email
Yunbo Li | Huawei | Shenzhen, China |  | liyunbo@Huawei.com
Yuchen Guo |  |  |  | 
Guogang Huang |  |  |  | 
Yue Zhao |  |  |  | 
Maolin Zhang |  |  |  | 
Zhenpeng Shi |  |  |  | 
Ming Gan |  |  |  | 
Notes: September 2012

## Slide 2: Background
R-TWT is introduced in TGbe for transmission of latency sensitive traffic;
AP and associated STA will terminate TXOP before the start of R-TWT SP;
R-TWT is extend to MAPC, and called Co-RTWT, in which a Co-RTWT responding AP will terminate the TXOP before the start time of Co-RTWT SP from a Co-RTWT requesting AP;
Below figure illustrates the operation of Co-RTWT.

## Slide 3: Discussion
A Co-RTWT responding AP may have its own R-TWT SP, during which Co-RTWT responding AP will communicate latency sensitive traffic with its associated STAs;
If the start time of SP1 fall into the SP2, whether responding AP should terminate its own TXOP before the start time of SP1?
If responding AP terminate its own TXOP will cause below issue
  Issue 1: increase responding AP’s delay
  Issue 2: low efficiency due to cut responding AP’s TXOP into two part, and also introduce contention overhead

## Slide 4: Proposed Solution 1
If the start time of Co-RTWT SP fall into its own R-TWT SP, a STA can continue current TXOP at the start time of Co-RTWT SP, otherwise, the STA will terminate its current TXOP;
The solution apply to both Co-RTWT responding AP and its associated STA;
Below is an example of proposed solution 1.
  When Co-RTWT SP11 doesn’t overlap with any R-TWT of responding AP, responding AP will terminate its TXOP before start time of SP11
  When Co-RTWT SP12 overlapped with R-TWT SP2 of responding AP, responding AP can continue current TXOP at the start of SP12

## Slide 5: Proposed Solution 2
The proposed solution 1 is friend to responding AP, but increase the delay of requesting AP;
A compensation solution is responding AP guarantee to transfer part of the remaining TXOP to requesting AP if responding AP doesn’t terminate TXOP before the start time of Co-RTWT SP;
Below is an example that responding AP obtained a TXOP within its own RTWT SP2, and doesn’t terminate TXOP before start time of Co-RTWT SP1, as a compensation, responding AP share part of TXOP to requesting AP through C-TDMA procedure.

## Slide 6: Summary
Co-RTWT responding AP needs to terminate TXOP before the start time of Co-RTWT SP;
The termination of TXOP will affect the latency of responding AP’s traffic if the it is within responding AP’s R-TWT SP;
Two solutions are proposed:
  Opt 1: responding AP and its associated STA will continue current TXOP if the start time of Co-RTWT SP fall into its own R-TWT SP
  Opt 2: responding AP may continue current TXOP at the start time of Co-RTWT SP, as a compensation, responding AP will transfer part of TXOP to requesting AP

## Slide 7: SP1
Do you agree that the Co-RTWT responding AP and its associated STAs will continue current TXOP at the start time of a Co-RTWT SP if the start time of the Co-RTWT SP falls into Co-RTWT responding AP’s R-TWT SP?