## Slide 1: Extended transition mode for DPS AP
Date: 2025-04-30
Authors:
Name | Affiliations | Address | Phone | Email
Yunbo Li | Huawei | Shenzhen, China |  | liyunbo@Huawei.com
Yuchen Guo |  |  |  | 
Guogang Huang |  |  |  | 
Yue Zhao |  |  |  | 
Maolin Zhang |  |  |  | 
Zhenpeng Shi |  |  |  | 
Ming Gan |  |  |  | 
Notes: September 2012

## Slide 2: Background
When an AP sending Data to a EMLSR STA, the EMLSR STA will transition back to the listen mode after the end of frame exchanges. If the AP intend to transmit to the EMLSR STA in the following TXOP, the transmission need to be deferred until the transition period expires;
Similar situations happen in DL transmission of DSP, DSO operation;
For uplink transmission, similar situation happens and only happens when associated mobile AP support DPS.

## Slide 3: Motivation
If STA1 communicate with DPS mobile AP in previous TXOP, STA1 knows the AP’s transition period, and the STA1 can defer the UL transmission until transition period expires, but it will add the complexity at STA1 side
If STA2 doesn’t involve into the communication with DPS mobile AP in previous TXOP, STA2 need to monitor the communication in previous TXOP in order to determine the transition period of the mobile AP. It will less power efficiency for STA2, and also add the complexity at STA2 side;
If STA3 is in doze state, or interfered by OBSS transmission during previous TXOP, STA3 will hard to know the transition period of the mobile AP. STA3 can not respect mobile AP’s transition period
We need a mechanism to
  Solve the issue that some non-AP STA can not identify the transition back period of DPS AP
  simplify the implement complexity at non-AP STA side.

## Slide 4: Example of Switch Back
Below is an example of switch back of DPS AP;
During the switch back delay period, another non-AP STA may finished backoff and initiate transmission to DPS, and will definitely failed due to the unavailability at DPS AP side;
The another non-AP STA will hard to know the reason of failures

## Slide 5: Proposed Solution – AP side
AP broadcast it is in extended transition mode, in which the non-AP that intend to transmit to the AP doesn’t need to consider the switch back delay from high capability (HC) mode to low capability (LC) mode;
  The AP may initiate the switch back during the transmission period of an OBSS PPDU; or,
  The AP may set a longer TXOP to protect the switch back delay; or,
  The AP may choose an estimated period that non-AP with low probability to initiate UL transmission based on internal algorithm.
The non-AP will treat switch back delay of AP as 0, so no modification about channel access procedure, which will simplify the implementation;

## Slide 6: Proposed Solution – non-AP side
An non-AP STA may indicate whether it can respect the switch back delay of the associated AP from HC mode to LC mode
  If the non-AP STA can respect the switch back delay, it will defer the UL transmission after the switch back delay of the AP
  If the non-AP STA can not respect the switch back delay, it may initiate UL transmission during the switch back delay period of the AP. The non-AP may or may not count the failure during switch back delay period into link adaption;
The AP can use the indication from associated non-AP STAs as reference to decide whether to enter extended transition mode
  If all associated non-AP STAs can respect the switch back delay of the AP, the AP can quit extended transition mode to save more power
  If some associated non-AP STAs can not respect the switch back delay, the AP may enter extended transition mode to help non-AP STAs to have better performance.

## Slide 7: Summary
During the switch back period of DPS AP, some non-AP STA may transmit frame to the DPS AP;
It is hard for some non-AP STAs to know the exact location of swith back period of DPS AP; and
It significantly add the complexity at non-AP STA side;
We propose AP can announce an extended transition mode to release the concern from non-AP STA side.