## Slide 1: DPS ICF Indication
Date: 2025-02-20
Authors:
Name | Affiliations | Address | Phone | email
Jason Yuchen Guo | Huawei Technologies |  |  | guoyuchen@huawei.com
Yunbo Li |  |  |  | 
Guogang Huang |  |  |  | 
Ming Gan |  |  |  | 
Yue Zhao |  |  |  | 
Maolin Zhang |  |  |  | 

## Slide 2: Introduction
The Dynamic Power Save (DPS) mode enables a non-AP STA to transition from a lower capability (LC) mode to a higher capability (HC) mode upon receiving an initial control frame (ICF).
The frame choice of ICF for DPS could be:
  RTS
  MU-RTS
  BSRP
MU-RTS or BSRP should be used when IFCS is required by the non-AP STA, otherwise, RTS can also be used.

## Slide 3: Introduction
In the DPS mode, a non-AP STA can enter the mode with ICF required equal to 0, which means that the AP can transmit data frame to the non-AP STA without transmitting an ICF, as long as the transmission parameters are supported by the non-AP STA under the LC mode.
However, before transmitting data frame, the AP may want to transmit control frame (which is not a DPS-ICF) to the non-AP STA for other purposes, e.g.,
  Transmitting RTS/MU-RTS for channel protection
  Transmitting BSRP to solicit buffer status
  Transmitting BSRP to solicit unavailability information (if the non-AP STA is in DUO mode)
After receiving the above control frames, the non-AP STA may think the received control frame is a DPS-ICF, and transitions to the HC mode, resulting in a waste of power
Motivation: we need a way to tell the receiver whether the current control frame is a DPS-ICF or not.

## Slide 4: Proposal
If padding is needed by the non-AP STA, MU-RTS or BSRP will be used as the DPS-ICF, we can add a field (e.g., 1 bit) in the MU-RTS or BSRP to indicate whether the current MU-RTS or BSRP is a DPS-ICF or not
  In other words, the added field is used to indicate whether the receiver need to switch to HC mode
If padding is not needed by the non-AP STA, then RTS may also be used as the DPS-ICF. Since there’s no reserved field in the RTS, we may need to reuse existing signaling (e.g., BW) to determine whether the current RTS is a DPS-ICF or not
The non-AP STA will only switch to HC mode if the received control frame is a DPS-ICF

## Slide 5: Conclusion
We consider the case that a DPS enabled STA may not know whether a received control frame is a DPS-ICF or not
We propose to add some signaling in the control frame to indicate whether the current control is a DPS ICF or not
A new field can be defined in MU-RTS and BSRP
Existing signaling in the RTS can be used as a DPS-ICF indication

## Slide 6: SP
Do you support to include in the 11bn SFD:
  MU-RTS and BSRP shall carry a field to indicate whether it is a DPS-ICF