## Slide 1: AMP frames – follow up
Date: 2025-07-07
Authors:

## Slide 2: Introduction
We discussed the general AMP frame format [1, 2, 3]
  Following similar formats and design philosophies to WUR frames
Three AMP frames have already been agreed:
  AMP Trigger frame, AMP Ack frame, and AMP Wake-Up frame
    See next slide for a summary of currently approved concepts

## Slide 3: AMP PPDU
AMP frame needs the following fields:
  A Frame Control to signal (aim at 8 bits long at most, same as WUR):
    AMP Type: Indicates the type of AMP frame (e.g., Trigger, Ack, etc.)
    Protected: Indicates whether the FCS field, if present, carries a CRC or MIC
    Other fields if needed are TBD
  IDs - target similar principles as 11ba, with appropriate considerations for AMP:
    One ID for the transmitter and/or one identifier for individual recipient(s), or group of recipients
  Frame Body can be optionally present
    This can be enabled if we are interested in variable-length PPDUs
      We defined similar PPDUs in WUR, albeit optional
  FCS, is optionally present and contains the CRC or MIC
    For WUR the FCS field was always present and was 16 bits
 | Optional Energizer Signal | PHY Preamble | MAC Header | Frame Body | FCS

## Slide 4: Defined AMP frames: Summary
AMP Trigger frame
  M1: 802.11bp defines an AMP Trigger frame that an AP transmits to solicit UL AMP PPDU(s) from one or more 802.11bp clients and may carry the following content
    Transmitter ID, Receiver ID(s), FCS, Other parameters TBD.
  M2: When the AP solicits UL AMP PPDUs from 802.11bp clients using a slot-based procedure, the AMP Trigger frame shall carry the following parameters
    Number of slots for UL PPDU transmissions in that TXOP
    Other parameters TBD.
  M3: AMP trigger frame may indicate parameters for a slot-based procedure of time slots to AMP non-AP STA(s).
    The exact parameters are TBD.
AMP Ack frame
  802.11bp defines an AMP Ack frame that an AMP AP transmits to acknowledge the received UL AMP frame(s).
AMP Wake Up frame:
  802.11bp defines an AMP Wake-Up frame, which an AMP AP transmits to AMP-enabled non-AP STA(s) to indicate that the AP intends to exchange non-AMP frames with the non-AP STA
    The expectation is to reuse WUR frame format for the AMP Wake-Up frame and to carry it in an AMP PPDU

## Slide 5: AMP frames: Proposals
AMP frames inherit WUR frame structure
  Frame Control contains Type, Protected, Frame Body Present, Length/Miscellaneous
    Type field will identify these AMP frame types (Trigger, Wake-Up, Ack, RFID, AMP Data, etc.).
ID field contains an identifier for the AMP frame
  Transmitter ID, Group ID, RX ID, etc.
    WUR frames use 12 bits IDs, however, in TGbp, 16-bit identifiers are also being discussed
    Need to converge on the size of these identifiers
Type Dependent Control will contain type dependent information
  WUR frames use 12 bits TD Control (suggest using the same size as the ID)
    Since for certain frame types the TD Control carries another identifier
Frame Body is optionally present in AMP frames
  Frame Body, if present is of variable length and maxes out at 16/64?? octets for WUR frames
  For AMP frames it appears there might be cases (albeit rare) that require larger payloads (e.g., 64 octets for RFID case)
    For these, we could either expand the length field size or increase the granularity or enable fragmentation.
FCS size and contents are inherited from WUR frame format
  Presence of Embedded BSSID needs to account for the context of these AMP frames being generated (prior to or post assoc.)
MAC Header | Frame Body | FCS
 | Frame Control | ID | Type Dependent Control
Bits | 8 | X | X

## Slide 6: AMP Trigger: Proposals
AMP Trigger is sent to one or more AMP STAs to solicit an AMP PPDU
  ID field contains the transmitter ID
  Type Dependent Control/Frame Body field contains info. for receiving AMP STAs
    Possibly a list of receiver identifiers,
    Number of slots for UL PPDU TXs in that TXOP, length of the UL AMP PPDUs, etc.
MAC Header | Frame Body | FCS
 | Frame Control | ID | Type Dependent Control
Bits | 8 | 12 (or 16) | 12 (or 16)

## Slide 7: AMP Ack frame format
AMP Ack frame is sent by an AMP STA in response to
  An AMP Trigger frame or another AMP frame that requires an acknowledgment
    Expectation is that the AMP Ack is sent an AMP SIFS after the soliciting AMP PPDU
  Needs to identify the transmitter (TX ID) (not essential) and the recipient (RX ID)
    The TX ID identifies the AMP AP (propose to not include it, like baseline Ack)
    The RX ID identifies the AMP STA (12 bits or expand to 16 bits if needed)
Proposal for AMP Ack frame (6 octets@250kbps~192us of PSDU airtime):
  ID field is set to the identifier of the intended receiver
    E.g., copy from the TX ID of the soliciting AMP PPDU
  Type Dependend Control field can be used to carry signaling in the AMP Ack frame
  Frame Body is not present in an AMP Ack frame
  FCS field is set as for WUR frames
    Note: If AMP Ack frames are allowed prior to association then Embedded BSSID may not be present
  Note: we can save another 2 octets by not including ID and TD Control (reducing PSDU airtime to 128 us)
    In this case RX ID can replace the Embedded BSSID in the FCS computation
MAC Header | Frame Body | FCS
 | Frame Control | ID | Type Dependent Control
Bits | 8 | 12 (or 16) | 12 (or 8)

## Slide 8: Summary
We discuss additional details for AMP frame format
  Defining fields and contents of AMP Trigger and AMP Ack