## Slide 1: MAC Comparison for Active AMP Operation
Date: 2025-05-12
Authors:

## Slide 2: Abstract
We compare two approaches to the AMP MAC for active AMP operation, namely without and with synchronization / duty cycle.

## Slide 3: Scope: Active Transmitter + Energy Harvesting
Limitations:
  How much power is available?
  How much power is required?
  Duty cycle, range, complexity
Assumptions (based on [1, 2, 3]):
  Three modes of operation:
    Active, Pactive = 1mW
    Listen, Plisten=10µW
    Sleep, Psleep=100nW
  Total efficiency harvesting to consumption: 10%

## Slide 4: AMP STA without Synchronization
Charge until Vhigh reached (linear increase here for simplicity)
Attempt to communicate with AMP AP
  Listen for AMP Trigger Frame
Communicate with AMP AP
  Reply if queried / execute command / report status (“active phase”)
t
Charge
Vhigh
Vlow
1
2
3
1
2
3
1
2
3
1
2
AP
3

## Slide 5: AMP STA without Synchronization
Assume 1ms active phase
Trivial:
  More (average) charge power  shorter minimum energy harvest duration
  Longer listen duration requires  longer minimum energy harvest duration
Considering limited charge powers [1]:
  Harvest durations > 10s
  Listen duration ~100ms
AMP AP sends AMP Trigger Frames in regular intervals
  Interval is larger than listening duration: AMP STA will spend energy on listening without receiving any frame (see [5] for meeting probabilities).
  OR
  Interval is equal or shorter than listening duration: AMP STA will always receive an AMP AP frame. However, most (here: 99%) AMP Trigger Frames are sent while AMP STA is sleeping.

## Slide 6: AMP STA with Synchronization
AMP STA has an ultra-low-power, high-drift clock [4]
  Consumption: 500pW
  Clock drift: 1%
AMP STA and AMP AP are synchronized to a duty-cycle
  Sleep and harvest energy until expected AMP Trigger Frame time
  Listen for AMP Trigger Frame
  Receive AMP Trigger Frame & re-synchronize to compensate clock drift
  Communicate with AMP AP (if needed)
t
Charge
Vhigh
Vlow
1
1
1
2
3
2
AP
3

## Slide 7: AMP STA with Synchronization
Assume
  1ms active phase (as before)
  Vhigh = 1.5V, Vlow=1.25V
Low AMP Trigger Frame interval (<1s)
  Requires sufficient charge power to harvest energy for active phase
  Clock drift not relevant
  Low required charge capacity
High AMP Trigger Frame interval (>100s)
  Requires sufficient charge power to harvest energy for listening phase (1% of interval)
  Charge power for active phase not relevant
  High required capacity
Sweet spot at 1s ... 100s
  Significantly less often than without synchronization
What about very-low duty cycle (e.g., 12h) applications?
  Compensation of clock drift (432s) required
  Better to support regular re-sync (e.g., every 100s)
<1s
>100s

## Slide 8: Comparison
Operation without synchronization
  AMP AP must often send AMP frames
    In the order of legacy IEEE 802.11 beacon frames
    The majority will be unanswered  high overhead
    May raise concerns on spectrum usage
Operation with synchronization
  AMP AP sends AMP frames synchronized to the duty cycle
    Tuned to average charge power
    Cannot be too often to enable sufficient harvesting
    Cannot be too seldom to limit absolute clock drift
    Efficient spectrum usage

## Slide 9: Conclusions
Synchronized operation should be preferred, if possible, to limit the overhead & unnecessary spectrum usage.
  Very low-duty cycle applications require frequent re-synchronization. There should be a short & efficient re-synchronize frame to support this.
However, phases may be required to reach synchronization
  Solution under the current restrictions: at “some point” the AMP AP sends Trigger Frames with a high frequency
  Interval equal to the expected AMP STA listen duration to support synchronization of new AMP STAs
  Then, it can relax and reduce the Trigger Frame interval as all AMP STAs should be synchronized

## Slide 10: Strawpoll
Do you agree that AMP shall have a mode of operation to reach synchronization that is more spectrum-efficient than high-rate transmission of trigger frames?
Yes
No
Abstain

## Slide 11: References
“Technical Report on support of AMP IoT devices in WLAN,” Ambient Power Communication Study Group, IEEE 802.11-23/2203r1,
“Wireless Power Transmission and Energy Harvesting for IoT Applications,” B. Yang (Huawei), IEEE 802.11-22/1294r1
“SP Timing Synchronization with AMP Beacon,” I. Bajaj (Huawei), IEEE 802.11-25/0285r1
“Discussion on ultra-low power timing clock,” Weijie Xu (OPPO) et. al., IEEE 802.11-24/1475r3
“Active AMP STA Polling Requirements,” S. Max (Ericsson) et. al., IEEE 802.11-25/0052r0