## Slide 1: .11bp Frame Formats for Active TX AMP STA
Date: 2025-05-06
Authors:

## Slide 2: Abstract
This presentation discusses approaches to separate access to Active TX AMP STA. The rationale and solution for individual delivery are presented.

## Slide 3: Unique ID of Active TX AMP STA
It may be necessary to have individual delivery to the Active TX AMP STA (AAMP STA). For example, to measure the temperature at a specific point or to block a specific AAMP STA using a remote command.
Each AAMP STA may or may not have a Unique AAMP STA ID (UID)
  The UID uniquely identifies an AAMP STA among other AAMP STAs at the Application/Cloud layer
  To maintain confidentiality/privacy, this UID or another persistent identifier is secret and not exposed to the network
  The UID may be encrypted when communicated
  The UID may be delivered to the cloud/application to identify the AAMP STA
  For example, the unique item identifier (UII) may be seen as such a UID
  The UID and use of it are outside of the standard scope

## Slide 4: Individual delivery to AAMP STA
There are several considerations regarding AAMP STA access to the network
  Individual delivery to the AAMP STA is used by the cloud/application
  If the UID or another persistent identifier is secret and not disclosed to the network, it cannot be used by the network to identify the AAMP STA that requires delivery
  The AAMP STA may not support network access, it does not support TCP/IP layer protocols
  The AAMP STA may not support association procedures to communicate with the AP STA
  The individual access to the AAMP STA shall not congest the network, this access should not generate too many redundant messages due to the hidden UID of the AAMP STA

## Slide 5: Broadcast access for the Individual delivery
Individual delivery to/from AAMP STA may use broadcast or/and individual addressing to access the network
  Individual DL delivery by broadcast access: the DL message is delivered to each AAMP STA, and it uses the UID to retrieve or discard the message.
  In the UL direction w/o unicast AAMP STA identification, multiple copies of the message are delivered if there are multiple routes through which the message is delivered to the application, and only the application can detect the redundant copies of the message
The lack of individual identification for network access results in redundant copies in the network. This phenomenon is especially significant in DL, where thousands of redundant network messages may be created for delivery to a single AAMP STA.

## Slide 6: Individual Access to AAMP STA (exemplary approach)
AMP AP
AAMP STA
Un-Associated mode
Associated mode
Cloud/Application
The AAMP STA communicates with the AMP AP, which communicates with the AP STA to provide access to the distribution system
The AAMP STA may or may not use local ID to communicate with the AMP AP.
The AAMP STA local ID may be temporal ID (TID)
The AAMP STA may communicate with the AMP AP w/o association
The AAMP STA may not support TCP/IP
The AMP AP may be a network endpoint. It supports the TCP/IP layers of the networking protocols
The AMP AP may be associated with the AP STA
The cloud/application can deliver data individually to the AAMP STA by establishing an internet connection with the AMP AP. The AMP AP accesses the AAMP using broadcast access or by addressing the AAMP STA by TID.

## Slide 7: Individual Access to AAMP STA (exemplary Infrastructure)
An AMP AP may be associated with an AP STA and serve as a TCP/IP network endpoint
  The AMP AP is identified by its IP address on the Internet and by its MAC address in the BSS.
An AAMP AP may communicate with one or more AAMP STAs
An AAMP STA may communicate with one or more AMP APs

## Slide 8: Individual Access to AAMP STA; Broadcast vs. TID (DL exemplary scenario)
Once the AMP AP is connected to the network and the AAMP STA is connected to the AMP AP, the IP address of the AMP AP and the UID of the AAMP STA are sent to the cloud/application. This establishes a relationship between the AAMP STA and the AMP AP with which the AAMP STA communicates, so that a message destined for a specific AAMP STA, can be delivered to the appropriate AMP AP.
To deliver a message to the specific AAMP STA, two options can be considered: broadcasting and using TID.
  Broadcasting means that a message intended for one AAMP STA is delivered to multiple AAMP STAs. The message contains an encrypted UID. Each AAMP STA must receive and decrypt the message, and only the station that matches the UID can use it, other stations must discard the message as irrelevant and useless.
  The TID is temporarily assigned to the AAMP STA and transmitted to the cloud/application along with the encrypted UID and the IP address of the AMP AP, so it can be used to individually access the station. In this way, the AMP AP delivers the message only to the desired station.
Both approaches preserve the privacy of the AAMP STA, since the UID is not revealed to the network and the TID is temporary and does not compromise the AAMP STA privacy

## Slide 9: Individual Access to AAMP STA; Broadcast vs. TID comparison
 | Pros | Cons
Broadcast | Easy access to the channel: no acknowledgment, no retransmission | Each AAMP STA must receive and decrypt the message. Each station spends energy to receive and decrypt, so all but one station is wasting energy.
 |  | Retransmission is problematic because there is no immediate acknowledgement, hence the low reliability
TID | Reliable delivery supported by acknowledgement and retransmission | A procedure for generating and assigning TIDs is required.
 | Efficient energy consumption due to early detection of frames addressed to other stations. There is no need to receive the entire frame and decrypt it if it is addressed to other stations | 
 | Targeted network transmissions, no redundancy required | 

## Slide 10: Summary
Suggest to include the AAMP STA TID field in the TGbp frame format
The AAMP STA TID field may be present in the DL format as Receiver Address and in the UL frame format as Transmitter Address.
The TID field size and assignment TBD

## Slide 11: SP
Do you agree to include the following text in the SFD Frame Formats section: "The AAMP STA TID may be present in the DL .11bp frame format as the Receiver Address field and in the UL .11bp frame format as the Transmitter Address field. The size of the TID and its assignment TBD”?

## Slide 12: References