## Slide 1: Energy-Level Status Reporting for AMP Devices – Follow-Up
Date: 2025-05-14
Authors:
Name | Affiliations | Address | Phone | Email
Mahmoud Hasabelnaby | Huawei |  |  | Mahmoud.Hasabelnaby@huawei.com
Osama Aboul-Magd |  |  |  | 
Junghoon Suh |  |  |  | 
Yan Xin |  |  |  | 
Abdallah Hussein |  |  |  | 
Notes: September 2012

## Slide 2: Problem Statement
AP cannot make informed decisions about wireless power transfer (WPT) management, channel access scheduling and resource allocation due to a lack of knowledge regarding the AMP STA's current energy level.
This can lead to the following problems:
  Inefficient Wireless Power Transfer scheduling: Without visibility into the AMP STA’s energy level, the AP may unnecessarily initiate wireless power transfer sessions or trigger the energizer to activate, while failing to prioritize AMP STAs with critical energy needs.
  Poor Scheduling Decisions: Without energy-level information, the AP cannot optimize transmission scheduling. It might prioritize AMP STAs that cannot complete the communication due to their low energy, while other AMP STAs with sufficient energy might be overlooked. This leads to suboptimal scheduling and inefficient resource use, as those resources remain unused
  Potential Data Loss: The AP might transmit a DL transmission to a low/no energy AMP STA, leading to potential packet loss and transmission failure.

## Slide 3: Motivation
The aforementioned limitations highlight the critical need for a robust mechanism for AMP STAs to report their energy state to the associated AP.
According to Motion #36 [1], IEEE 802.11bp defines a mechanism that allows an AMP non-AP STA to report its energy harvesting and power related information to AMP AP STA.
  The parameters that are included in the report and how to report such information is TBD.
This contribution introduces a lightweight Energy-Level Status Reporting (ELSR) mechanism that enables AMP STAs to report their current energy state to the AP with minimal energy consumption.

## Slide 4: Proposal: Piggybacking ELSR with AMP non-AP STA’s Uplink Transmission
AMP STAs may send a dedicated Energy-Level Status report to their associated AP upon request. However, this dedicated Energy-Level Status report transmission consumes energy, which is a concern for energy-constrained AMP STAs [2-5].
To minimize energy usage for the Energy-Level Status report, the AMP STA can embed its energy-level status (e.g., one-bit indication) within regular uplink transmissions (e.g., data PPDUs, TB-PPDUs, etc.) to the associated AP.
  a value of 0 signifies an high or non-critical energy level, and;
  a value of 1 indicates a low or critical energy level.
This eliminates the need for standalone Energy-Level Status reporting frames, reducing control overhead and conserving energy, thereby extending the operational lifespan of AMP STAs.

## Slide 5: Proposal: Piggybacking ELSR with AMP non-AP STA’s Uplink Transmission
Following this, the AP can track the energy status of AMP STAs more frequently as energy updates are included in regular AMP STA’s uplink transmissions.
This allows the AP to make timely and informed decisions about WPT scheduling and resource allocation.
  For instance, if the energy-level status value embedded in the AMP STA’s uplink transmission indicates a critical energy level, the AP should prioritize WPT to that AMP STA—either by adjusting the WPT schedule or by triggering the corresponding energizer to transmit energy signals targeted to that AMP STA.

## Slide 6: Conclusion
In this contribution, we introduced a lightweight Energy-Level Status Reporting (ELSR) mechanism that enables AMP STAs to report their current energy state to the AP with minimal energy consumption.
AMP STA can embed its energy-level status (e.g., one-bit indication) within regular uplink transmissions to the AP.
This allows the AP to make timely and informed decisions about WPT scheduling and resource allocation.

## Slide 7: References
[1] 802.11-24/1322r6, “TGbp Motion Dock”.
[2] 802.11-24/1381r0, “AMP Device Power Status”.
[3] 802.11-24/1524r2, “Follow-up on the AMP WPT protocol”.
[4] 802.11-24/1539r0, “Energy-Level Status Reporting for AMP Devices”.
[5] 802.11-24/1561r1, “AMP Power Budget Negotiation”.

## Slide 8: Straw Poll
Do you agree to add the following to the 11bp SFD:
  AMP STA shall embed its energy-level status within its uplink transmissions to the AP.
    1-bit energy-level status shall be piggybacked at a TBD location in the AMP STA’s uplink frame.
Y/N/A