## Slide 1: Optimize Mode Transitions in DPS Operation
Date: 2025-05-05
Authors:
Name | Affiliations | Address | Phone | email
Sam Shi | OPPO |  |  | sam.shi@oppo.com
Chuanfeng He |  |  |  | 
Chaoming Luo |  |  |  | 
Liuming Lu |  |  |  | 
Ning Gao |  |  |  | 
Yapu Li |  |  |  | 
Liangxiao Xin |  |  |  | 

## Slide 2: Introduction
The UHR SG agreed to define a mechanism to reduce power consumption for Access Points (APs) (including mobile APs) and improved Peer-to-Peer (P2P) operation in UHR proposed PAR.
A motion was approved stating that:
  TGbn defines a power save mode for a STA that is a UHR Mobile AP or a UHR non-AP STA wherein the STA may transition from a lower capability mode to a higher capability mode upon reception of an initial control frame.
Discussions on AP power save (PS) and dynamic power save (DPS) have focused on several key aspects [1-9]
  Lower capability mode (e.g., 20 MHz BW, one SS, limited data rates, PPDU format)
  Higher capability mode (e.g., 40+ MHz BW, NSS and MCSs)
  Design and selection of Initial Control Frame (ICF) and Initial Control Response (ICR)
  Coexistence with other features, such as MLO and NPCA
  Protection mechanism of higher capability mode
  etc.

## Slide 3: Background
Several contributions have highlighted that transitioning between lower and higher capability mode, especially involving channel bandwidth change, can be time-consuming, at hundreds of microseconds [10].
  As shown in the figure below, it is not optimal for a DPS non-AP STA to transition to a lower capability mode when additional DL data at the AP is pending for transmission.
    A DPS assisting AP has DL data for a DPS non-AP STA.
    The AP uses ICF to bring the STA to higher capability mode but only transmits part of the data e.g. due to a limited TXOP duration.
    The STA then transitions back to lower capability mode while waiting for next TXOP.
    The AP again uses ICF to bring the STA to higher capability mode for data transmission.
    The above steps may repeat till all data complete transmission
    This results in redundant mode transitions, which introduces unnecessary latency and inefficiency. Also, the intended power saving is not significant as frequent mode switch consumes extra power.

## Slide 4: Background
Previous studies [11] have proposed higher capability protection mechanisms in DPS to reduce frequent capability state transitions and avoid unnecessary time, padding, and power overhead before the completion of data transmission.
  This approach is promising by providing a buffer period before a STA transitions back to lower capability mode.
  A protection timer is introduced allowing a DPS STA to remain in higher capability mode.
  The timer value is explicitly signaled in each ICF/ICR and can be dynamically adjusted as needed.
The protection timer-based solution requires the timer field to be present in every ICF and ICR.
Consequently, it mandates ICF and ICR exchange for every transmission, even when the STA is already operating in higher capability mode, potentially introducing signaling overhead.

## Slide 5: Proposal 1 – explicit data indicator (DL)
Proposal 1: Use of explicit data indicator for sustaining higher capability mode
Example scenario: downlink (DL) data from a DPS assisting AP to a DPS non-AP STA
  The DPS assisting AP uses ICF to bring the DPS non-AP STA to higher capability mode.
  The AP uses a data indicator to inform the STA that additional DL data is pending.
  This indicator can be defined and transferred through various mechanisms: further methods can be discussed. In this example, the indicator is embedded in the DL data PPDU.
  Upon receiving the indicator with value of '1', the STA remains in higher capability mode, avoiding unnecessary mode transitions are prevented.

## Slide 6: Proposal 1 – explicit data indicator (UL)
Example scenario: uplink (UL) data from a DPS assisting non-AP STA to a DPS mobile AP
  The DPS assisting non-AP STA uses ICF to bring the DPS mobile AP to higher capability mode.
  The STA uses a data indicator to inform the mobile AP that additional UL data is pending.
  Like the DL case, details of the indicator can be further defined. In this example, the indicator is embedded in the UL data PPDU.
  Upon receiving the indicator with value of '1', the mobile AP remains in higher capability mode avoiding unnecessary mode transitions.
  In a light traffic channel environment, where APs can acquire TXOPs in quick succession, staying in higher capability mode longer is more efficient in both latency and power consumption.

## Slide 7: Proposal 2 – guard timer
In some cases, after a data indicator is set to 1, no additional data arrives or a TXOP is not acquired. To prevent the AP or STA from remaining in higher capability mode unnecessarily, a guard timer mechanism is proposed.
Proposal 2: use of guard timer to avoid unnecessary prolonged higher capability mode. This mechanism is only applicable when data indicator is set to 1.
The timer is managed in a lightweight manner:
  It does not need to be configured in ICF/ICR.
  It can be configured during DPS preparation phase or at other occasions (TBD).
If the guard timer expires, the device transitions back to lower capability mode.
The exact rules for when to start, restart, or stop the timer can be further defined.

## Slide 8: Summary
It is important to keep a non-AP STA or a mobile AP in higher capability mode when additional data is pending to avoid unnecessary delays caused by repeated mode transitions.
The previously proposed protection timer is a promising solution [11] , but it may require further refinement and optimization.
Proposal 1: use of explicit data indicator for sustaining higher capability mode.
Proposal 2: use of guard timer to avoid unnecessary prolonged higher capability mode. This mechanism is only applicable when data indicator is set to 1.

## Slide 9: References
[1] 11-23/10r0, “Considerations for enabling AP power save”, Alfred Asterjadhi et al.
[2] 11-23/15r0, “AP MLD power management”, Liwen Chu, et al.
[3] 11-23/225r0, “Considering unscheduled AP power save”, Guogang Huang et al.
[4] 11-23/244r1, “AP Power Save PAR addition proposal”, Amelia Andersdotter, et al.
[5] 11-23/1875r1, “Power save proposal for non-AP/mobile AP”, Sindhu Verma et al.
[6] 11-23/1965r2, “Dynamic Power Save - follow up”, George Cherian et al.
[7] 11-23/2003r1, “Client-power-save”, Laurent Cariou et al.
[8] 11-24/451r0, “AP state transitions in DPS mode”, Vishnu V. Ratnam et al.
[9] 11-24/833r0, “Dynamic Power Saving for AP”, Geonhwan Kim et al.
[10] 11-24/844r0, “Padding Time in Dynamic Power Save”, Maolin Zhang et al.
[11] 11-24/2080r1, “High-Capability Protection in DPS Follow Up”, Maolin Zhang et al.
[12] 11-24/171r26, “TGbn Motions List - Part 1”, Alfred Asterjadhi.

## Slide 10: Straw Poll
Straw Poll 1:
  Do you support to define an explicit data indicator for sustaining higher capability mode?
Straw Poll 2:
  If an explicit data indicator is defined, do you support to define a guard timer to avoid unnecessary prolonged higher capability mode?