## Slide 1: Feasibility Study of Mono-static Backscatter in Sub-1 GHz
Date: 2025-05-10
Authors:
Name | Affiliation | Address | Email
Panpan Li | Huawei | Singapore | lipanpan25@huawei.com
Lei Huang |  | Singapore | 
Lumin Liu |  | Singapore | 

## Slide 2: Background
This contribution intends to discuss the feasibility of mono-static backscattering communication in sub-1 GHz
  Use cases
  AMP S1G tag reading
  Prior arts of self-jammer cancellation
  Link budget analysis
  Operating bands, bandwidth
  PHY design principle
  Coexistence issues

## Slide 3: Use cases
According to AMP technical report, some mobile device related use cases like item tracking and smart home require coverage up to 10 meters [2].
Mobile device related mono-static backscattering use cases in 2.4 GHz discussed in [3] has coverage 10~20cm.
Mono-static backscattering communication in sub-1GHz is expected to achieve >5m coverage.

## Slide 4: AMP S1G Tag reading
AMP AP
Single antenna
Leakage removal modules
  RF carrier cancellation (including directional coupler/circulator)
  Baseband leakage removal
AMP tag
Similar simple tag as 2.4G
Carrier
OOK signal
RF Harvesting & Power Management
Digital Logic
RF carrier cancellation
ADC
Directional coupler/Circulator
Tx
Rx
Tx
Rx
Baseband leakage removal

## Slide 5: Prior Arts of self-jammer cancellation
 | Tx power (dBm) | Rx sensitivity (dBm)
[8] | 33, 11 | -103, -98, -93, -84
[9,11] | 30, 17.5 | -80, -77
[10] | 33, 27, 11 | -88, -82, -75
Typical RF carrier cancellation in UHF RFID achieve 50-70dB [5]
Baseband algorithm can bring >60dB (up to 80dB) suppression [6, 7]
RFID chips [8-11] achieve [-103, -77]dBm Rx sensitivity
  10dBm self-jammer at Rx port is usually assumed
  Assume backscatter signal -90dBm, >100 dB self jammer cancellation are achieved

## Slide 6: RF carrier cancellation circuit examples in [8-11]

## Slide 7: Link budget analysis
Pt_AP=35dBm
Antenna loss: -5dB
5m PL: -45.7dB
Backscatter loss: -5dB
5m PL: -45.7dB
Antenna loss: -5dB
Backscatter signal: -81.4dBm
SINR=>3dB
We need to mitigate leakage to at least -85dBm (~95dB suppression), which should be achievable for very narrow band signal (e.g., CW)
  RF carrier cancellation (45dB)
  Baseband interference suppression (50dB)
Thermal noise: -114dBm (1MHz)
Leakage before removal: 10dBm
Leakage after removal: -85dBm
95dB
Return loss: 15dB
Coupling: -10dB
Coupling: -10dB

## Slide 8: Operating bands, bandwidth
To achieve >5m coverage in sub-1GHz, AMP may seek operating bands with higher Tx power.
Possible AMP operating bands in sub-1GHz [Appendix A]:
  For US, comply with FCC
  For China, RFID bands
  For EU: maybe RFID bands
  For other areas, choose operating bands with higher Tx power limitation
Possible AMP BW in sub-1GHz:
  200 kHz , 400 kHz, 250 kHz, 500 kHz,...

## Slide 9: PHY design general principle
AMP-S1G PHY should be consistent with 2.4 GHz as much as possible
  Device type: mono-static backscatter, bi-static backscatter, active transmission
  PPDU format: overall formats remain same with 2.4G, details maybe different
  Modulation: OOK is baseline
  Coding: start with Manchester, open to other choices
Focus on difference of AMP PHY operating on sub-1 GHz and 2.4G
  Operating class, bandwidth, channelization
  Data rates: limited by BW
  Waveform: start with CW, since narrow BWs make DSSS/OFDM/MC-OOK not suitable

## Slide 10: AMP-S1G PPDUs
S1G preamble | Excitation | AMP-Sync | AMP-SIG | AMP-Data | Excitation | ….
AMP-Sync | AMP-SIG | AMP-Data
DL PPDU
UL PPDU
AMP-S1G DL PPDU
  Backscatter:
    (S1G preamble) + Excitation + AMP-Sync + (AMP-SIG) + AMP-Data + Excitation
    The existence of S1G preamble depends on regions
    S1G preamble can be changed based on S1G_1M PPDU (11ah)
    could exist repetitions of “AMP-Sync + (AMP-SIG) + AMP-Data + Excitation”
  Non-backscatter:
    (S1G preamble) + AMP-Sync + (AMP-SIG) + AMP-Data
AMP-S1G UL PPDU
  AMP-Sync + AMP-Data

## Slide 11: Coexistence
Level 1: 802.11 & non 802.11 [2]
  Energy detection, LBT,…
Level 2: 11bp & 11ah
  11ah devices are expected to recognize AMP-S1G PPDUs
  S1G preamble in AMP-S1G PPDUs can be constructed based on 11ah preamble
Level 3: AMP data communication in sub-1 GHz & AMP WPT
  First need to decide whether WPT PPDU should be designed and distinguished
Also, interference from 2.4 GHz may be considered.
802.11
Non 802.11: RFID, etc
AMP
11ah
Data communication
WPT
Coex issues
Energy detection, LBT

## Slide 12: Summary
In this contribution, we investigated the feasibility of mono-static backscattering communication in sub-1 GHz. According to the evaluations, it is feasible to achieve >5 meter coverage with
  High Tx power
  RF and baseband self-jammer cancellation

## Slide 13: Reference
[1] 11-25-0338-00-00bp-amp-data-communication-in-sub-1-ghz
[2] 111-23-2203-01-0amp-updated-technical-report-on-support-of-amp-iot-devices-in-wlan
[3] 11-23-2038-01-0amp-close-range-amp-backscattering-in-2-4ghz
[4] https://www.digikey.com/en/products/filter/rf-circulators-and-isolators/1010
[5] https://ieeexplore.ieee.org/stamp/stamp.jsp?tp=&arnumber=9418696
[6] https://ieeexplore.ieee.org/stamp/stamp.jsp?tp=&arnumber=9380725
[7] Q. Guo et al., “A novel adaptive leakage suppression method for UHF RFID reader,” in Proc. IEEE Int. Conf. RFID (RFID), May 2017, pp. 187–192.
[8] https://support.impinj.com/hc/article_attachments/40267970973459
[9] https://www.st.com/resource/en/data_brief/st25ru3993-hpev.pdf
[10]https://www.cisper.com/datasheets/MTI%20Micro%20Electronics/MTI_Micro_Electronics_MSx10_RFID_Reader_SiP_Datasheet_v1.2a.pdf
[11] https://www.st.com/resource/en/application_note/an5532-carrier-cancellation-for-rain-rfid-readers-with-st25ru3993-stmicroelectronics.pdf

## Slide 14: SP 1
Do you agree to add the following text to TG bp SFD?
  11bp defines at least one mode of MAC/PHY that supports mono-static backscattering communication in sub-1 GHz.
  Yes
  No
  Abstain

## Slide 15: Appendix
 | China [i] | Europe [ii] |  | US [iii] | 
 | RFID | RFID |  | Frequency hopping spread spectrum | Digital modulated systems
Bands (MHz) | 840-845, 920-925 | 865-868 | 915-921 | 902-928 | 
Bandwidth | 250 kHz | 200 kHz | 400 kHz |  | 
TX power | 2W (ERP) | 2W (ERP) | 4W (ERP) | >=50 channel: 36 dBm (EIRP) <50 channel: 30 dBm (EIRP) | 36 dBm (EIRP); <=8 dBm in any 3 kHz
Transmit mask | Adjacent Channel Power Ratio (ACPR): 40dB (first adjacent channel), 60 dB (second adjacent channel) |  |  | Channel<250kHz, at least 50 channels; Channel>250kHz, at least 25 channels; Maximum allowed 20dB bandwidth is 500kHz | minimum 6 dB bandwidth shall be at least 500 kHz
[i] 关于发布800/900MHz 频段射频识别（RFID）技术应用试行规定的通知.
[ii] https://www.etsi.org/deliver/etsi_en/302200_302299/302208/03.04.01_60/en_302208v030401p.pdf.
[iii] https://www.law.cornell.edu/cfr/text/47/15.247.
[iv] https://www.itu.int/dms_pubrec/itu-r/rec/sm/R-REC-SM.2151-0-202209-I!!PDF-E.pdf
Except the table below, other regulations [iv] may also be considered.

## Slide 16: Appendix : Simulation results
DL PER of data field
Simulation setting:
TX
  Payload: 100 bits
  Encoding: Manchester
  Modulation: OOK
  Waveform: CW
  No Tx filter
Channel
  AWGN channel
RX
  No Rx filter
  Non-coherent detector
Notes: Rx: 2M, Mono-static: SNR ​ = P_AP_Tx​ − backscatter loss​ - 2*Path loss - P_noise
P_noise=-70, Pt=35
80MHz thermal noise: -95dBm

## Slide 17: Appendix : Simulation results
UL PER of data field
Simulation setting:
AP side:
  Packet size = 100 bits
  Manchester encoding
  EIRP: 35dBm (0dBr)
  Leakage : modeled in Rx noise
  Rx noise: -55dBm (-90dBr)
  No filter
  Coherent detector
STA side:
  Modulation noise: -20dBr
  Backscatter loss: 5dB
  No filter
AP
STA
d
Leakage