## Slide 1: Thoughts on AMP frame format
Date: 2025-04-26
Authors:

## Slide 2: Background
Motion #29 defines AMP non-AP STA functional entities, including
  Backscatter non-AP AMP STA: A non-AP AMP STA that is capable of receiving only AMP Downlink PPDUs and supports uplink backscatter transmission.
  Active Tx non-AP AMP STA: A non-AP AMP STA that is capable of receiving only AMP Downlink PPDUs and supports active transmission of AMP Uplink PPDUs.
  AMP Enabled non-AP STA: A non-AP STA (e.g. non-HT, HT or HE STA) that is also capable of receiving AMP Downlink PPDUs.
Three types of AMP non-AP STA uplink access mechanisms have passed the motion, including
  time-slot based random access mechanism for Active Tx non-AP AMP STAs
  time-slot based scheduled access mechanism for Active Tx non-AP AMP STAs
  duty-cycle operation for an AMP device is able to support TSF
In this contribution, we’d like to discuss which information needs to be indicated in the DL or UL frames during the channel access process of AMP non-AP STAs
Notes: AMP-assisted devices tend to achieve compatibility and coexistence with legacy STAs, and further reduce power consumption through environmental energy harvesting, while AMP-only devices may have active transmitters or just transmit through backscatter

## Slide 3: AMP UL access frame exchange
Based on the TG discussion,
The time-slot based access mechanism includes,
A DL frame, like AMP trigger, indicates parameters of time slots
AMP non-AP STA selects a time slot to access based on scheduling or random methods
AMP ack
The duty cycle operation includes,
Indication of duty cycle parameters, including available window parameters and corresponding AMP non-AP STA (s)
After configuration, periodic DL frames, such as AMP triggers, indicating the start time of the available window

## Slide 4: For AMP DL frame
MAC Header | Frame Body | FCS
control | duration | T ID | R ID | …
For AMP DL frame，
T ID： Transmitter address
R ID： Used for receiver addressing, such as AMP non-AP STA(s) identifier\ group identifier \ broadcast address
Duration: Protection time indication
  Legacy STA will not access during this time period
Control: Necessary control information, of course, simplify as much as possible
  Distinguish downlink frames, or
  Indication of frame variants
The time slot parameters for AMP trigger frames or the necessary information for the AMP beacon can be indicated in the frame body
At the same time, the downlink frame can also indicate the type of uplink feedback for this request, such as requesting STA to report data, device information, device energy level, device power-saving status, etc,

## Slide 5: AMP DL frame-control field (1/2)
Type | subtype | ……
Control field Method 1
Method 1：For different uplink access mechanisms, use different frame types,
Type：Indicate ‘AMP frame’, which facilitates differentiation from other .11 MAC frames
Subtype：Further indicate the frame type, such as ‘AMP random access trigger’\ ‘AMP scheduled access trigger’\ ‘AMP beacon’ \ ‘AMP duty cycle trigger’ …
Other necessary information, such as operating parameters(like BW, data rate), protection frame indication, etc
Subtype | Indication
0 | AMP beacon
1 | AMP Backscattering frame
2 | AMP random access trigger
3 | AMP scheduled access trigger
4 | AMP duty cycle trigger
5 | AMP ack
… | …
Example of using frame categories for differentiation

## Slide 6: AMP DL frame-control field (2/2)
Control field Method 2
Method 2：For different uplink access mechanisms, indicate different access modes,
Type：indication ‘AMP trigger frame’ / ‘AMP beacon’ / ‘AMP discovery’…that is, define AMP trigger frames under different access methods as the same type of frame
Operation/access mode: indicate the access/operation mode of the uplink AMP PPDU triggered by the frame if it’s an AMP trigger
Other necessary information, such as operating parameters(like BW, data rate), protection frame indication, etc
Subtype | Indication
0 | time slot based random access
1 | time slot based scheduled
2 | duty cycle operation
… | …
Example of operation/access mode for AMP trigger
Subtype | Indication
0 | AMP beacon
1 | AMP Backscattering frame
2 | AMP trigger
3 | AMP ack
… | …
Example of AMP frame type

## Slide 7: For AMP UL frame (response)
At the stage of discovering AMP devices, AMP AP needs to obtain device information of AMP non-AP STAs for management and control, and the response from AMP non-AP STA should include the following information
  Identifier of AMP non-AP STA
  STA type: Backscatter non-AP AMP STA / Active Tx non-AP AMP STA /AMP Enabled non-AP STA…
  Operation parameters: BW, data rate…
  (Optional) Capability Information: TSF supported, power management supported…
At the stage of solicited data transmission, the response from AMP non-AP STAs should include,
  T ID: the identifier of AMP non-AP STA(s)
  R ID: the identifier of AMP AP
  data
  There may be some security parameters

## Slide 8: Summary
Based on TG current progress we have provided some thoughts on AMP frames.
Discussed the possible fields that AMP DL frames may contain and proposed two methods for the design of the control field
Possible response information from AMP non-AP STA during discovery and solicited data transmission stage
April 2025

## Slide 9: References
[1]11-24-1613r7, Specification Framework for TGbp
April 2025