## Slide 1: Discussion on Numerology and Bandwidth for 11bq
Date: 2025-05-11
Authors:
Name | Affiliation | Address | Phone | Email
Eunsung Park | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | esung.park@lge.com
Insun Jang |  |  |  | insun.jang@lge.com
Hongwon Lee |  |  |  | hongwon.lee@lge.com
Insik Jung |  |  |  | insik0618.jung@lge.com
Dongju Cha |  |  |  | dongju.cha@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com
Sanggook Kim |  | 10680 Treena St 550, San Diego CA 92131 |  | sanggook.kim@lge.com

## Slide 2: Introduction
Many contributions discussed high level design ways and technical scope for IMMW during the SG phase [1-6]
  Although some of the details are slightly different, they have almost identical views
    Leverage the sub-7 GHz PHY design and 11be MLO architecture
In this contribution, we discuss numerology and bandwidth which can be supported in 11bq
  To this end, we look into the following aspects
    Upclocking parameter
    1x and 4x numerologies (i.e., ac and ax/be/bn numerologies)
    Possible bandwidths

## Slide 3: Upclocking Parameter (1/2)
To determine the upclocking parameter, the following factors can be taken into consideration
  Peak data rate
  Implementation
  Impairment factors
    CFO / phase noise / inter-carrier interference
    Delay spread / inter-symbol interference
The larger the upclocking parameter is, the wider the bandwidth will be, and thus, the higher peak data rate we can achieve
However, along with an increase in the upclocking parameter and the bandwidth, the hardware clock rate also needs to be faster
  It can be a burden on implementation

## Slide 4: Upclocking Parameter (2/2)
Based on the packet error rate results shown in [7], the upclocking parameter should be equal to or larger than 4 times
  Wider subcarrier spacing is more robust to CFO, inter-carrier interference, etc.
However, as the upclocking parameter grows, the symbol and guard interval lengths decrease, and thus, the PPDU can become vulnerable to inter-symbol interference
  Many research papers cited in [8] show that, in a mmWave band, most of the delay spreads are measured within 0.1 us
    For a reliable performance, it may be better to have at least 0.1 us GI in a mmWave band which can be guaranteed by applying up to 8 times upclocking to 0.8 us GI
We recommend 4 / 8 times upclocking
  8 times upclocking may be preferable considering CFO, phase noise, etc., while 4 times upclocking may be better in terms of implementation

## Slide 5: 1x and 4x Numerologies
To compare 1x and 4x numerologies (i.e., ac based and ax/be/bn based numerologies), the following factors can be taken into consideration
  Performance
  Future extension
When it comes to the performance, although 1x numerology is slightly better in terms of PER, 4x numerology may be preferable given a better data rate / throughput as shown in [7]
Moreover, 4x numerology can be easily expanded to advanced features such as OFDMA, higher modulation, etc., in the future, by simply reusing the existing sub-7 GHz designs
We recommend to reuse 4x numerology

## Slide 6: Possible Bandwidth (1/2)
Possible bandwidths which can be supported in 11bq are investigated and we provide our thoughts on them
The minimum bandwidth should be larger than (or equal to) 160 MHz
  In the sub-7 GHz band, bandwidths up to 80 / 160 MHz are mandatory and can be frequently used in conjunction with preamble puncturing
  STAs capable of a mmWave band operation may be high-end, and thus, may have a capability larger than 80 / 160 MHz
The maximum bandwidth should be large enough to support various use cases of 11bq [9] although it is probably determined as an optional bandwidth considering hardware complexity
  The maximum bandwidth which is depending on the reused numerology and applied upclocking parameter should guarantee at least a similar level of the peak data rate supported in the sub-7 GHz band

## Slide 7: Possible Bandwidth (2/2)
Possible bandwidths for 11bq are as follows according to the upclocking parameters and numerologies
We recommend to define 320 MHz, 640 MHz, and 1280 MHz by applying 4 / 8 times upclocking to 4x numerology (in red)
  We are open to define 160 MHz and 2560 MHz (in green)
  160 / 320 / 640 / 1280 / 2560 MHz can achieve about 1.4 / 2.8 / 5.7 / 11.5 / 23.0 Gbps with 64 QAM and 2 spatial streams based on the analysis in [9]
  A duplicated tone plan introduced in [10] is possible when using certain bandwidths (e.g., 320 / 640 / 1280 MHz based on 4 times upclocking)
Upclock. parameter | 1x numerology |  |  |  | 4x numerology |  |  |  | 
 | 20 MHz | 40 MHz | 80 MHz | 160 MHz | 20 MHz | 40 MHz | 80 MHz | 160 MHz | 320 MHz
4 | 80 MHz | 160 MHz | 320 MHz | 640 MHz | 80 MHz | 160 MHz | 320 MHz | 640 MHz | 1280 MHz
8 | 160 MHz | 320 MHz | 640 MHz | 1280 MHz | 160 MHz | 320 MHz | 640 MHz | 1280 MHz | 2560 MHz
16 | 320 MHz | 640 MHz | 1280 MHz | 2560 MHz | 320 MHz | 640 MHz | 1280 MHz | 2560 MHz | 5120 MHz

## Slide 8: Conclusion
We have discussed numerology and bandwidth based on the following aspects
  Upclocking parameter
  1x and 4x numerologies (i.e., ac and ax/be/bn)
  Possible bandwidths
We have recommended to define 320 MHz, 640 MHz, and 1280 MHz by applying 4 / 8 times upclocking to 4x numerology
  We are open to define 160 MHz and 2560 MHz

## Slide 9: Straw Poll #1
Do you support the following in 11bq?
  Bandwidths for 11bq are defined by applying 4 times upclocking to bandwidths defined in sub-7 GHz
    Whether to reuse 1x numerology (e.g., ac) or 4x numerology (e.g., ax/be/bn) is TBD
Y/N/A:

## Slide 10: Straw Poll #1-1
Do you support the following in 11bq?
  Bandwidths for 11bq are defined by applying 8 times upclocking to bandwidths defined in sub-7 GHz
    Whether to reuse 1x numerology (e.g., ac) or 4x numerology (e.g., ax/be/bn) is TBD
Y/N/A:

## Slide 11: Straw Poll #2
How many bandwidths do you support to define in 11bq?
  Option1: less than or equal to two bandwidths
  Option2: more than two bandwidths
Op1/ Op2 / A:

## Slide 12: Straw Poll #2-1
Do you support the following in 11bq?
  320 MHz, 640 MHz and 1280 MHz bandwidths are defined
    Other bandwidths are TBD
    Upclocking parameter is TBD
    Whether to reuse 1x numerology (e.g., ac) or 4x numerology (e.g., ax/be/bn) is TBD
Y/N/A:

## Slide 13: Straw Poll #2-2
Do you support the following in 11bq?
  320 MHz and 640 MHz bandwidths are defined
    Other bandwidths are TBD
    Upclocking parameter is TBD
    Whether to reuse 1x numerology (e.g., ac) or 4x numerology (e.g., ax/be/bn) is TBD
Y/N/A:

## Slide 14: Straw Poll #2-3
Do you support the following in 11bq?
  320 MHz bandwidth is defined
    Other bandwidths are TBD
    Upclocking parameter is TBD
    Whether to reuse 1x numerology (e.g., ac) or 4x numerology (e.g., ax/be/bn) is TBD
Y/N/A:

## Slide 15: Straw Poll #3
Do you support the following in 11bq?
  The smallest bandwidth for 11bq is 320 MHz
    Upclocking parameter is TBD
    Whether to reuse 1x numerology (e.g., ac) or 4x numerology (e.g., ax/be/bn) is TBD
Y/N/A:

## Slide 16: Straw Poll #3-1
Do you support the following in 11bq?
  The smallest bandwidth for 11bq is 160 MHz
    Upclocking parameter is TBD
    Whether to reuse 1x numerology (e.g., ac) or 4x numerology (e.g., ax/be/bn) is TBD
Y/N/A:

## Slide 17: Straw Poll #4
Do you support the following in 11bq?
  4x numerology (e.g., ax/be/bn) is reused to define a bandwidth and a tone plan for 11bq
Y/N/A:

## Slide 18: References
[1] 11-23-1819-01-immw-integrated-mmwave-design-considerations
[2] 11-23-1878-01-immw-high-level-design-considerations-of-immw
[3] 11-23-1905-00-immw-high-level-thoughts-on-immw
[4] 11-23-1968-00-immw-discussion-on-general-direction-of-integrated-mmwave
[5] 11-23-2004-00-immw-technical-scope-proposal
[6] 11-24-0066-00-immw-discussion-on-target-objectives-for-immw
[7] 11-25-0854-00-00bq-considerations-on-numerology-for-immw
[8] 11-22-1872-00-0uhr-considerations-on-phy-designs-for-mmwave-band
[9] 11-24-0066-00-immw-discussion-on-target-objectives-for-immw
[10] 11-25-0365-01-00bq-ppdu-format-for-immw