## Slide 1: Improve the Robustness of Intermediate FCS
Date: 2025-05-08
Authors:
Name | Affiliation | Address | Phone | Email
Ning Gao | OPPO |  |  | gaoning1@oppo.com
Chaoming Luo |  |  |  | 
Liuming Lu |  |  |  | 
Weijie Xu |  |  |  | 
Liangxiao Xin |  |  |  | 
Huixuan Zhou |  |  |  | 

## Slide 2: Introduction
An intermediate FCS (I-FCS) within an ICF was proposed in [1] to trigger DPS STAs to switch their capability mode before the end of the ICF.
[2] proposed to use two contiguous User Info fields, known as I-FCS User Info fields, to form an I-FCS and the two I-FCS User Info fields are identified by a same special AID12 value.
However, due to the non-fixed location, the I-FCS is still facing a high miss detection probability issue if there are error bits in the AID12 field. [3]
To be specific, the entire I-FCS could be invalid if at least one of the two I-FCS User Info fields is not detected. Because the receiver can not distinguish the detected single I-FCS User Info field is the first one or the second one. So the receiver can not get all the 32 bits I-FCS.
In this contribution, some methods are provided to improve the robustness of the I-FCS in case of only one I-FCS User Info field is detected.

## Slide 3: Proposed Methods
Idea: if a DPS STA can distinguish the detected single I-FCS User Info field is the first one or the second one. Then, it can recover the other one I-FCS User Info field.
If the first one is detected, then the following 5 octets is the second one.
If the second one is detected, then the preceding 5 octets is the first one.
Three methods are provided here to distinguish I-FCS User Info fields:
Option 1: odd or even number
The first I-FCS User Info field is always an odd-numbered User Info field in the User Info List while the second I-FCS User Info field is always an even-numbered User Info field in the User Info List, vice versa.
A dummy User Info field can be inserted before the I-FCS to achieve this.

## Slide 4: Proposed Methods
Option 2: different special AID12 values
The first I-FCS User Info field and the second I-FCS User Info field are identified with different special AID12 values (e.g., 2011 and 2012).
Option 3: additional indication field
A field within each I-FCS User Info field indicates whether it is the first one or the second one.

## Slide 5: Summary
Three methods are provided in this contribution to improve the robustness of the I-FCS in case of only one of the two I-FCS User Info fields is detected:
  Use odd or even number
  Use different special AID12 values
  Use additional indication field
When a DPS STA can distinguish the detected single I-FCS User Info field is the first one or the second one. Then, it can recover the other one I-FCS User Info field.

## Slide 6: Reference
[1] 11-24-1227-00-00bn-some-usage-of-intermediate-fcs
[2] 11-25-0144-01-00bn-ifcs-pn-and-mic-inclusion-in-a-trigger-frame
[3] 11-24-1702-00-00bn-consideration-on-the-signalling-method-of-intermediate-fcs

## Slide 7: SP 1
Which method do you prefer to improve the robustness of the I-FCS in case of only one of the two I-FCS User Info fields is detected:
  Option 1: Use odd or even number
  Option 2: Use different special AID12 values
  Option 3: Use additional indication field
  Option 1/Option 2/Option 3/Abstain