## Slide 1: AP-assisted Opportunistic Power Saving
Date: 2025-0-05
Authors:

## Slide 2: Context
You arrive at your favourite restaurant, 10 minutes before the Happy Hour finishes, and it is full (I am sorry madam/sir, there is a wait). Outside it is raining.
Bad scenario: You are left with the option to wait outside, until there is a free table (indeterminate wait – leave hungry, thirsty and wet).
Good scenario: There is at least a 20-minute wait, but you can wait at the bar and order your Happy Hour drinks there (and stay dry on the outside).
Which experience would one prefer?
Why is the second scenario better? Because you know how long you need to wait and you are offered alternatives.

## Slide 3: Abstract
This kind of service is also desirable for the modern STA.
This submission proposes an enhancement to enable a non-AP STA to:
  opportunistically save power or
  make/implement alternative useful plans
while the AP has committed to not service the non-AP STA.
What is needed: The AP announces that it commits to not initiating a frame exchange containing a frame addressed to (certain) STA(s)

## Slide 4: Problem
A non-AP STA spends significant amounts of time with its radio on:
  waiting for DL data traffic
  waiting for a Trigger frame which may solicit UL data traffic
When a STA has its radio on, NAV and AID are used today to optimise power consumption at the STA, within the TXOP duration. However:
  Often the ICF which initiates the TXOP does not announce/cover the full TXOP duration
  TXOP duration tends to get smaller, in pursue of low latency
Therefore, a non-AP STA can save more power if it knows that there is no interesting DL/UL opportunity beyond the end of current TXOP
An AP may already possess this information:
  It plans its DL/UL beyond the current TXOP
  Several use cases to consider: Large number of STAs, Congested channel, Co-TDMA Mobile-AP limited resources, QoS requirements, etc…

## Slide 5: Solution
Provide new information, in the ICR/ICF or in a Control response from the AP, to help the non-AP STA turn off its radio beyond the end of the TXOP
Specifically, AP signals to the non-AP STA(s)
  Abstinence Start Time
  Abstinence Duration
  Abstinence Type (DL and/or UL MU)
The AP commits to not initiating a frame exchange containing a frame addressed to the signalled STA(s)
  AP may use special AID to signal to all receiving STAs
  AP may use BSRP or Multi-STA BlockAck
Major advantage: Non-AP STA(s) may turn off radio (no explicit PM signalling, for longer than current NAV/TXOP)

## Slide 6: Problem (and possible solution) in a picture
STA may switch off radio for longer - No need for PM signalling
BSRP below is just an example – used as an ICF

## Slide 7: Examples of usage – Multi-STA BA / BSRP

## Slide 8: Alternative actions at the non-AP STA
Using the information provided by the AP, the STA may:
turn its radio off
reconsider priority/timing of local events/operations:
  Local coex events; some are movable, so can be brought forward. E.g. BT A2DP
  Repurpose resources (radio or/and buffers) for other traffic, e.g. switch to P2P channel or use TX buffers for TDLS traffic
realise that its QoS requirements are not met:
  Can trigger countermeasures, e.g. use rTWT, or come out of Power Save mode, or move to Active state more often, etc
Note: None of these need to be specified in normative text (but could if members would support defining non-AP behaviour)

## Slide 9: Can we use PUO instead?
No: during PUO the AP is unavailable
During Abstinence the AP is available for several operations:
  The STA may transmit a PPDU to the AP – subject to other rules applicable
  STA(s) not addressed by the AP ignore the abstinence information

## Slide 10: Multi-STA BlockAck
Similar format to IDC and A-MPDU feedback design
May use special AID value for broadcast (to all STAs)

## Slide 11: Examples – non-AP STA uses provided information
AP provides the information in “best effort”. May commit to DL abstinence only, or UL abstinence only, or to both DL and UL abstinence
STA can adjust own behaviour, according to received information
Note: DL includes SU Sounding, UL MU includes MU (triggered) Sounding
(Abstinence) DL | (Abstinence) UL MU | STA example behaviour
0 | 0 | Keep radio on (current behaviour)
1 | 1 | Turn radio off, or (MLO case) Prefer/schedule UL on different AP, or (P2P case) Switch radio to P2P channel, or (P2P/TDLS case) Schedule TX to P2P/TDLS peer
0 | 1 | (MLO case) Prefer/schedule UL on different AP, or (P2P/TDLS case) Schedule TX to P2P/TDLS peer
1 | 0 | Turn radio off (if no outstanding UL MSDUs/MPDUs)

## Slide 12: Straw poll
Do you support to:
- Define Multi-STA BlockAck and BSRP variants that an AP can use to provide Non-Periodic Abstinence information?
- Allow use of the Multi-STA BlockAck variant as a response frame to UL SU A-MPDU?
Y
N
A

## Slide 13: References
11-24-1247-00 icf-icr-design-for-coex
11-25-0063-00 indication-of-the-unavailability-information-for-idc
11-24-0002 A-MPDU Coexistence Feedback