## Slide 1: CoBF Nsym Field Definition
Date: 2025-05-12
Authors:

## Slide 2: Introduction
PHY related parameters in CoBF Invite/Response frames are SPed [1, 2]
Number of OFDM symbols are included for sharing AP and shared AP to negotiate CoBF PPDU duration
In this contribution, the bit definition of Number of OFDM Symbol is discussed.

## Slide 3: Recap: CoBF Invite and Response [1]
CoBF Invite CoBF Response
Category | 
Control | ‘CoBF Invite’
PHY Common Info | Minimum Number of Data OFDM Symbols
 | Maximum Number of Data OFDM Symbols
 | PHY Version Identifier
 | Bandwidth
 | Punctured Channel Information
 | GI+LTF Size
 | Maximum Total Nss Allowed for shared AP
 | Number of CoBF Users in sharing BSS
Per-User Info in Sharing BSS | STA ID
 | Nss
Category | 
Control | ‘CoBF Acceptance’
PHY Common Info | Suggested Number of Data OFDM Symbols
 | PHY Version Identifier
 | Extra LTF Allowed
 | Number of CoBF Users in shared BSS
Per-User Info in Shared BSS | STA ID
 | MCS
 | Nss
 | 2xLDPC

## Slide 4: Number of OFDM Symbols
Number of bits: 9-bits, the same as in ELR-SIG
  Each value = Num of OFDM symbols - 1
Valid range: 0 to 110001110 (399 symbols)
  PPDU limit: 5.484ms
  Preamble: min 66.4us
    UHR-SIG (min 16us): Two users with UHR-SIG MCS0
    UHR-LTF (min 14.4us): Two LTFs with 2xLTF+0.8us
Other values are not valid
  110001111 to 111111111

## Slide 5: Nsym Values setting in CoBF
CoBF Invite:
  Two subfields
    Minimum Number of Data OFDM Symbols
    Maximum Number of Data OFDM Symbols
  Set to 0 to 110001110, entries >= 110001111 are invalid
  In some implementation, sharing AP only want to specify one length
    Set Max value = Min value
CoBF Response
  One subfield: Suggested Number of Data OFDM Symbols
    Valid range: 0 to 110001110
  Define one entry to indicate “no suggestion”.
    Shared AP is ok with min/max Nsym range, or flexible with any value
    Propose to use ‘111111111’ (511)

## Slide 6: Summary
Discussed the definition of subfields related to Number of OFDM Symbols in CoBF Invite and Response
Propose to define one entry ‘111111111’ (511) as “no suggestion” for Suggested Number of OFDM Symbols

## Slide 7: SP1
Do you agree to add the following to 11bn SFD?
11bn defines the three “Number of Data OFDM Symbols” subfields in CoBF Invite and Response frames to be 9-bits, and
  Value n indicate “Number of OFDM Symbols – 1”
  Value 511 (‘111111111’) indicates “No suggestion” in “Suggested Number of Data OFDM Symbols” subfield in CoBF Response frame
  Note:
    Minimum Number of Data OFDM Symbols
    Maximum Number of Data OFDM Symbols
    Suggested Number of Data OFDM Symbols

## Slide 8: Reference
[1] 11-25/0389r2, information-exchange-in-the-cobf-transmission-phase
[2] 11-25/0381r1, some-open-issues-on-cobf