## Slide 1: PHY Version indications in Co-SR transmissions
Date: 2025-05-08
Authors:
Name | Affiliations | Address | Phone | email
Ross Jian Yu | Huawei |  |  | ross.yujian@huawei.com
Jason Yuchen Guo |  |  |  | 
Genadiy Tsodik |  |  |  | 
Ming Gan |  |  |  | 

## Slide 2: Background
The following motion has passed regarding Co-SR transmission:
  TGbn defines a multi-AP Coordinated Spatial Reuse (Co-SR) at TXOP-level with power control.
    Other multi-AP coordination modes are TBD.
  [Motion #29, [1] and [49-65]]
  11bn defines the following modes for Co-SR transmission:
    Mode 1: trigger + same L-SIG contents, could be different U-SIG contents.
      For UHR+EHT, or EHT+UHR or EHT+EHT Co-SR transmission.
      Provided no changes to non-UHR EHT non-AP STAs are needed.
    Mode 2: Tigger + same L-SIG contents + same U-SIG contents
      For UHR+UHR Co-SR transmission.
    For all modes, the two PPDUs will start and end at the same time.
    UHR PPDU for Co-SR transmission will be used for either mode 1 or mode 2 when UHR transmission exists.
      There exists an indication in U-SIG field to indicate the UHR PPDU is a UHR PPDU for Co-SR transmission.
  [Motion #252, [264] and [282]]
In this proposal, we focus and discuss our thinking on information exchange during Co-SR transmissions, especially on PHY version indications.

## Slide 3: Two modes of Co-SR modes
There are two modes of Co-SR transmissions:
Mode 1: UHR+EHT, or EHT+UHR or EHT+EHT | Mode 2: UHR+UHR
L-SIG fields/Co-SR PPDU length | L-SIG fields/Co-SR PPDU length, U-SIG fields
Two BSS colors in U-SIG field of UHR PPDU for UHR+EHT, EHT+UHR, single BSS color for EHT+EHT. An indication in U-SIG field to indicate the UHR PPDU is a UHR PPDU for Co-SR transmission | Two BSS colors in U-SIG field of UHR+UHR An indication in U-SIG field to indicate the UHR PPDU is a UHR PPDU for Co-SR transmission
Signaling of U-SIG field is not needed. | Signaling of U-SIG field is needed.

## Slide 4: PHY version indications in Co-SR invite and Co-SR response exchange
During Co-SR invite and Co-SR response exchange, there could be two options:
  Opt1: sharing AP indicates its intended PHY version(s) for its own PPDU in the upcoming Co-SR transmission. Shared AP responds with its intended PHY version(s) for its own PPDU in the upcoming Co-SR transmission.
  Opt2: sharing AP indicates single intended PHY version for its own PPDU in the upcoming Co-SR transmission. Shared AP responds with single intended PHY version for its own PPDU in the upcoming Co-SR transmission, if it accepts the invitation.
Opt 2 is easier for implementation and preferred.
Applicable PHY versions of Co-SR PPDUs by sharing AP and shared AP are based on the Co-SR invite and response exchange.
Co-SR invite
Co-SR response
Co-SR TF
Co-SR PPDU 2
Co-SR PPDU 1
AP1
AP2
STA1
STA2
UHR
EHT
PPDU1: UHR, PPDU2: EHT

## Slide 5: PHY Version indications in Co-SR Trigger frame
In Co-SR Trigger frame, the PHY Version Identifier in the Special User Info field is set to 1 (UHR) to indicate the Trigger frame is a UHR variant Trigger Frame.
Within the UHR variant Trigger Frame, we propose that the PHY version of PPDU 1 and the PHY version of PPDU 2 are indicated.
  The exaction signaling can be further studied.
The PHY version of PPDUs signaling are thus self-contained, easy for implementations. And the exact signaling may be different for different PHY combinations.

## Slide 6: Other agreed details for Co-SR Trigger frame
The followings are also agreed regarding Co-SR Trigger frame.
In Coordinated Spatial Reuse, the following information shall be carried in the Trigger frame that initiates concurrent CSR transmissions of the 2 APs
  The duration of the data PPDU transmitted by the sharing AP and of the data PPDU transmitted by the shared AP, which are the same, after the Trigger frame
  Other parameters TBD
[Motion #254, [264] and [283, 284]]
The sharing AP, that transmits a Trigger frame as part of a transmission sequence in a Multi-AP coordinated transmission scheme, identifies the shared AP via an AP ID carried in the AID12 field of the User Info field of the frame
  Note: the name of "sharing AP" and "shared AP" are TBD
  Note: Multi-AP coordinated transmission schemes are Co-SR, Co-BF and Co-TDMA
[Motion #135, [1] and [207, 208, 157, 117, 118, 122, 123, 108, 115, 124, 158]]
Do you support to include in the 11bn SFD:
In Coordinated Spatial Reuse, the following information shall be carried in the Trigger frame that initiates concurrent CSR transmissions:
  The transmit power limit of the shared AP
    The shared AP Tx power limitation indicated by the sharing AP should not be lower than the minimum TX power indicated by the shared AP in its request.
  The transmit power of the sharing AP
Supporting docs: 23/1868r2; 24/2060r1; 25/254r0
SP result: no objections

## Slide 7: Summary
In this contribution, we first discuss the PHY version indications during Co-SR invite and Co-SR response exchange. We further discuss the PHY version indications in the Co-SR Trigger frame.
The details of Co-SR invite, Co-SR response, and Co-SR Trigger frame will be further studied.
Co-SR invite
Co-SR response
Co-SR TF
Co-SR PPDU 2
Co-SR PPDU 1
AP1
AP2
STA1
STA2
UHR
EHT
PPDU1: UHR, PPDU2: EHT

## Slide 8: Straw Poll #1
Do you agree to include the following into 11bn SFD?
  During Co-SR invite and Co-SR response exchange, sharing AP indicates single intended PHY version for its own PPDU in the upcoming Co-SR transmission. Shared AP responds with single intended PHY version for its own PPDU in the upcoming Co-SR transmission, if it accepts the invitation.

## Slide 9: Straw Poll #2
Do you agree to include the following into 11bn SFD?
  In Co-SR Trigger frame, the PHY version of PPDU 1 and the PHY version of PPDU 2 are indicated.
    How to signal is TBD

## Slide 10
11-24-0209-14-00bn-specification-framework-for-tgbn, Ross Jian Yu (Huawei)
11-25-0087-00-bn-Co-Triggering-frame-design-for-CoBF, Insik Jung (LG Electronics)
11-25-0389-02-00bn-information-exchange-in-the-cobf-transmission-phase, Alice Chen (Qualcomm)
References