## Slide 1: Considerations on Numerology for IMMW
Date: 2024-xx-xx
Authors:
Name | Affiliation | Address | Phone | Email
Insik Jung | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | insik0618.jung@lge.com
Eunsung Park |  |  |  | esung.park@lge.com
Insun Jang |  |  |  | insun.jang@lge.com
Dongju Cha |  |  |  | dongju.cha@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com
Sang Kim |  |  |  | sanggook.kim@lge.com

## Slide 2: Introduction
Utilization of wide bandwidth is one of the main benefit of introducing the mmWave communications
As proposed in [1]-[4], BW upclocking can be one of the good solutions to support wide bandwidth transmission with low implementation complexity
In this contribution, we investigate the base numerologies to conduct the upclocking
  We provide some base numerologies and discuss which option could be better
  Simulation results are provided for the verification

## Slide 3: Upclocking BW
Motivations
  We can reuse the PPDU structure defined in sub-7GHz standards to reduce the implementation cost
  To fully utlilze the wide bandwidth characteristics of the mmWave band, we can consider upclocking of the base numerology
Design Considerations
  Applying higher upclocking factor brings several benefits
    We can achieve higher throughput because of the wider bandwidth
    Effects of HW impairments like CFO/PN are reduced
    Also, we can prevent the system deviates from the CFO estimation range
  It also has some drawbacks
    Relatively vulnerable to ISI due to the shorter OFDM symbol duration
    We may need faster clock rate to implement wider bandwidth system

## Slide 4: Base Numerology
Numerology 1
  312.5kHz subcarrier spacing in a data part
  11a/n/ac-based PPDU can be considered
  Robust against CFO/Phase noise when same upclocking is applied
  Relatively less complexity (smaller FFT size)
Numerology 2
  78.125kHz subcarrier spacing in a data part
  11ax/be-based PPDU can be considered
  Relatively sensitive to CFO/Phase noise when same upclocking is applied
  Higher data tone ratio over FFT size
  With the same CP length, better throughput can be achieved

## Slide 5: CFO Impact
Estimationable Range
  If CFO exceeds the estimation range (four times of subcarrrier spacing), it cannot be simply estimated through time domain correlation method
  Instead, frequency domain autocorrelation of STF/LTF might be needed which poses additional computation burden to the receiving device
  To avoid the CFO deviates from the estimationable range, we need to set sufficient subcarrier spacing
    For the 40ppm CFO in 60GHz center frequency, 4.8MHz would be the CFO range [2][3]
    If we consider L-STF/LTF with 312.5kHz subcarrier spacing, 4.8MHz / (312.5KHz * 4) = 3.84 times upclockng is needed at least
Estimationable CFO
  CFO can be estimated and compensated through the time domain correlation method

## Slide 6: Simulation Environment
Parameter | Description
MCS | MCS 4
Base bandwidth | 80MHz
CP length | 0.2us
Channel model | 802.11ad channel model (conference room, CR)
TX/RX | 1T1R
Fc | 60 GHz
Channel coding | BCC
Packet size | 1000bits
CFO | 40ppm
*CFO is esimated and compensated using legacy preamble (e.g., L-STF and L-LTF) for both numerologies

## Slide 7: Simulation Results (1/3)
Settings
  Numerology 1 is used
Discussions
  For 1x, 2x BW upclocking, FER is severely degraded
    This is because CFO is in the non-estimationable range
  For 4x, 8x BW upclocking, we have fine FER performance
    This is because the CFO is in the estimationable region
Non-estimationable CFO
Estimationalble CFO

## Slide 8: Simulation Results (2/3)
Metric
  Frame Error Rate (FER)
Settings
  80MHz base BW
  4x upclocked (320MHz)
Discussions
  Performance of 1x and 4x numerologies are similar
    We can think that CFO can be sufficiently compensated for the both numerologies

## Slide 9: Simulation Results (3/3)
Metric: Throughput (bps)
  (1-FER)*NSD*Mod_order*Code_rate /(Sym_duration+N_CP)
Settings
  80MHz base BW
  4x upclocked (320MHz)
  MCS 1-4 are considered
Discussions
  Numerology 2 (78.125kHz base SCS) has higher throughput
    Data tone ratio of numerology 2 is better than that of numerology 1
    CP ratio of numerology 2 is smaller than that of numerology 1
  We observed that 4x numerology is more degraded by phase noise but it might be overcome by implementations. We still think 4x can be beneficial due to the above gains

## Slide 10: Conclusion
We have discussed about the candidate numerologies to support 11bq
We pointed out that BW upclocking can be beneficial to leverage sub-7GHz PHY design
  We can leverage 1x and 4x numerologies
Simulation results demonstrates that the numerology 2 (78.125kHz base SCS) has higher throughput than the numerology 1

## Slide 11: Straw Poll #1
Do you support the following in 11bq?
  4x numerology (e.g., ax/be/bn) is reused to upclock the sub-7GHz PHY for 11bq

## Slide 12: Reference
[1] 11-22-1872-00, Considerations on PHY designs for mmWave band, LGE
[2] 11-23-0066-02, Thoughts on Utiliizing mmWave, Huawei
[3] 11-22-1395-00, Thoughts on high frequency band, Samsung
[4] 11-23-0165-02, Realistic Rates on 60GHz terminals, Broadcom