## Slide 1: Signalling for inextensible ESSes
Date: 2025-07-24
Authors:

## Slide 2: Abstract
This submission proposes a mechanism to reduce latency, improve throughput and save power in ESSes that consist of only one BSS (or of a known set of BSSes), or that consistently use BTM, and a mechanism to improve scanning reliability for mobile APs

## Slide 3: Problem
A STA generally needs to be prepared to roam, in various situations
  E.g. low RSSI, high retries, high congestion, beacon loss, deauth, some coex scenarios
This means a STA typically has to be scanning at fairly frequent intervals
  Especially if conditions are getting worse
This consumes power and typically takes the STA off-channel, increasing latency and decreasing throughput
  Multiplicatively worse if conditions are getting worse so scanning is more frequent
  Scans on all possible channels are especially bad

## Slide 4: Solution
If the ESS is known to only contain one AP MLD (e.g. small home or personal hotspot) then there’s no point looking for another AP MLD to roam to
When connected to AndroidAP5cb2, no point scanning for any other APs with that SSID

## Slide 5: Solution
Add a bit e.g. in the UHR Capabilities or Basic ML to signal “I am the only AP MLD in this ESS”
  Then a STA knows there is no point scanning for another AP MLD to roam to, while connected
    I.e. no time wasted doing directed scans for the SSID
  Just fall back to another ESS, or to cellular, when it gets too bad on the current AP MLD
    If trying for another ESS, no time wasted doing a final directed scan for the old SSID first
  Note: current NR/RNR cannot be used to determine this condition because list not guaranteed complete (Subclause 11.49: “A Reduced Neighbor Report element might not be exhaustive either by choice or by the fact that there may be neighbor APs not known to the reporting AP.”)
Alternatively a protected unicast Neighbor Report exchange could be used

## Slide 6: Solution
Another bit could signal “all the other AP MLDs in this ESS are collocated with the reporting AP MLD”
  Then a STA knows it need only scan on the channels this physical AP has BSSes on
  These channels could be obtained using e.g. NR/RNR (or a new Channel Usage etc.)
This can be generalised to “all the other AP MLDs in this ESS are known (and I can tell you which channels they’re on)”
When connected to MyHome, which has an APs on channels 6, 36, 11 and 40, no point scanning on any other channels for any other APs with that SSID

## Slide 7: Solution
Signal “all the other AP MLDs in this ESS are known (and I can tell you which channels they’re on)”
  Then a STA knows it need only scan on the channels this ESS has BSSes on
  These channels could be obtained using e.g. NR/RNR (or a new Channel Usage etc.)
  Preferably such that a STA is in range of two of them as it moves from one AP MLD to another
Could also apply for “only BSS” indication using empty NR/RNR
  But currently spec requires non-empty list in RNR

## Slide 8: Solution
A third bit could signal “there are multiple AP MLDs in this ESS, but I will use BTM to steer you”
When connected to MyFactoryFloor, which reliably uses BTM to steer to the best AP, no need to scan for any other APs with that SSID

## Slide 9: Solution
Signal “I will reliably use BTM to steer you”
  Then a STA knows it need not perform scanning, or need not do so frequently
  This is more than advertising BSS Transition Management capability: it’s a commitment to always use it to ensure the STA is on its best AP
  More likely to be of value/trusted in controlled (enterprise/warehouse, mesh) environments
    AP needs to be able to reliably identify STA conditions
    STA could benefit from being given justifications (e.g. performance metrics) for the steer
      E.g. latency, throughput, BSS load

## Slide 10: Problem
A mobile AP MLD by definition might be moving out of or into range
This means a STA trying to track it might want to scan for it at more frequent intervals

## Slide 11: Solution
A fourth bit could signal “I am a mobile AP MLD”
  Then a STA knows it might need to perform scanning more aggressively to keep track of the AP
  A STA could also use this to determine whether an AP is useful for positioning
  Note a mobile AP MLD might not be an NSTR mobile AP MLD
When connected to MyAP, but tracking MyDog, should scan for MyDog frequently (and should not try to triangulate my position with it!)

## Slide 12: Straw poll 1
A mechanism should be added to signal that an AP MLD is the only one for an ESS
Y
N
A

## Slide 13: Straw poll 2
A mechanism should be added to signal that all the other AP MLDs in an ESS are collocated with the reporting BSS, or more generally that all the other AP MLDs in the ESS are known (and their channels can be provided, e.g. using RNR with an indication that the list is complete)
Note: This could be combined with the previous mechanism, with empty “other channels in ESS” signalling
Y
N
A

## Slide 14: Straw poll 3
A mechanism should be added to signal that an ESS will consistently use BTM to steer STAs between AP MLDs
Note: Additional information (e.g. performance metrics) might be provided to the STA to justify the steer
Y
N
A

## Slide 15: Straw poll 4
A mechanism should be added to signal that an AP MLD is mobile (even if it is not an NSTR mobile AP MLD)
Y
N
A

## Slide 16: Straw poll 5
The signalling suggested in the previous straw polls should be performed using UHR Capabilities element bits or currently reserved Basic Multi-Link element bits in the (Re)Association Response frame
Note: whether it is also performed in other ways is TBD
Y
N
A

## Slide 17: Straw poll 6
The signalling suggested in the previous straw polls should be performed in unicast Neighbor Report exchanges (with some signalling to indicate the list is complete)
Note: whether it is also performed in other ways is TBD
Y
N
A

## Slide 18: Straw poll 7
The “single AP MLD in ESS” signalling suggested in straw poll 1 should be performed in beacons (and probe responses), using an Interworking element with the HESSID field containing a MAC address with the I/G bit set to 1
Note: whether it is also performed in other ways is TBD
Y
N
A