## Slide 1: Channel Access Mechanisms for the NPCA Operation
Date: 2025-06-04
Authors:

## Slide 2: Introduction
Some details of the channel access mechanism on the NPCA primary channel are defined in TGbn D0.3 [1]
  NPCA STAs that perform channel access on the NPCA primary channel reuse the conventional EDCA mechanism with some exceptions
This contribution discusses the channel access mechanism that defers transmission considering the NPCA switching delay, and proposes necessary modifications to ensure that an NPCA AP which has completed its backoff procedure first can be guaranteed TXOP acquisition

## Slide 3: Channel access on the NPCA primary channel
Channel Access Mechanism on the NPCA primary channel (11bn D0.3)
  The NPCA STA operating on the NPCA primary channel
    Use the same (MU, EPCS) EDCA parameter set for the NPCA primary channel as it uses on the BSS primary channel
    May initiate a TXOP on the NPCA primary channel by following the rules defined in 10.23.2.2 (EDCA backoff procedure) and 10.23.2.4 (Obtaining an EDCA TXOP) with the following exceptions
      Each time that the NPCA STA switches to the NPCA primary channel, it shall initialize
        CW_NPCA[AC] to TBD value and randomly choose a new backoff counter between 0 and CW_NPCA[AC]
      QSRC_NPCA[AC] shall be set to 0
      If the STA is a non-AP STA and the associated AP has disabled the use of untriggered UL transmission, then the STA shall not initiate a TXOP on the NPCA primary channel
Additional rule for the NPCA STA
  The NPCA STA shall not initiate a transmission on the NPCA primary channel to another NPCA STA until that STA's NPCA switching delay time has elapsed
    The specific method by which an NPCA STA defers its transmission initiation on the NPCA primary channel, in consideration of the switching delay of the peer NPCA STA, is not clearly defined

## Slide 4: Mechanism for deferring TX initiation
Two different mechanisms for deferring Tx initiation in the baseline [2]:
  Mechanism 1. Maintaining the backoff counter at 0
    For the STAs with empty Tx queue or the STAs transmitting a Start Time Sync PPDUs
  Mechanism 2. Regenerate a random backoff counter using the current CW[AC] value when the BO is reached to 0
    For the case where the start time of an R-TWT SP is imminent
We propose to reuse the Mechanism 2 for the NPCA STAs
  Applying the Mechanism 1 to the NPCA may cause multiple NPCA STAs to begin transmitting simultaneously after the NPCA AP’s switch delay, potentially resulting in collisions
AP
2
1
0
Non-AP STA1
P80
S80
P80
S80
OBSS TXOP
OBSS TXOP
switching
SW
0
0
0
0
ICF
ICF
ICR
ICR
AP
2
1
0
Non-AP STA1
P80
S80
P80
S80
OBSS TXOP
OBSS TXOP
switching
SW
4
3
2
1
ICF
ICF
ICR
ICR
0
Mechanism 1
Mechanism 2

## Slide 5: Problem statement
Background
  It seems natural for an NPCA AP must defer its transmission until the NPCA STA with the longest switching delay among the intended recipients completes switching
Problem
  During this deferral duration, another NPCA STA may initiate NPCA ICF transmission
    If the AP that completes the backoff procedure first is not guaranteed to obtain the TXOP, the AP may attempt to increase its chances by scheduling only NPCA non-AP STAs with short switching delays
      This implies that the benefits of NPCA operation could become concentrated only among STAs with shorter switching delays
To address the issue, it is necessary to ensure that all the NPCA non-AP STAs also defer their transmissions during the time when the AP is deferring its transmission initiation
AP
2
1
0
Non-AP STA1
P80
S80
P80
S80
OBSS TXOP
OBSS TXOP
switching
SW
5
4
3
2
1
0
4
3
2
2
1
0
ICF
ICF
ICR
ICR
UL PPDU
UL PPDU
BA
BA
Deferred due to NPCA switching delay of another STA

## Slide 6: Proposal
UL TXOP Restricted Duration
  To prevent NPCA non-AP STAs from initiating uplink transmissions while an NPCA AP is deferring its own transmission, a mechanism to restrict the initiation of UL TXOPs may be considered
  The AP can indicate a UL TXOP Restricted Duration through the NPCA Operation Information field element
    When the AP sets a non-zero UL TXOP Restricted Duration, non-AP STAs shall not initiate a UL TXOP on the NPCA primary channel until the indicated duration has expired
  The AP may set UL TXOP Restricted Duration covering the longest NPCA switching delay among the NPCA STAs in the BSS to obtain sufficient scheduling flexibility
NPCA Primary Channel | NPCA Minimum Duration Threshold | NPCA Switching Delay | NPCA Switch Back delay | UL TXOP Restricted Duration
NPCA Operation Information field format

## Slide 7: Proposal (cont’d)
UL TXOP Restricted Duration (cont’d)
  Since EDCAF operates based on aSlotTime, it is reasonable to consider using a unit of 9 μs (or its multiple) for the UL TXOP Restricted Duration
  When the UL TXOP Restricted Duration is set to its maximum value, it may indicate that untriggered UL transmissions on the NPCA primary channel are prohibited
    In this case, the signaling of untriggered UL transmission disablement—already introduced in D0.3—can be achieved through the UL TXOP Restricted Duration field
NPCA non-AP STA operation
  When the UL TXOP Restricted Duration is indicated by the AP, non-AP STAs shall defer the start of their transmissions during the indicated duration
    A non-AP STA that defers its transmission due to the UL TXOP restricted duration may use the same mechanism as when deferring based on the NPCA switching delay, i.e., by re-generating the backoff counter

## Slide 8: Benefits of the Hybrid NPCA Operation Mode
When a non-zero/non-maximum UL TXOP Restricted Duration is designated by the NPCA AP, NPCA operation is carried out in a hybrid form that combines Trigger-only mode and EDCA mode
  This hybrid NPCA operation mode not only ensures that the AP which completes its backoff procedure first gains the TXOP, but also offers the following additional benefits
    Effective Utilization of NPCA Opportunities:
      The Trigger-only mode is effective in mitigating the "different view" problem among NPCA STAs
      However, in Trigger-only operation, if the NPCA AP does not transmit a Trigger Frame or DL PPDU, the NPCA opportunity may be lost
      In contrast, under the hybrid mode, the NPCA opportunity can be utilized by the NPCA non-AP STAs when the UL TXOP Restricted Duration expires
    Improved Fairness Among NPCA STAs:
      An NPCA STA with a longer switching delay enable to begin contention on the NPCA primary channel later than one with a shorter delay, potentially causing fairness issues in EDCA-based NPCA operation
      In hybrid mode, since UL TXOP initiation is restricted before the expiration of the UL TXOP restricted duration, the fairness issue among NPCA STAs can be alleviated

## Slide 9: Summary
The channel access mechanism on the NPCA primary channel for deferring the start of transmission has been discussed
  Reusing the baseline mechanism—generating a new random backoff counter when the backoff counter reaches zero—is preferred
The issue where an NPCA AP that has completed the backoff procedure may lose the opportunity to initiate its TXOP has been discussed
  A UL TXOP Restricted Duration was proposed to ensure AP’s TXOP initiation
The benefits of the hybrid NPCA operation mode have been discussed

## Slide 10: References
[1] Draft P802.11bn D0.3
[2] Draft P802.11be D7.0