## Slide 1: Explicit Sounding Type and Rounds Indication in Co-BF Sounding
Date: 2024-07-24
Authors:
Name | Affiliations | Address | Phone | Email
Mahmoud Hasabelnaby | Huawei |  |  | Mahmoud.Hasabelnaby@huawei.com
Junghoon Suh |  |  |  | 
Osama Aboul-Magd |  |  |  | 
Yan Xin |  |  |  | 
Abdallah Hussein |  |  |  | 

## Slide 2: Problem Statement
Co-BF Sounding process can be carried over a single TXOP or separate TXOPs [1].
Without an explicit indication of the Co-BF sounding rounds to be performed within the shared TXOP in the Co-BF Sounding Invite frame, the Responding AP cannot determine whether the initiating AP is inviting it to perform all rounds of Co-BF Sequential or Joint Sounding within the same TXOP or over separate TXOP.
  For example, following the Joint-BSS1 sounding round, the responding AP would not know whether it is allowed to proceed with initiating its Joint-BSS2 sounding round after collecting OBSS CSI reports from the Joint-BSS1 round, or if no further action is required.
As a result, it is crucial for the Initiating AP to include the sounding type and the specific sounding rounds to be performed within the current TXOP in the Co-BF Sounding Invite frame.
Joint Sounding
Shall AP2 stop here?
or proceed with Joint-BSS2 sounding?

## Slide 3: Proposal: Sounding Type and Rounds Indication in Co-BF Sounding Invite Frame
The initiating AP shall explicitly indicate the following in the Co-BF sounding Invite frame:
  The Co-BF sounding type (i.e., sequential or joint sounding);
  For sequential sounding:
    Whether the initiating AP will perform both cross-BSS and in-BSS sounding or only cross-BSS sounding;
    Whether the responding AP is allowed to initiate after the initiating AP’s Co-BF sequence both cross-BSS and in-BSS sounding, only cross-BSS sounding, or neither.
  For joint sounding:
    Whether the responding AP is allowed to initiate its joint-BSS sounding, right after the initiating AP’s joint-BSS sounding.

## Slide 4: Proposal: Required Rounds Indication in Co-BF Sounding Response Frame
Following this, the responding AP is informed in advance—through the Co-BF Sounding Invite frame—of which Co-BF sounding rounds to be performed within the shared TXOP, enabling it to:
  Decide whether to accept or decline the Co-BF sounding invitation.
  If it accepts, the responding AP may also indicate in the Co-BF Sounding Response frame whether it is capable of performing its own Co-BF sequence, should the initiating AP permit it.

## Slide 5: Summary
In this contribution, we propose to allow the Initiating AP to include the sounding type and the specific Co-BF sounding rounds to be performed within the shared TXOP in the Co-BF Sounding Invite frame.
Following this, the responding AP is informed in advance—through the Co-BF Sounding Invite frame—of which Co-BF sounding rounds to be performed within the shared TXOP, enabling it to:
  decide whether to accept or decline the Co-BF sounding invitation.
  If it accepts, the responding AP may also indicate in the Co-BF Sounding Response frame whether it is capable of performing its own Co-BF sequence, should the initiating AP permit it.

## Slide 6: References
11-25/0681r11, “PDT-CRs-Joint-sounding-procedure”.

## Slide 7: Straw Poll 1
Do you agree to add to 11bn SFD that:
  the Initiating AP shall explicitly indicate to the Responding AP, in the Co-BF Sounding Invite frame, which UHR Co-BF sequential or joint NDP sounding sequence(s) are to be carried out during the TXOP?
  Y/N/A