## Slide 1: IMMW PHY Performance and Design Implications
Date: 2025-05-12
Authors:
Name | Affiliations | Address | Phone | E-mail
Thomas Handte | Sony Group Corporation |  |  | Thomas.Handte@sony.com
Kosuke Aio |  |  |  | Kosuke.Aio@sony.com
Yusuke Tanaka |  |  |  | Yusuke.YT.Tanaka@sony.com
Dana Ciochina |  |  |  | 
Daniel Verenzuela |  |  |  | 
Ryuichi Hirata |  |  |  | 
Qing Xia |  |  |  | 

## Slide 2: Introduction
TGbq aims [1,2] to …
  … combine mmWave and sub-7 GHz via MLO framework
  … reuse sub-7GHz OFDM waveform for application in mmWave
Studies have been done which compare parameters of upclocked 11ac waveform with EDMG OFDM waveform e.g. [3,4]
An earlier submission [5] compared OFDM with single carrier (SC) waveform and provided some design considerations
  The design considerations targeted unchanged PHY performance between IMMW OFDM and EDMG SC
This submission is a follow-up and provides …
  … additional insights in PHY performance of a radio reusing upclocked sub-7 GHz OFDM waveform
  … predicted PHY performance tables for sensitivity, bitrate, and exemplary link margin
  … suggested PHY design considerations in terms of bandwidth and MCS for TGbq PHY

## Slide 3: Sensitivity overview
PHY design of IMMW is yet under discussion
  Consideration of existing waveforms to predict sensitivity
Table lists sensitivity of BPSK with code rate R ½
  Note that sensitivity definition may be slightly different among PHY formats
Comparison of PHY formats reveals
  Sensitivity at a bandwidth of 320 MHz is almost same
  Spectral efficiency except VHT is almost same
  => Assume -73dBm and 0.85 in the following
PHY format | Bandwidth (BW) [MHz] | Sensitivity for BW [dBm] | Sensitivity for 320 MHz [dBm] | Spectral efficiency
EDMG SC | 1760 | -66 | -73 | 0.87
EDMG OFDM | 1760 | -66 | -73 | 0.83
EHT/UHR | 320 | -70 | -70 | 0.85
HE | 160 | -73 | -70 | 0.85
VHT | 160 | -73 | -70 | 0.73
-73
0.85

## Slide 4: Predicted sensitivity
Sensitivity [dBm] for several MCS and BWs can be predicted based on
  a reference value of -73dBm for BPSK R1/2 at 320 MHz
  relative MCS sensitivity spacing of EHT
  +/- 3dB for double/half bandwidth
Bandwidth [MHz] / MCS | 80 | 160 | 320 | 640 | 1280
BPSK R1/2 | -79 | -76 | -73 | -70 | -67
QPSK R1/2 | -76 | -73 | -70 | -67 | -64
QPSK R3/4 | -74 | -71 | -68 | -65 | -62
16Q R1/2 | -71 | -68 | -65 | -62 | -59
16Q R3/4 | -67 | -64 | -61 | -58 | -55
64Q R2/3 | -63 | -60 | -57 | -54 | -51
64Q R3/4 | -62 | -59 | -56 | -53 | -50
64Q R5/6 | -61 | -58 | -55 | -52 | -49
256Q R3/4 | -56 | -53 | -50 | -47 | -44

## Slide 5: RF frontend at 60 GHz is different
A mmWave RF frontend is challenging to implement
  Need for power splitters, switches, and phase shifting circuitries to implement analog beamforming
    Those components have non-zero loss
  RF power is scarce resource [6, 7]
    A CMOS power amplifier (PA) for 60 GHz has typ. 10 to 15 dBm peak transmit power
    PAs on other substrate may achieve higher peak transmit power
  Various PAs reside in an RF frontend
    It is difficult to do digital predistortion (DPD) for all [8]
Thus, consideration of PA characteristic is very important
  For our analysis, we use the PA model of EDMG evaluation methodology [9]
  PA backoff parameter is defined as
average transmit power
peak transmit power
of [7]

## Slide 6: Estimation of link margin and range
Link margin can be estimated under the following assumptions
  Carrier frequency 60 GHz
  Phased antenna array (PAA) gain at Tx and Rx each 8 dB
  Power amplifier (PA) maximum transmit power 10 dBm
  PA backoff
    OFDM: 8dB (same for all MCS)
    SC: 0.5 / 3 / 5dB (for BPSK, QPSK / 16QAM / 64QAM)
  AWGN channel
  Unlimited power spectral density for the considered bandwidths
Range can be estimated based on link margin
  Friis’ pathloss
      Good model for 60 GHz LOS propagation [10,11]

## Slide 7: Predicted link margin for IMMW waveform
Link margin [dB] at 1m distance
  OFDM suffers high BO for low constellation sizes
    320 MHz OFDM has same margin as 1760 MHz SC for BPSK/QPSK
    Gap between OFDM and SC closes for higher QAM
  64QAM may be applicable for very directive PAAs or high-power PA
  256QAM may be rarely used
  1280 MHz may be applicable for small constellations only
Predicted range can be found in Appendix
  10m => -20dB
Bandw. [MHz] / MCS | 80 | 160 | 320 | 640 | 1280
BPSK R1/2 | 29 | 26 | 23 | 20 | 17
QPSK R1/2 | 26 | 23 | 20 | 17 | 14
QPSK R3/4 | 24 | 21 | 18 | 15 | 12
16Q R1/2 | 21 | 18 | 15 | 12 | 9
16Q R3/4 | 17 | 14 | 11 | 8 | 5
64Q R2/3 | 13 | 10 | 7 | 4 | 1
64Q R3/4 | 12 | 9 | 6 | 3 | 0
64Q R5/6 | 11 | 8 | 5 | 2 | -1
256Q R3/4 | 6 | 3 | 0 | -3 | -6
1760 (EDMG SC)
23
20
18
13
9
-
2
-
-

## Slide 8: Predicted Rate
Rate [Mbps] for several MCS and BWs can be predicted
  Based on the spectral efficiency value of 0.85
Comparable PHY performance
  BPSK and QPSK at 320 MHz have same PHY performance as EDMG SC at 1760 MHz
    Rate is 18% compared to EDMG
  16Q and 64Q at 640 MHz have same PHY performance as EDMG SC at 1760 MHz
    Rate is 35% compared to EDMG
Bandw. [MHz] / MCS | 80 | 160 | 320 | 640 | 1280
BPSK R1/2 | 34 | 68 | 136 | 272 | 544
QPSK R1/2 | 68 | 136 | 272 | 544 | 1088
QPSK R3/4 | 102 | 204 | 408 | 816 | 1632
16Q R1/2 | 136 | 272 | 544 | 1088 | 2176
16Q R3/4 | 204 | 408 | 816 | 1632 | 3264
64Q R2/3 | 272 | 544 | 1088 | 2176 | 4352
64Q R3/4 | 306 | 612 | 1224 | 2448 | 4896
64Q R5/6 | 340 | 680 | 1360 | 2720 | 5440
256Q R3/4 | 408 | 816 | 1632 | 3264 | 6528
1760 (EDMG SC)
770
1540
2310
3080
4620
-
6930
-
-
≈18%
≈35%

## Slide 9: Conclusions
Constellation size
  Constellations ≤ 64-QAM are sufficient
Bandwidth
  ≤ 640 MHz is sufficient
  Use of 1280MHz questionable
    Reasonable link margin for small constellation sizes
  80 MHz may be needed for omni-reception (or even omni-transmission)
Achievable rates are generally smaller as in EDMG
  Rates for a bandwidth of 640 MHz are about 35% of single channel EDMG SC
    This brings rates quite close to those of EHT PHY which is beneficial for MLO
      MLO of sub-7 and 60 GHz combines links of comparable rates
  Rates for a bandwidth of 320 MHz are about 18% of single channel EDMG SC

## Slide 10: Straw Poll
Do you agree that TGbq PHY design should consider the following boundary conditions?
  Min. bandwidth greater or equal to 80 MHz
  Max. bandwidth lower or equal to 640 MHz
  Min. modulation constellation greater or equal to BPSK
  Max. modulation constellation lower or equal to 64QAM

## Slide 11: References
[1] 11-23/1819r1 “Integrated mmWave Design Considerations”
[2] 11-23/1905r0 “High Level Thoughts on IMMW”
[3] 11-22/1395r0 “ Thoughts on high frequency band”
[4] 11-22/1872r0 “Considerations on PHY designs for mmWave band”
[5] 11-24/0076r0 “Comparison of OFDM and EDMG SC Waveform”
[6] Power Amplifiers Performance Survey 2000-Present
[7] K. Kohama et al., IWPC Workshop, A GaN Technology to Meet Future Radio Requirements, October 2024
[8] Why Millimeter Wave Requires a Different Approach to DPD and How to Quantify Its Value | Analog Devices
[9] 11-15/0866r4 “11ay evaluation methodology”
[10] 11-09/0334r8 “Channel Models for 60 GHz WLAN Systems”
[11] 11-09/0553r1 “ Path Loss Model Development for TGad Channel Models”

## Slide 12: Appendix

## Slide 13: Predicted range for IMMW waveform
Range [m]
  OFDM suffers high BO for low constellation sizes
    320 MHz OFDM has same range as 1760 MHz SC for BPSK/QPSK
    Gap between OFDM and SC closes for higher QAM
  64QAM may be applicable for very directive PAAs or high-power PA
  256QAM may be rarely used
  1280 MHz may be applicable for small constellations only
Bandw. [MHz] / MCS | 80 | 160 | 320 | 640 | 1280
BPSK R1/2 | 28 | 20 | 14 | 10 | 7
QPSK R1/2 | 20 | 14 | 10 | 7 | 5
QPSK R3/4 | 16 | 11 | 8 | 6 | 4
16Q R1/2 | 11 | 8 | 6 | 4 | 3
16Q R3/4 | 7 | 5 | 4 | 3 | 2
64Q R2/3 | 4 | 3 | 2 | 2 | 1
64Q R3/4 | 4 | 3 | 2 | 1 | 1
64Q R5/6 | 4 | 3 | 2 | 1 | 1
256Q R3/4 | 2 | 1 | 1 | 1 | 0
1760 (EDMG SC)
14
10
8
4
3
-
1
-
-

## Slide 14: Link margin and Rate vs. Bandwidth and MCS
Graphical representation of predicted rate and predicted link margin
  Table of slide 8 and side 9 combined in one graphic
Color is rate [Mbps]
Number is link margin [dB] at 1m

## Slide 15: Recap of [5]
OFDM and SC waveform have different power amplifier (PA) backoff (BO) requirements
  SC has an advantage of 7.5dB over OFDM for BPSK and QPSK
  OFDM can compensate by lower bandwidth
    Factor of
Bit rate of OFDM is only 17.8% of the SC bit rate at same PHY performance
  Same PHY performance means same link margin or achievable range
The analysis has certain limitations
  E.g. impact of phase noise, unknown guard bands, guard interval, implementation specific parameters, etc.
7.5dB
0.178