## Slide 1: Further Considerations on DPS Operation for Sounding Procedure
Date: 2025-05-09
Authors:

## Slide 2: Trigger-Based Sounding Procedure with DPS STA
A DPS assisting AP (AP1) intends to send traffic to non-AP STAs (STA1, STA 2) and a DPS non-AP STA (STA3) using DL MU-MIMO. AP1 perform a TB sounding procedure with STA1~3.
Before sounding procedure begins, AP1 transmits an ICF to the STA3, so that the STA3 transitions from the LC mode to a HC mode.
While the STA1 operates in the HC mode, the AP1 then transmits an NDPA to initiate a TB sounding sequence (e.g., an EHT TB sounding sequence).
STA3 may transition to LC mode after detecting BFRP1 that is not addressed to STA3.
As such, AP1 needs to perform additional ICF2/ICR2 frame exchange with STA3 before BFRP2 to STA3. Overhead may be increased during the sounding procedure.

## Slide 3: DPS Operation for TB Sounding Procedure (Solution 1)
DPS non-AP STA (STA3) operates in LC mode when not solicited by AP1.
  The NDPA requests that STA3 transition to LC mode after receiving NDP.
  While STA3 operates in LC mode, AP1 transmits BFRP1 soliciting feedback (BFRs 1 & 2) from STA1 & 2.
Method :
  AP1 sends BFRP2 as an ICF. STA3 response BFR3 as an ICR.

## Slide 4: DPS Operation for TB Sounding Procedure (Solution 2)
AP1 solicits DPS non-AP STA (STA3) firstly before other non-AP STA after transmitting NDP.
  A SIFS after transmitting NDP, AP1 is configured to transmit BFRP1 soliciting feedback (BFR3) from STA3, while STA3 operates in HC mode.
  STA3 transitions to LC mode after transmitting BFR3 to AP1.

## Slide 5: Transmit Beamforming with DPS STA
A DPS assisting AP (AP1) intends to send traffic with a DPS non-AP STA (STA1) using transmit. AP1 performs a sounding procedure with STA1.
Before sounding procedure begins, AP1 and STA1 performs ICF/ICR frame exchange, so that the STA3 transitions from the LC mode to a HC mode. While the STA1 operates in the HC mode, the AP1 then transmits an NDPA to initiate a sounding sequence (e.g., an EHT TB sounding sequence).
After transmitting BFR to AP1, STA1 transitions to LC mode.
Option 1: AP1 needs to perform another ICF/ICR frame exchange with STA1 before transmitting a PPDU using TxBF to STA1.
  Problem: The 2nd ICF/ICR exchange creates an overhead.
Option 2: STA1 may remain in HC mode and consume power for waiting for AP1 transmitting the PPDU.
  Problem: Power inefficient on STA1 if AP1 transmits the PPDU in a different TXOP after the sounding procedure.

## Slide 6: DPS Operation for Transmit Beamforming (Solution)
NDPA indicates a period 1 for requesting STA1 to operate in a HC mode during the period 1, and a period 2 for recommending STA1 to operate in LC mode during the period 2.
  Period 2 occurs after STA1 sends a BFR to AP1 and before period 1.
After sending BFR to AP1, STA1 transitions from HC to LC mode at the beginning of the period 2.
At the beginning of the period 1, STA1 transitions to HC mode to receives PPDU.

## Slide 7: Straw Polls
SP1. Do you support defining a DPS operation that includes the following?
  When a DPS assisting AP performs TB sounding sequence including a DPS non-AP STA, the DPS assisting AP shall/may send to the DPS non-AP STA a BFRP trigger frame a SIFS after transmitting an NDP, while the DPS non-AP STA operates in a LC mode.
  Yes
  No
  Abstain

## Slide 8: Straw Polls
SP2. Do you support defining a DPS operation that includes the following?
  When a DPS assisting AP performs a sounding sequence including a DPS non-AP STA, the DPS assisting AP shall/may send an NDPA frame indicating a period for the DPS non-AP STA to operate in a high capability mode. The period may occur after the DPS non-AP STA sends a BFR frame.
  Yes
  No
  Abstain

## Slide 9: References
Draft P802.11bn D0.1
Draft P802.11be D7.0
24/0209r9: Specification Framework for TGbn, Ross Jian Yu (Huawei)
24/2016r3: PDT MAC Power Save, Liwen Chu (NXP)
24/1987r2: Detailed text proposal for dynamic power save and eMLSR, Liwen Chu (NXP)
23/1875r1: Power save proposal for non-AP/mobile-AP, Shubhodeep Adhikari (Broadcom)
23/1965r2: Dynamic power save follow-up, Alfred Asterjadhi (Qualcomm)
23/2003r1: Client power save, Laurent Cariou (Intel)