## Slide 1: COSR Misc
Date: 2025-05-12
Authors:
Name | Affiliations | Address | Phone | Email
You-Wei Chen | Mediatek | 2840 Junction Ave. San Jose, CA, 95134 |  | You-Wei.Chen@mediatek.com
Jianhan Liu |  |  |  | 
Kaiying Lu |  |  |  | 
Eric Pc |  |  |  | 
Thomas Pare |  |  |  | 

## Slide 2: Introduction
  In this presentation, we will discuss the power control and the frame exchange for COBF/COSR.

## Slide 3: Passed SP
SP1: Jason, CSR; Result: No objection.
  In Coordinated Spatial Reuse, the following information shall be carried in the Trigger frame that initiates concurrent CSR transmissions:
    The transmit power limit of the shared AP
      The shared AP Tx power limitation indicated by the sharing AP should not be lower than the minimum TX power indicated by the shared AP in its request.
    The transmit power of the sharing AP
From the passed SP:
  Shared AP need to info the sharing AP its minimum TX power.
  If shared AP is willing to lower its TX power when COSR, then we want to clarify the power control starting power from the PPDU.

## Slide 4: Power control starting point
There was some discussion before about the power control starting point.
  Option1: power control from the beginning
  Option2: power control from the UHR-SIG
We prefer option1, the power change in the middle is like a new mode of PHY, we prefer no further change at this moment.
Option1: power control from the beginning:
UHR-SIG
UHR-STF
UHR-LTF
PE
UHR-Data
L-preamble
U-SIG
Option2: power control from the UHR-SIG:
UHR-SIG
UHR-STF
UHR-LTF
PE
UHR-Data
L-preamble
U-SIG

## Slide 5: A common frame exchange for COBF/COSR
It is desirable to have a common framework for both COBF and COSR.
  To simply the standard design.
Prefer to exchange necessary info for performing COBF/COSR.
  To simply the carried info
Prefer to confirm and carry self-contained info for COBF/COSR PPDU transmission.
  To simply the implementation.
Sharing AP STA
AP1
Shared AP STA
AP2
COBF/COSR PPDU
  Exchange necessary Info for performing CoBF/CoSR PPDU transmission.
Invite
  Confirmed COBF/COSR transmission and provided the confirmed info (self-contain).
non-AP STA2
non-AP STA1
Response
Sync
COBF/COSR PPDU
  Detailed frame exchange will be determined in MAC

## Slide 6: Straw Poll #1
Do you agree to include the following into the 11bn SFD?
COBF/COSR use a common frame exchange design.
  There will be a COSR Invite/ Response/ Sync before the COSR data transmission.
  Note: ICF/ICR (between Response and Sync) if present will be discussed in MAC

## Slide 7: Straw Poll #2
Do you agree to include the following into the 11bn SFD?
In the COSR data transmission, the same power level is applied to the whole PPDU.