## Slide 1: On CoBF AP’s Carrier Synchronization Overhearing CSI Report in CoBF Sounding
Date: 2025-05-06
Authors:

## Slide 2: Introduction
In CoBF joint sounding sequence and cross-BSS sounding sequence of CoBF sequential sounding, a CoBF AP needs to overhear the cross-BSS or joint CSI report triggered by OBSS AP.
When transmitting CSI Report, the STAs pre-compensate CFO and synchronize carrier frequency of the TB CSI Report to their associated AP.
The overhearing AP needs to correct CFO when receives the CSI report to correctly decode the CSIs.

## Slide 3: Problem Statement
When the CoBF AP overhears BFRP from OBSS AP, it may inform its MAC to receive the CSI Report as a TB PPDU a SIFS time after BFRP.
  WIFI 6, WIFI 7 specs of TB PPDU allow the receiver (i.e., AP STA) to skip the processing of preambles, and use the information sent in TF to decode the TB PPDU correctly.
  But in CoBF AP overhearing OBSS/joint CSI case, the AP can’t skip CFO correction to receive the TB CSI report. It shall correct CFO when receives this TB PPDU to correctly decode CSI Report.

## Slide 4: Proposed Solution
It is recommended that a CoBF AP conducts regular preamble processing and CFO correction when it receives a cross-BSS/joint CSI feedback in a TB PPDU.

## Slide 5: CoBF AP Receives Cross-BSS CSI Report as A TB PPDU
Brown color filled blocks indicate carrier frequency synchronized to AP1 (sync-reference);
Non-color filled blocks indicate carrier frequency synchronized to AP2 (sync-follower).
STAs associated with AP1
STAs associated with AP2
AP2 (sync-follower)
NDPA
NDP
BFRP
AP1 (sync- reference)
CSI Report
SIFS
SIFS
SIFS
CSI Report
BFRP
CSI Report
Tx
Rx
Tx
Rx
NDPA
NDP
BFRP
…
…
…
…
Pre-correct CFO
BFRP
CSI Report
SIFS
SIFS
SIFS
NDPA
Est. CFO
Pre-correct CFO
Est. CFO
NDPA
Pre-correct CFO
Pre-correct CFO
Pre-correct CFO
BFRP
Est. CFO & Correct CFO
BFRP
Est. CFO & Correct CFO
CoBF Sequential Sounding Sequence
NDP
NDPA
NDPA
NDP
Tx
Rx
Tx
Rx

## Slide 6: SP1
Do you support to add the following text to 11bn draft?
Note: When a CoBF AP receives a cross-BSS or joint CSI feedback in a TB PPDU, the carrier frequency of the TB PPDU may not be synchronized with its own.