## Slide 1
P-EDCA Discussion
Date: 2025-06-07
Authors:

## Slide 2: Introduction
In 11bn SFD[1], 11bn defines Prioritized EDCA (P-EDCA) mechanism to reduce the access delay distribution tail for low latency AC_VO traffic.
In [2], the following conditions to start P-EDCA contention are described.
  P-EDCA is enabled by the AP in the BSS and the P-EDCA non-AP STA has notified the AP of its intent to use P-EDCA on the link.
  The P-EDCA STA has pending AC_VO buffered traffic
  QSRC[AC_VO] is equal or greater than dot11PEDCARetryThreshold and PSRC[AC_VO] is not greater than dot11PEDCAConsecutiveAttempt
In this contribution, we discuss some additional consideration points for enabling P-EDCA operation.

## Slide 3: P-EDCA enablement/disablement signaling
P-EDCA enablement
  STEP1: P-EDCA in the BSS is enabled by AP's broadcast management frame.
    When the AP indicates the P-EDCA enablement bit equal to TRUE in the Beacon frame, P-EDCA is enabled in the BSS.
  STEP2: P-EDCA per non-AP STA is enabled by exchanging individually addressed management frames.
    When P-EDCA is advertised as being enabled in the BSS, a non-AP STA may exchange individually addressed frames (e.g., OMP request and OMP response frames) with the AP to enable P-EDCA for the non-AP STA.
      The AP shall accept the P-EDCA enablement request from the non-AP STA by sending the OMP response frame in response to the OMP request frame.
      P-EDCA is enabled by the non-AP STA when receiving the OMP response frame or at the expiration of the transition timeout, which comes first.
      An OMP request frame to enable P-EDCA shall not be transmitted when P-EDCA is advertised as being disabled in the BSS.
Consideration
  The AP can track the the number of P-EDCA STA being enabled and be aware of the overall P-EDCA load.
  The AP can control/balance P-EDCA load with various options (see the next slides)

## Slide 4: AP controlled P-EDCA channel access load
To adjust/reduce the P-EDCA channel access load and its collision probability,
  #1: AP may announce P-EDCA disablement.
    It forces all P-EDCA STAs, that have been P-EDCA enabled, to disable P-EDCA operation in the BSS.
    It disallows a new P-EDCA enablement request from a STA that has not enabled P-EDCA yet.
    The AP is not allowed to reject a P-EDCA enablement request from a non-AP STA, which means the AP is not able to control/balance P-EDCA channel access load while it is enabled.
  #2: AP may advertise the updated P-EDCA parameters (e.g., DSAIFS, P-EDCA CWmin/max, P-EDCA AIFSN, etc.) to reduce collision probability of DS-CTS and subsequent RTS.
    It may be helpful to reduce P-EDCA collision probability among multiple P-EDCA STAs, but it is not a direct method to control the P-EDCA load.
We need to define an efficient mechanism for an AP to control the P-EDCA channel access load while P-EDCA is enabled in the BSS.

## Slide 5: Proposal: Indication of allowing a new P-EDCA request
The AP may advertise an indication in a broadcast management frame (e.g., Beacon), in addition to the indication of P-EDCA enablement/disablement.
  The indication field indicates whether or not the AP allows a new P-EDCA request from a non-AP STA in the BSS.
    0: A new P-EDCA request from a non-AP STA is disallowed.
    1: A new P-EDCA request from a non-AP STA is allowed.
  The indication field is valid only if the P-EDCA is indicated as being enabled in the BSS. Otherwise, the field is reserved.
  The indication field can be merged with the P-EDCA enabling indication field.
    00: P-EDCA disabled.
    01: P-EDCA enabled and a new P-EDCA request is allowed.
    10: P-EDCA enabled and a new P-EDCA request is disallowed.
    11: reserved.
A non-AP STA may transmit an individually addressed management frame to its associated AP that requests P-EDCA enablement if P-EDCA is announced as being enabled in the BSS and as being allowed for a new P-EDCA enablement request.
Otherwise, the non-AP STA shall not transmit a management frame requesting a new P-EDCA enablement.

## Slide 6: Summary
For balanced P-EDCA channel access load in the BSS,
  P-EDCA can be enabled per non-AP STA's request.
  AP shall be able to advertise whether a new P-EDCA enablement request from a non-AP STA is allowed.

## Slide 7: Straw Poll 1
Do you agree to add the following text in the TGbn SFD?
  AP shall be able to advertise whether a new P-EDCA enablement request from a non-AP STA is allowed.

## Slide 8: References
[1] 11-24/209r15 Specification Framework for TGbn
[2] Draft P802.11bn_D0.3