## Slide 1
P-EDCA Discussion
Date: 2025-09-08
Authors:

## Slide 2: Introduction
In [1], the following conditions to start P-EDCA contention are described.
  P-EDCA is enabled by the AP in the BSS and the P-EDCA non-AP STA has notified the AP of its intent to use P-EDCA on the link.
  The P-EDCA STA has pending AC_VO buffered traffic.
  QSRC[AC_VO] is equal or greater than dot11PEDCARetryThreshold and PSRC[AC_VO] is less than dot11PEDCAConsecutiveAttempt.
In this contribution, we discuss some additional consideration points for P-EDCA operation.

## Slide 3: P-EDCA enablement/disablement signaling
P-EDCA enablement
  STEP1: P-EDCA enablement in the BSS is announced by an AP.
    The P-EDCA Enabled field equal to one in the UHR Operation element of the Beacon frame indicates P-EDCA being enabled in the BSS.
  STEP2: P-EDCA is enabled at a non-AP STA by sending an OMP Request frame.
    When P-EDCA is announced as being enabled in the BSS, a non-AP STA may exchange individually addressed frames (e.g., OMP Request and OMP Response frames) with the AP to enable P-EDCA for the non-AP STA.
      The AP shall accept the P-EDCA enablement request from the non-AP STA by sending the OMP response.
      P-EDCA is enabled at the non-AP STA upon receiving of the OMP response or at the expiration of the transition timeout, which comes first.
      The OMP Request frame to enable P-EDCA shall not be transmitted when P-EDCA is advertised as being disabled in the BSS.
Consideration
  The AP can track the the number of P-EDCA STA being enabled and be aware of the overall P-EDCA load.
  The AP can control/balance P-EDCA load with various options (see the next slides)

## Slide 4: Controlled P-EDCA access load
To adjust/reduce the P-EDCA channel access load and its collision probability,
  #1: AP may announce P-EDCA disablement.
    It forces all P-EDCA STAs, that have been P-EDCA enabled, to disable P-EDCA operation in the BSS.
    Note: The AP is not allowed to reject a P-EDCA enablement request from a non-AP STA, which means the AP is not able to control/balance P-EDCA channel access load while it is enabled.
  #2: AP may update the P-EDCA operation parameters to reduce collision probability during P-EDCA contention.
    It could be helpful to control the P-EDCA load indirectly, but it affects P-EDCA performance to the P-EDCA STAs that have already enabled P-EDCA in the BSS.
We need to define an efficient mechanism for an AP to control the P-EDCA channel access load while P-EDCA is enabled in the BSS.

## Slide 5: Proposal 1: Announcement of whether new P-EDCA enablement request is allowed
The AP may advertise an indication in a broadcast management frame (e.g., Beacon), in addition to the indication of P-EDCA enablement/disablement.
  The indication field indicates whether or not the AP allows a new P-EDCA request from a non-AP STA in the BSS.
    0: A new P-EDCA request from a non-AP STA is disallowed.
    1: A new P-EDCA request from a non-AP STA is allowed.
  The indication field is valid only if the P-EDCA is indicated as being enabled in the BSS. Otherwise, the field is reserved.
  The indication field can be merged with the P-EDCA enabling indication field.
    00: P-EDCA disabled.
    01: P-EDCA enabled and a new P-EDCA request is allowed.
    10: P-EDCA enabled and a new P-EDCA request is disallowed.
    11: reserved.
A non-AP STA that supports P-EDCA may transmit an OMP Request frame to the AP to enable P-EDCA when the non-AP STA receives a management frame, from the AP, indicating as P-EDCA being enabled and being allowed for new P-EDCA enablement request in the BSS.
Otherwise, the non-AP STA shall not transmit a OMP Request frame to enable P-EDCA.

## Slide 6: P-EDCA to a DPS mobile AP
Background
  Mobile AP may enable DPS mode by setting the DPS enabled field to 1 and it may enable P-EDCA in the BSS by setting the P-EDCA enabled field to 1.
  If a DPS mobile AP indicates the non-zero DPS padding delay, a non-AP STA shall use a BSRP NTB Trigger as the ICF. Otherwise, it shall use either an RTS or a BSRP NTB Trigger as the ICF.
  P-EDCA shall use the following frame sequences: DS-CTS + RTS/CTS + VO Data + ACK/BA.
Problem statement
  The current P-EDCA procedure is not compatible with the DPS mobile AP that requires an ICF with a non-zero DPS padding delay.

## Slide 7: Proposal 2: P-EDCA to a DPS mobile AP
Proposal
  Based on the DPS padding delay, a mobile AP shall be able to enable both P-EDCA and DPS mode, or either one.
    If a mobile AP requires the zero DPS padding delay, the mobile AP can enable both DPS mode and P-EDCA at the same time.
      An RTS shall be used as a DPS ICF by a DPS Assisting STA that enables P-EDCA. A BSRP NTB Trigger shall not be used as a DPS ICF by a DPS Assisting STA that enables P-EDCA.
    If a mobile AP requires a non-zero DPS padding delay, the mobile AP can enable either DPS mode or P-EDCA mode only. It shall not enable both modes at the same time.
      A mobile AP that enables DPS mode with non-zero DPS padding delay shall not support P-EDCA or shall disable P-EDCA if it supports.

## Slide 8: Summary
For balanced P-EDCA channel access load in the BSS,
  AP shall be able to advertise whether a new P-EDCA enablement request from a non-AP STA is allowed or not.
For P-EDCA to a DPS mobile AP,
  Based on the DPS padding delay, a mobile AP shall be able to enable both P-EDCA and DPS mode, or either one.

## Slide 9: Straw Poll 1
Do you agree that an AP shall be able to advertise whether a new P-EDCA enablement request from a non-AP STA is allowed or not?

## Slide 10: Straw Poll 2
Do you agree to the following text?
  A mobile AP that supports both P-EDCA and DPS mode may enable both modes or only one mode of them, based on the DPS padding delay.
  If the mobile AP requires zero DPS padding delay, the mobile AP may enable both DPS mode and P-EDCA at the same time.
    An RTS frame shall be used as a DPS ICF by a DPS Assisting STA that enables P-EDCA. A BSRP NTB Trigger frame shall not be used as a DPS ICF by a DPS Assisting STA that enables P-EDCA.
  If the mobile AP requires non-zero DPS padding delay, the mobile AP may enable either DPS mode or P-EDCA mode only. It shall not enable both modes at the same time.

## Slide 11: Reference
[1] Draft P802.11bn_D1.0