## Slide 1
UHR BSS Parameter Update
Date: 2025-06-07
Authors:

## Slide 2: Introduction
In [1] [2], Beacon bloating issue were discussed, and the followings were suggested for UHR BSS parameter update.
  The elements related to UHR features (e.g., UHR Capabilities IE, UHR Operation IE, etc.) are not carried in Beacons transmitted by a UHR AP.
  The Beacon carries an indication that the AP supports UHR
  A UHR non-AP STA can obtain the complete set of UHR parameters via Probe Response or Association Response during association procedure.
  To efficiently update UHR BSS parameters, separate UHR CUF and UHR BPCC can be defined.
In this contribution, we discuss a mechanism about how to update the UHR feature related parameters.

## Slide 3: Recap) UHR CUF and UHR BPCC
In [1] [2], the UHR CUF and the UHR BPCC were introduced.
When a UHR AP has critical update for UHR BSS parameters, the AP announces such critical update in the Beacon frame using the UHR CUF and the UHR BPCC.
In case of the critical update, Beacons can carry the updated UHR IEs for several beacon intervals (e.g., multiple TBTTs or multiple DTIM intervals)
  The updated UHR IEs can be carried in Beacon frames for multiple DTIM intervals, to make sure associated STAs that may be in power save also obtain the updated IEs.
  The UHR Critical Update Flag (UHR CUF) and the UHR BSS Parameters Change Count (UHR BPCC) can be used to indicate that there is any update on the UHR BSS parameters and the Beacon carrying the updated IEs.
  If there is any change on the UHR CUF and the UHR BPCC, a UHR STA can acquire the critical update of the UHR BSS parameters through exchanging the Probe Request/Response, AP’s unsolicited broadcast Probe Response, or the Beacon frame temporarily carrying the updated UHR BSS parameters.

## Slide 4: Announced UHR feature parameters
Background
  Some UHR features can be enabled/disabled through the feature enablement/disablement signaling by AP.
    E.g., Enablement/disablement of NPCA, DSO, P-EDCA, DBE, etc.
    UHR Operation element can include each feature enablement/disablement indication.
  Some UHR feature specific parameters can be updated through AP’s announcement.
    E.g., NPCA primary channel, DBE BW, P-EDCA parameters, DPS operation parameters.
    UHR operation element can include these parameter changes.
  AP’s announcement for specific UHR feature parameter changes shall be considered as UHR critical update to the non-AP STA that supports the indicated feature.
Problem
  If UHR feature parameter change is indicated as a critical update (w/ the UHR CUF and the UHR BPCC), a UHR STA not supporting the UHR feature also shall perform unnecessary UHR BSS parameter update by transmitting a request management frame to retrieve the updated parameter when detecting the mismatched UHR BPCC.
    It increases STA’s power consumption and the signaling overhead.

## Slide 5: Example of unnecessary UHR BSS parameter update
UHR AP
UHR STA
(Deep Sleep w/ only P-EDCA support)
DTIM Beacon
Beacon
UHR CUF = 1
UHR BPCC = 3
UHR CUF = 0
UHR BPCC = 2
UHR CUF = 1
UHR BPCC = 3
UHR CUF = 1
UHR BPCC = 3
UHR CUF = 1
UHR BPCC = 3
UHR CUF = 0
UHR BPCC = 3
UHR CUF = 0
UHR BPCC = 3
UHR CUF = 0
UHR BPCC = 3
Doze
Awake
Probe Req
Probe Rsp (w/ updated NPCA params)
w/ updated NPCA params
Unnecessary probing execution
Detecting mismatched BPCC (BPCC2 vs. BPCC3)
w/ UHR BPCC2
UHR CUF = 0
UHR BPCC = 3
…
w/ updated NPCA params
w/ updated NPCA params
w/ updated NPCA params

## Slide 6: Proposal: UHR feature specific change count
To help a UHR STA updating its necessary UHR BSS parameters,
Propose the Change Count for each UHR feature (e.g., NPCA CC, P-EDCA CC, DBE CC, etc.)
  If there is any change for a specific UHR feature parameter as critical update,
    the UHR feature specific change count is incremented by 1.
    the updated UHR feature parameter can be included in the Beacon frame for several TBTTs, or
    the updated UHR feature parameter can be advertised in a broadcast Probe Response frame or in a group addressed management frame (e.g., NPCA announcement frame, DBE announcement frame, etc.), or
    the updated UHR feature parameter can be transmitted in an individually addressed response management frame (e.g., Probe Response frame, TBD Response frame, etc.) in response to a request management frame (e.g., Probe Request, TBD Request, etc.).
  The UHR feature specific change count can be included in Beacon frames or a broadcast Probe Response frame.
  The UHR CUF field and the UHR BPCC field indicates any change for a UHR feature related parameter and the change count for each UHR feature indicates any update/change of each UHR feature.
  If the UHR feature change count values between the AP and a non-AP STA are different, the non-AP STA that supports the feature shall do the UHR BSS parameter update procedure by transmitting a request management frame (e.g., Probe Request) to retrieve the updated feature parameter from the AP.

## Slide 7: Example of UHR feature parameter update
UHR AP
UHR STA1
(Deep Sleep w/ only NPCA support)
DTIM Beacon
Beacon
UCF = 0
UBC = 5
NCC = 2
PCC = 3
Doze
Awake
Probe Req
Probe Rsp (w/ updated NPCA params)
w/ updated NPCA params
…
UHR STA2
(Deep Sleep w/ only P-EDCA support)
Doze
Awake
w/ UBC=5,
PCC=3
Detecting mismatched UHR BPCC, but matched P-EDCA CC
UHR CUF: UCF
UHR BPCC: UBC
NPCA CC: NCC
P-EDCA CC: PCC
UCF = 1
UBC = 6
NCC = 3
PCC = 3
UCF = 1
UBC = 6
NCC = 3
PCC = 3
UCF = 1
UBC = 6
NCC = 3
PCC = 3
UCF =1
UBC = 6
NCC = 3
PCC = 3
UCF = 0
UBC = 6
NCC = 3
PCC = 3
UCF = 0
UBC = 6
NCC = 3
PCC = 3
UCF = 0
UBC = 6
NCC = 3
PCC = 3
UCF = 0
UBC = 6
NCC = 3
PCC = 3
w/ UBC=5,
NCC=2
Detecting mismatched UHR BPCC and UHR NPCA CC
No Probe Req Tx
w/ updated NPCA params
w/ updated NPCA params
w/ updated NPCA params

## Slide 8: Summary
The elements related to UHR features (e.g., UHR Capabilities IE, UHR Operation IE, etc.) may not be carried in Beacons transmitted by a UHR AP.
To efficiently update UHR BSS parameters, separate UHR CUF and UHR BPCC can be defined.
If UHR feature parameter change is indicated as a critical update with UHR CUF and UHR BPCC, a UHR STA not supporting the UHR feature should perform the UHR BSS parameter update procedure unnecessarily.
To help a UHR STA update necessary UHR BSS parameters, we propose to add the Change Count for each UHR feature in broadcast management frames.

## Slide 9: Straw Poll
Do you agree to add the following text in the TGbn SFD?
  11bn shall define a mechanism for a UHR STA to update the UHR feature specific parameter by checking the UHR feature specific change count carried in Beacon frames.

## Slide 10: References
[1] 11-24/1880r1 Solutions for Beacon Bloating
[2] 11-24/1888r0 light beacon consideration