## Slide 1: NPCA Operation for Co-TDMA Procedure
Date: 2025-05-09
Authors:

## Slide 2: Introduction
NPCA has been described and discussed [1-3].
NPCA switch conditions during Co-TDMA are further discussed in [4].
In this contribution, we propose methods to improve the NPCA operation further for Co-TDMA procedure.

## Slide 3: Recap: Non-primary channel access (NPCA)
  In TGbn SFD (24/0209r9), Subclause 3.4
    TGbn defines a mode of operation that enables a STA to access the secondary channel while the primary channel is known to be busy due to OBSS traffic or other TBD conditions.
      The mode of operation shall not assume that the STA is capable to detect or decode a frame and obtain NAV information of the secondary channel concurrently with the primary channel.
      A BSS shall only have a single NPCA primary channel (name TBD) on which the STA contends while the primary channel of the BSS is known to be busy due to OBSS traffic or other TBD conditions.
    [Motion #11, [1] and [21-30]]

## Slide 4: NPCA AP/STA Operation during Co-TDMA
A Co-TDMA sharing AP (AP1) that is a TXOP owner may transmit a MU-RTS TXS Trigger (MRTT) frame, via primary channel (PCH), sharing a time portion of the TXOP.
AP2 responds a CTS, via PCH, to the MRTT followed by a data frame sent via the PCH to STA2 during the time portion.
AP1 detects the data frame from AP2 (i.e. OBSS transmission) and sets a basic NAV. So that AP1 switches from the PCH to a NPCA PCH.
As the TXOP owner and the sharing AP of Co-TDMA, AP1 doesn’t intend for transmission during the Allocation Duration.
However, STA1 doesn’t know the MRTT frame initiates the Co-TDMA. Even AP1 remains in the NPCA PCH, its associated STA1 may still switch from the PCH to the NPCA PCH.

## Slide 5: NPCA Operation for Co-TDMA - Solution 1
The Co-TDMA Sharing AP (AP1) doesn’t switch to NPCA PCH during a time portion of a TXOP shared to AP2 by a MRTT (via PCH).
AP1 informs STA1 not to switch to NPCA PCH) during the time portion.
  Method 1: sending MRTT frame indicating that STA1 to decode the time portion in the Allocation Duration field of a User Info field for AP2.
  Method 2: sending MRTT frame indicating the time portion in the common info field, a special user info field, or in a user info field for STA1.

## Slide 6: NPCA Operation for Co-TDMA - Solution 2
AP1 informs STA1 not to switch to NPCA PCH during the time portion.
After Co-TDMA polling phase and before the TXOP allocation phase, AP1 sends to STA1 a frame (broadcast no ack frame or a QoS Null frame) indicating:
  Method 1: the time portion as indicated in allocation duration field in the MRTT frame to be sent to AP2.
  Method 2: STA1 to decode an allocation duration field of the MRTT frame to be sent to AP2.
The Co-TDMA Sharing AP (AP1) doesn't switch to NPCA PCH during a time portion of a TXOP shared to AP2 by a MRTT (via PCH).

## Slide 7: Summary
In this contribution, we shared some thoughts of conditions of NPCA operation.
  A Co-TDMA sharing AP that is an NPCA AP disables/deactivates NPCA mode of operation during a time portion of its TXOP allocated to another AP (Co-TDMA coordinated AP).

## Slide 8: Straw Poll
SP1. Do you support defining an NPCA operation that includes the following?
  An NPCA AP that is a Co-TDMA sharing AP shall not switch to the NPCA primary channel for NPCA operation during a time portion of a TXOP within a Co-TDMA procedure.
  Yes
  No
  Abstain

## Slide 9: Straw Poll
SP2. Do you support defining an NPCA operation that includes the following?
  An NPCA AP that is a Co-TDMA sharing AP shall/may send to a non-AP NPCA STA that is associated with the NPCA AP a frame indicating, during a time portion of a TXOP obtained by the NPCA AP and to be shared to another AP:
    the non-AP NPCA STA not to switch to the NPCA primary channel, and
    the time portion for the non-AP NPCA STA not switching to the NPCA primary channel.
  The format of the frame is TBD.
  Yes
  No
  Abstain

## Slide 10: References
Draft P802.11bn D0.2
11-24/1762, PDT-MAC-NPCA
11-24/0209: Specification Framework for TGbn, Ross Jian Yu (Huawei)
11-24/2061r2, Usage of NPCA in M-AP Coordination, Si-Chan Noh, (Newracom)