## Slide 1: TXOP protection for ELR Transmissions
Date: 2025-05-12
Authors:

## Slide 2: Abstract
The UHR receive procedure allows an ELR capable STA to process an ELR PPDU even without a valid U-SIG [1]
  If the U-SIG field indicates an invalid CRC: the PHY shall issue the error condition PHY RXEND.indication(FormatViolation) primitive … if the PHY entity is not ELR capable. Otherwise, the PHY entity should continue searching for the ELR-MARK.
When this happens, an ELR capable STA does not know the TXOP duration of the received ELR PPDU.
  TXOP field is not present in the ELR-SIG
In this contribution, we propose that an ELR capable STA defer using EIFS when it doesn’t obtain the TXOP duration in an ELR PPDU.

## Slide 3: TXOP_DURATION
The TXVECTOR parameter TXOP_DURATION of an HE/EHT/UHR PPDU indicates duration information for NAV setting and protection of the TXOP.
The TXOP_DURATION is signaled in the HE-SIG-A and U-SIG. It helps protect ACK or BlockAck of HE/EHT/UHR PPDUs.
A STA may set the TXOP_DURATION to UNSPECIFIED to indicate no duration information.

## Slide 4: EIFS
EIFS is used after a STA detects a frame with errors (e.g., due to a failed CRC check). The idea is to give the intended recipient of that frame enough time to transmit an Ack or BlockAck.
TX STA
RX STA
Third STA
DATA
Ack
Error
EIFS
DIFS
Random BO
DATA

## Slide 5: EIFS for HE/EHT/UHR PPDU
For HE/EHT/UHR PPDUs, EIFS is not used as long as the TXOP_DURATION is not UNSPECIFIED.
10.3.2.3.7 EIFS… EIFS shall not be invoked if the RXVECTOR parameter TXOP_DURATION of a received HE PPDU is not set to UNSPECIFIED.
TX STA
RX STA
Third STA
DATA
Ack
Error
DIFS
Random BO
DATA
TXOP_DURATION
TXOP_DURATION

## Slide 6: Problem
For an ELR PPDU, the EIFS exception rule has a problem. The baseline spec assumes that an HE/EHT/UHR PPDU has a TXOP_DURATION. For ELR PPDU, an ELR capable STA may not detect a U-SIG and hence may not obtain the TXOP_DURATION. It is unclear whether an ELR STA will use EIFS or not (since TXOP_DURATION exists but not decoded correctly).
TX STA
RX STA
Third STA
DATA
Ack
U-SIG
error
DIFS/BO
DATA
TXOP_DURATION
Error

## Slide 7: Solutions
Solution 1: To bypass EIFS, require an ELR capable STA to decode the U-SIG (i.e. including TXOP field). This protects the acknowledgement but not longer frame exchanges. (Recommended)
Solution 2: Signal TXOP in the ELR-SIG
TX STA
RX STA
Third STA
DATA
Ack
EIFS/BO
DATA
TXOP_DURATION
U-SIG error

## Slide 8: Proposed baseline spec text change for Solution 1
EIFS shall not be invoked for an A-MPDU if one or more of its frames are received correctly. EIFS shall not be invoked if the RXVECTOR parameter TXOP_DURATION of a received HE/EHT/UHR PPDU is obtained and not set to UNSPECIFIED.

## Slide 9: SP 1
Do you support adding in the TGbn SFD:
An ELR capable STA shall invoke the EIFS for ELR PPDUs when the U-SIG is not decoded with a valid CRC.

## Slide 10: References
[1] https://mentor.ieee.org/802.11/dcn/25/11-25-0696-02-00bn-uhr-rx-procedure.docx